## Slide 1: TRILL Base Protocol Clarifications and Corrections
Donald E. Eastlake, 3rd (Huawei)
Mingui Zhang (Huawei)
Anoop Ghanwani (Dell)
Ayan Banerjee (Cisco)
Vishwas Manral (HP)
d3e3e3@gmail.com
zhangmingui@huawei.com
anoop@alumni.duke.edu
ayabaner@cisco.com
vishwas.manral@hp.com

## Slide 2: TRILL Clarifications and Corrections
draft-eastlake-trill-rbridge-clear-correct-01
Covers an accumulation of clarifications that have come up since the TRILL protocol was approved as a standard in March 2010.
Mostly updates RFC 6325 but also includes one clarification of RFC 6327.
Corrects three Errata against RFC 6325.

## Slide 3: TRILL Clarifications and Corrections
draft-eastlake-trill-rbridge-clear-correct-01
Topics in current draft:
  Overloaded / Unreachable RBridges
  Distribution Tree Updates
  Nickname Selection
  MTU
  The CFI / DEI bit
  When LSP synchronization starts

## Slide 4: Overloaded / Unreachable RBridges
When an RBridge campus partitions, an RBridge determines tree roots and calculates distribution trees only within its partition, regardless of LSPs hanging around from Rbridges now unreachable by LSP flooding.
Discusses receipt and origination of known unicast and multi-destination frames.
  Adds an optional feature for Overloaded Rbridge Origination of Multi-destination Frames (OOMF).

## Slide 5: Overloaded RBridges OOMF
Overloaded RBridges cannot be trusted to either correctly calculate distribution trees or perform the reserve path forwarding check (RPFC).
Overloaded Origination of Multi-destination Frames (OOMF) feature:
  If Rbridge RB1 is in overload but immediate neighbor RB2 is not and
  RB2 can use a distribution tree on which RB1 is a leaf node from RB2 and
  RB2 volunteers to offer this service, then
  RB1 can send the frame to RB2 with a special egress nickname requesting this service.

## Slide 6: Overloaded RBridges OOMF
R1
R2
R3
R3
R4

## Slide 7: Distribution Tree Updates
Recommends that, if nickname N1 ceases to be a tree root and there is enough room in local tables, forwarding and RPFC entries for N1 be retained in case there are frames in flight on that tree.

## Slide 8: Nickname Selection
Fixes Errata in Section 3.7.3 of RFC 6325 related to psuedonodes concerning priorities to hold nicknames.
Discusses effects of partition on nickname selection.
Explains effects in the very unlikely case of nickname exhaustion.

## Slide 9: MTU
This section of the draft is intended to provide an exact explanation of what various MTU numbers mean on links of various technologies.

## Slide 10: The CFI / DEI Bit
Update to RFC 6325 to accommodate the IEEE change of the CFI (Canonical Format Indicator) bit in C-VLAN tags to be a DEI (Drop Eligibility Indicator) bit in 802.1Q-2011.

## Slide 11: When LSP Synchronization Starts
Clarify RFC 6327 by adding a specification of when an RBridge starts to send LSPs on a link. It is when its state with regard to at least one neighbor out at port is in the Two-Way or Report state.

## Slide 12: END
Donald E. Eastlake, 3rd (Huawei)
Mingui Zhang (Huawei)
Anoop Ghanwani (Dell)
Ayan Banerjee (Cisco)
Vishwas Manral (HP)
d3e3e3@gmail.com
zhangmingui@huawei.com
anoop@alumni.duke.edu
ayabaner@cisco.com
vishwas.manral@hp.com