## Slide 1: TRILL issue: Using Pseudonode Nicknames for Ingress RBridge
Radia Perlman
radiaperlman@gmail.com
Hongjun Zhai
Fangwei Hu
<number>
November 2011
Notes: <number>
2011 November

## Slide 2: Issue
If the Appointed forwarder on a link changes from R1 to R2, remote RBridge endnode caches will be incorrect
<number>
November 2011

## Slide 3: Endnode cache wrong if AF changes
shared link
R1
R2
R3
R8
rest of campus
17
136
38
S1
Endnode cache
S1/17
S2/38
S3/17
S2
S3
<number>
November 2011

## Slide 4: Solution: Use pseudonode nickname for ingress
shared link
R1
R2
R3
R8
rest of campus
17
136
38
92
Endnode cache
S1/92
S2/92
S3/92
S1
S2
S3
<number>
November 2011

## Slide 5: Some subtleties
Interaction with access links (links that are supposed to only be leaves…no inter-RB traffic…no inter-RB links advertised)
  Can be done by not using a pseudonode (and having all RBs on the link claim they are using nickname “92”)
  Or a pseudonode with nickname 92, and “overload” bit set, so paths through 92 not formed
<number>
November 2011

## Slide 6: Access link: need to forward rcv’d pkt addressed to “92” to AF
shared link
R1
R2
R3
R8
rest of campus
17
136
38
92
Endnode cache
S1/92
S2/92
S3/92
S1
S2
S3
If R8 sends to “92”,
pkt might reach non-AF
Only AF can decapsulate!
<number>
November 2011

## Slide 7: Special case: might have “link aggregation port group”
There’s a feature where a bridge B has two “up-links” to the RBs, only forwarding on one up-link (chosen at random), and never forwarding between the up-links
But there wouldn’t be any AF’s in that case, and the RBs wouldn’t see each other’s Hellos
<number>
November 2011

## Slide 8: But in general case, need to forward on last hop to AF
<number>
November 2011

## Slide 9: Or not use pseudonode nickname on access links
shared link
R1
R2
R3
R8
rest of campus
17
136
38
S1
Endnode cache
S1/17
S2/38
S3/17
S2
S3
<number>
November 2011

## Slide 10: Another subtlety: Reusing nickname when DRB changes
<number>
November 2011

## Slide 11: Reuse nickname if DRB changes
DRB needs to tell other RBs what the pseudonode nickname is (in Hellos)
If new DRB comes up, perhaps old RBs that remember the pseudonode nickname should tell the new DRB (in Hellos) what the pseudonode nickname was
<number>
November 2011

## Slide 12: But what if the link partitions into two links?
Can the new DRB even tell the difference between a link partitioning and the DRB dying?
<number>
November 2011

## Slide 13: Issue: LAN partition vs DRB dies
shared link
R1
R2
R3
R8
rest of campus
17
136
38
92
S1
S2
S3
Endnode cache
S1/92
S2/92
S3/92
<number>
November 2011

## Slide 14: Issue: DRB dies: Reuse “92”
shared link
R1
R2
R3
R8
rest of campus
17
136
38
92
S1
S2
S3
Endnode cache
S1/92
S2/92
S3/92
<number>
November 2011

## Slide 15: Issue: LAN partition: Can R3 reuse “92”? Both R1 and R3 will want 92
shared link
R1
R2
R3
R8
rest of campus
17
136
38
92
S1
S2
S3
Endnode cache
S1/92
S2/92
S3/92
<number>
November 2011

## Slide 16: Recommendation
Be optimistic and reuse the nickname
If it’s really a partition, LSPs will resolve it
Whoever has higher priority gets to keep it
No reason why it’s better for old DRB to keep it rather than new one
  in either case, some endnodes will have incorrect entries in distant RBridges
<number>
November 2011

## Slide 17: Another issue
If nickname changes, alerting distant RBs that their endnode cache is now wrong
  Either tell them to delete entries associated with nickname “92”, or tell them “entries that were 92 should now be 51”
<number>
November 2011

## Slide 18: Subtle issue: RPF check
<number>
November 2011

## Slide 19: Multidestination frames, pseudonode nickname, and the RPF check
shared link L
R1
R2
R3
R8
17
136
38
92
Assume R3 is AF
Chooses tree T4:
S1
S2
S3
<number>
November 2011

## Slide 20: If “92” really was ingress, R8 will rcv packet via R1
shared link L
R1
R2
R3
R8
17
136
38
92
Assume R3 is AF
Chooses tree T4:
S1
S2
S3
<number>
November 2011

## Slide 21: How to simulate “92” ingressing the frame
The AF has to be the one to encapsulate the frame
And send it back onto the link
But that’s not the same as “receiving the packet on the tree”
So assume R3 is AF, and look at previous slide…
R3 should encapsulate the frame, send it onto the link, but not forward it further until it receives the frame on a port in the tree
<number>
November 2011

## Slide 22: If “92” really was ingress, R8 will rcv packet via R1
shared link L
R1
R2
R3
R8
17
136
38
92
Assume R3 is AF
Chooses tree T4:
R6
S1
S2
S3
<number>
November 2011

## Slide 23: In that case, RPF check just works
If those rules followed
  AF encapsulates, and forwards back onto link
  And only forwards encapsulated pkt on tree if pkt received on port in the tree
No matter who is AF, packet looks like it comes from the pseudonode
And will be received via only one path
<number>
November 2011

## Slide 24: So the RPF check will always be OK
shared link
R1
R2
R3
R8
17
136
38
92
R8 will always receive packets
from pseudonode 92, tree T4,
via R1
RPF: 92
S1
S2
S3
<number>
November 2011

## Slide 25: Note double multidestination traffic on L
Twice as much multicast traffic on L
  native, and encapsulated
  in both directions (first hop and last hop)
This is a problem even without pseudonode nickname
And can’t be avoided
<number>
November 2011

## Slide 26: Access links
shared link
R1
R2
R3
R8
17
136
38
92
RPF: 92
without pseudonode nickname,
no problem: ingress=AF’s nickname
with: if R3 is AF, and that link
is not in the tree, R3 must
encapsulate and transmit
onto L
even though spec says not
to ever send encapsulated
traffic on an access link
S1
S2
S3
<number>
November 2011

## Slide 27: Potential solution
R3 should not volunteer to be an AF on L if R3’s port to L is not in any tree
Else (R3’s port to L is in at least one tree) R3 should only ingress on behalf of L for trees that R3’s port to L is on
<number>
November 2011