## Slide 1: Reactions to Signaling from ECN Support for RTP/RTCP
draft-carlberg-tsvwg-ecn-reactions-00.txt
14 November 2011
Piers O’Hanlon
Ken Carlberg

## Slide 2: Background
RFC 3168: Addition of ECN to IP
  Two layer design: IP ECN field, Transport negotiation & feedback
  Specifies support for TCP
  Obsoletes rfc-2481, and updates rfc-2474
draft-ietf-avtcore-ecn-for-rtp-05
  Specifies signaling to support ECN for RTP/UDP flows
    Specification for SDP signaling extensions
    Define RTP/AVPF ECN feedback packet
    Define RTCP eXtended Report (XR) for ECN summary information
  Specifies default reaction based on congestion control algorithm
    Note: discussion of algorithm(s) is out-of-scope
    MAY be other reactions

## Slide 3: Purpose of Draft
Follow-on informational document that extends the discussion of draft-ietf-avtcore-ecn-for-rtp concerning …
  Recommended default congestion control algorithm
  Additional reactions
  Other potential reaction

## Slide 4: Additional Reactions
Signaling
  RSVP
  Diff-serv
Fault Tolerance
  Redundant transmissions
  Application Layer Forward Error Correction
  Codec Swapping
Note:
  Requires downstream peer support
  May require additional security mechanisms

## Slide 5: Potential Other Reactions
draft-ietf-avtcore-ecn-for-rtp
  “MAY be other reactions”…if “considered safe for deployment”
    e.g., emergency communications, though not 911-type
    In other words, make sure the exception is not significantly disruptive
Consider alternative for 1% and 5% of aggregate set
  Exemption or less aggressive back-off reaction
  Emergency Telecommunications Service (ETS) example
    Authorized service
    Reference: rfc-3690, rfc-4190

## Slide 6: Simulation with Gradual Congestion (1)
NS
NS simulator
Normal set of users
  TFRC for ECN and Loss
  50 initial, 50 gradually joining flows
Exception set of users
  TFRC for Loss
  Ignore ECN/CE
  5 flows
Introduce ECN/CE and Loss

## Slide 7: Simulation with Gradual Congestion (2)
NS simulator
Normal set of users
  TFRC for ECN and Loss
  50 initial, 50 gradually joining flows
Exception set of users
  TFRC for Loss
  Ignore ECN/CE
  1 flow
Introduce ECN/CE and Loss

## Slide 8: Default Reaction: Congestion Control Alg.
draft-carlberg-tsvwg-ecn-reactions-00
  Recommends TFRC in response to ECN/Congestion Experience feedback
  Recognizes that TFRC is a “target” versus an absolute
  Observes that TFRC is used in Googletalk, Empathy, and Farsight, Magor

## Slide 9: Questions/Issues
Should a different CC algorithm be used?
  RTCweb is considering a new approach
    draft-alvestrand-rtcweb-congestion-01
      TCP equation to drive the send rate, bounded by path characterization.
Should the Reactions draft avoid singling out a single CC algorithm and only identify a variety of approaches?
Should the “other reaction” example related to emergency communications be moved to the body of the draft?