## Slide 1: Analysis and recommendation for the ULA usage draft-liu-v6ops-ula-usage-analysis-00
Bing Liu(speaker), Sheng Jiang
IETF 82@Taipei
Nov 2011
<number>
Notes: <number>

## Slide 2: Motivation of this draft
ULA (RFC4193) defined in 2005, how to use it seems un-documented and controversial
There are explicit requirements of using ULA in some scenarios (e.g. renumbering, homenet). The use cases are not scenario-specific only, they involve common ULA usage.
So we think it is worth to make comprehensive analysis, and try to make some recommendations according to the discussion
<number>
Notes: <number>

## Slide 3: ULA’s features
FC00::/7 prefix
40bit(or varieties) Global ID to provide (quasi)uniqueness
Independent address space
Not routed globally, only locally
<number>
Notes: <number>

## Slide 4: Contents
General Use Cases
ULA-only: The hosts only configured with ULA.
- Isolated network
- Connected network
ULA + Global address(es)
Some special Use Cases
Private routing
NAT64 pref64
Session identifier
<number>
Notes: <number>

## Slide 5: ULA-only
Isolated network
Straightforward way with minimal administrative cost for address provision
Suitable for close systems, e.g. cars, plane, buildings, which don’t intend to connect to internet
Automatic ULA provision is needed
<number>
Notes: <number>

## Slide 6: ULA-only
Connected network
- Using IPv6 NAT (e.g. NPTv6-rfc6296), rfc1918 mode
Avoiding renumbering from uplink
Better security? (old argument about IP leaking, topology hiding)
Inheriting NAT issues (end-to-end transparency, global multicast .etc)
- Using Proxies
No IP layer connectivity
Ensure high level security; easy to monitor/record/audit user’s behavior
<number>
Notes: <number>

## Slide 7: ULA+Global
ULA for local communication, while Global for outside. Address selection policy is needed.
Benefit to renumbering: Stable local communication while renumbering from uplinks
Argument of operation complexity and cost (may be a common worry about running multiple prefixes in IPv6)
<number>
Notes: <number>

## Slide 8: Some Special Use Cases-1
Privacy routing (Fred Baker, draft-baker-v6ops-b2b-private-routing)
Business to business private link
End-to-end transparent
<number>
Notes: <number>

## Slide 9: Some Special Use Cases-2
Used as NAT64 pref64 (proposed by Cameron Byrne)
ensures that only local systems can use the NAT64 translation
helps clearly identify traffic that is locally contained
Being really used in T-Mobile USA
pref64 shorter than /48 violate the 40bit Global ID of ULA, not recommended to use
<number>
Notes: <number>

## Slide 10: Some Special Use Cases-3
Used as identifier
E.g. RFC6124 BTMM, using ULA as transport-layer identifier
Seems ULA is suitable to be identifier
IPv6-compliant, easy to be grabbed from the stack
(quasi)uniqueness to avoid collision in most of the cases
Stable, assigned to the interface, no need for the application to maintain it
But may have privacy issues
<number>
Notes: <number>

## Slide 11: Thank you! Comments are appreciated Adopted as a WG item? Bing Liu, Sheng Jiang Nov 17-2011, @Taipei
<number>
Notes: <number>