## Slide 1: Current Burst Gap related Drafts
26/7/30
AVTCore IETF 82 Taipei
Jing Zhao (zhaojing@sttri.com.cn)
Sunshine Zhang(Zhangyx@sttri.com.cn)

## Slide 2: Overview
26/7/30
AVTCore IETF 82 Taipei
Two Burst Gap drafts:
  draft-ietf-xrblock-rtcp-xr-burst-gap-loss-00
  draft-ietf-xrblock-rtcp-xr-burst-gap-discard-00
One Burst Gap related draft (Discard Draft)
  draft-ietf-xrblock-rtcp-xr-discard-00
One Burst Gap Summary draft
  draft-zorn-xrblock-rtcp-xr-al-stat-03
Background
  Discard draft discusses discard basic metric
  Two Burst Gap drafts discusses burst gap related basic metric.
  Burst Gap Summary draft add dependency to both Discard draft and two burst Gap drafts.
  Four drafts all focus on transport related terminal metrics.
  00 version contains a few changes
  Follow consensus to draft-ietf-avtcore-monarch

## Slide 3: Common Changes since 00
26/7/30
AVTCore IETF 82 Taipei
Remove tag field in Block header
Add SSRC field in the Block payload.
Remove the reference to tag field that is related to measurement identity draft.
Fix typo on the New XR Block Type value.
Reference update.

## Slide 4: Metrics overview
26/7/30
AVTCore IETF 82 Taipei
1. No dependency between three metric Block
2. Uses a time window to differentiate packet loss and packet discard
3. Uses Gmin or Threshold to distinguish Gap and Burst.
4. Discard metric is used to calculate gap discard rate defined in
Burst Gap Loss Summary XR Block of
Draft-zorn-xrblock-rtcp-xr-al-stat
Dependency overview

## Slide 5: Issue- combined loss/discard
This comment is applied to burst gap loss draft and burst gap discard draft.
Option 1: Yes
  A combined loss/discard draft is more useful for QoE assessment
  Most of measurement results in two draft are redundant
    E.g., Threshold. Sum of Burst duration, Total packet expected in the burst,……
  Suggestion proposed by Alan
    combined to a single burst-gap-loss-discard draft
Option 2: No
  there may be some cases in which reporting only loss may be useful
    Separated as burst-gap-loss-discard and burst-gap-loss drafts
Recommendations:
  In some case, we need combining, in some case we don’t
  Suggestion in the Option 1:
    conflicts with principle developed in MONARCH draft
      Break the following rule:
    “contain a single metric or a small number of metrics relevant to a single parameter “
  Delete redundant data from burst Gap discard draft and only keep packet discard in burst metric.
  combine Loss/discard is required, sent together.
    26/7/30if
AVTCore IETF 82 Taipei

## Slide 6: Issue – early vs late discard
This comment is applied to both burst gap discard draft and discard draft.
Pro:
  identify early vs late discards help to determine what the cause was. (Alan Clark)
  In some case, only later discard is reported.
  It will be useful in sender driven congestion control and Multipath RTP case. (Varun Singh)
Con:
  None
Action:
  Is there any consensus to distinct early discard from late discard?
26/7/30
AVTCore IETF 82 Taipei

## Slide 7: Comments on potential extension to burst gap drafts
These proposed extensions are applied to burst gap loss draft and burst gap discard draft.
Is there a need to add Time Since Last Burst into burst gap drafts?
  Helpful to know when the last substantial loss/discard burst occurred relative to the report time
  But we may estimate time such last burst based on measurement interval carried in the measurement information XR Block?
Is there a need to add Max burst length into burst gap drafts
  Max burst length is important as this is the period that impacted the user most
  This represents the “worst” period from a QoE perspective
Is there a need to add average burst and gap loss/discard rates without keeping and reporting sums/ sums of squares of burst duration?
26/7/30
AVTCore IETF 82 Taipei

## Slide 8: Follow Up
26/7/30
AVTCore IETF 82 Taipei
Question?
WGLC to the following drafts:
  draft-ietf-xrblock-rtcp-xr-burst-gap-loss-00
  draft-ietf-xrblock-rtcp-xr-burst-gap-discard-00
  draft-ietf-xrblock-rtcp-xr-discard-00