## Slide 1: RTCP XR Report Block for Delay metric Reporting draft-ietf-xrblock-rtcp-xr-delay-00
26/7/31
AVTCore IETF 82 Taipei
Kevin Gross (kevin.gross@comcast.net )
Qin Wu (sunseawq@huawei.com)
G. Hunt (r.geoff.hunt@gmail.com )
Alan Clark (alan.d.clark@telchemy.com )

## Slide 2: Overview
26/7/31
AVTCore IETF 82 Taipei
Background
  draft discusses the metric for packet delay.
  The metric belong to transport metrics
  00 version received comments on the list
  00 version contains a few changes
    Follow consensus to draft-ietf-avtcore-monarch
Changes since 00 version
  Remove tag field in Block header
  Add SSRC field in the Block payload.
  Remove the reference to tag field that is related to measurement identity draft.
  Reference update.

## Slide 3: Metric overview
26/7/31
AVTCore IETF 82 Taipei
End System Delay =
accumulation and encoding delay
+
the jitter buffer Delay
+
Decoding delay
+
playout buffer delay
Network Round Trip delay =
Overal Round trip delay
-
end system delay

## Slide 4: Comment from avtcore on One way delay
Network Round Trip delay T0 = One way delay T1 from Source to Receiver + One way delay T2 from Receiver to Source
Is this always true when we say one way delay T1= ½ Network Round Trip Delay T0
  This is not true if the way in two directions is not symmetrical?
26/7/31
AVTCore IETF 82 Taipei
T1
T2

## Slide 5: Open issue for one way delay calculation
Do we have measurement method for one way asymmetric delay?
  E.g., NTP timestamp in SR –arrival time of SR
Problem to the proposed measurement method is :
  how to guarantee wall clock is synchronized
  how accuracy you expect such measurement?
Do we need one way delay to this XRBLOCK
  Option 1:Yes,
    we have use case in IDMS draft,
    And this is not unspecified in any existing XR Block document.
  Option 2: No
    No general way to calculate one way delay
    Complicated calculation if synchronization is not guaranteed.
26/7/31
AVTCore IETF 82 Taipei

## Slide 6: Follow Up
26/7/31
AVTCore IETF 82 Taipei
Need another revision if the open issue is confirmed.
WGLC if there is no open issue?