## Slide 1: RTCP XR Blocks for layered Stream statistics metric reporting draft-xia-xrblock-rtcp-xr-layered-statistics
26/7/31
AVTCore IETF 82 Taipei
Jinwei xia (xiajinwei@huawei.com)
Zorn Glen(gwz@net-zen.net )
Qin Wu (sunseawq@huawei.com)
Roland Schott (Roland.Schott@telekom.de )

## Slide 2: Overview
26/7/31
AVTCore IETF 82 Taipei
Background
  draft-xia-xrblock-rtcp-xr-layered-statistics-01 is split from draft-wu-avt-rtcp-xr-quality-monitoring right after split of avt.
  Draft discusses summary statistics for layered Stream.
  This metric block is more applicable to the case when each layer is sent in its RTP session.
  Changes since 00 version
  Add the layer dependency field in the format of this metric block.
  Clear unused references.
  Other Editorial changes.

## Slide 3: Metric block overview
26/7/31
AVTCore IETF 82 Taipei
  Challenge: when base layer and enhance layer are encapsulated in the same RTP stream, it is a challenge to distinguish the statistics on losses and duplicates in both layers.
Layered stream summary statistics
    Metric name: Lost Layered Component Packets
    Measurement method:
    First identify layer it measured by looking at NAL unit header
    Then count the lost packets in the specific layer
    the number of lost packets is measured in the same way as
    defined in section 4.6 of RFC3611
    Metric name: Dup Layered Component Packets
    Measurement method:
    First identify layer it measured by looking at NAL unit header
    Then count the duplicated packets in the specific layer
    the number of dup packets is measured in the same way as
    defined in section 4.6 of RFC3611

## Slide 4: Next Step
26/7/31
AVTCore IETF 82 Taipei
Adoption as work item?
Question?