## Slide 1: RTCP XR Report Block for Packet Delay Variation Metric Reporting draft-ietf-xrblock-rtcp-xr-pdv-01
26/7/31
AVTCore IETF 82 Taipei
Qin Wu (sunseawq@huawei.com)
G. Hunt (r.geoff.hunt@gmail.com )
Alan Clark (alan.d.clark@telchemy.com )

## Slide 2: Overview
26/7/31
AVTCore IETF 82 Taipei
Background
  draft discusses the metric for packet delay variation.
  The metric belong to transport metrics
  01 version received comments on the list
  01 version contains a few changes
    Follow consensus to draft-ietf-avtcore-monarch
Changes since 00 version
  Remove tag field in Block header
  Add SSRC field in the Block payload.
  Remove the reference to tag field that is related to measurement identity draft.
  Fix typo on SDP parameter from “delay” to “pkt-dly-var”.
  Reference update.

## Slide 3: Metric overview
26/7/31
AVTCore IETF 82 Taipei

## Slide 4: Issue- Cumulative, Interval and Sample metrics
Current draft assigned one bit for Cumulative/Interval indication
Proposal to increase two bits to allow for the indication of a Sampled value
Discussion about sample metric
  PPDV also can be cumulative metric when all the packets in the whole measurement duration are measured.
  PPDV also can be Interval metric when all the packets in the recent measurement Interval are measured.
  Some metrics are sampled and don’t have validity for an interval or a call/session
  PPDV can be a sampled value of a running average and only has validity for the last 200-300ms before the value is sampled.
  When it is impractical to gather all the packets, you may sample a subset of packets during each consecutive measurement Interval.
  PPDV algorithm is better described in sample metric since computation overhead is overwhelming
Action
  Apply this sample indication only to PDV metric? (Qin)
  Apply this sample indication to any future metric? (Alan)
26/7/31
AVTCore IETF 82 Taipei

## Slide 5: Proposed changes
Proposed change to the Interval metric flags in relevant XR blocks:
  Interval Metric flags (I): 2 bits This field is used to indicate whether the ???????????? metrics block is an Interval, Cumulative or Sampled report, that is, whether the reported values apply to the most recent measurement interval duration between successive metrics reports (I=10) (the Interval Duration) or to the accumulation period characteristic of cumulative measurements (I=00) (the Cumulative Duration) or to the value of a continuously measured or calculated that has been sampled at end of the interval (I=01) (Sampled Value).
Proposed change to Monarch draft
  Do we have Interval Metric Flags definition in Monarch draft
    This definition apply to almost all the new metric block
    But it influence monarch draft? No?
    Have definition for terms like interval, cumulative, sample metric?
      Reasonable!
      Interval metric flags definitions should refer to this terms
26/7/31
AVTCore IETF 82 Taipei

## Slide 6: Follow Up
26/7/31
AVTCore IETF 82 Taipei
Question?
WGLC ?