## Slide 1: RTCP XR Blocks for multimedia quality metric reporting draft-wu-xrblock-rtcp-xr-quality-monitoring-04
26/7/31
AVTCore IETF 82 Taipei
Zorn Glen(gwz@net-zen.net )
Qin Wu (sunseawq@huawei.com)
Roland Schott (Roland.Schott@telekom.de )
Kai Lee (leekai@ctbri.com.cn)

## Slide 2: Overview
26/7/31
AVTCore IETF 82 Taipei
Background
  draft-wu-xrblock-rtcp-xr-quality-monitoring-04 is split from draft-wu-avt-rtcp-xr-quality-monitoring prior split of avt.
  3rd presented in the IETF meeting.
  draft discusses QoE metric for multimedia application.
  03 version contains a few changes that follow consensus of monitoring architecture document.
  No IPR concerned.

## Slide 3: Changes since 00 version
26/7/31
AVTCore IETF 82 Taipei
Separate Summary statistics metric, layered stream statistics, synchronization delay and offset from this draft
Use Mos Type field in the XRBlock header to distinguish different MoS types
Define and use a Numeric format for MoS value
Change 32bits MoS Value into 16bits MoS Value
Clarify the algorithm calculation for MoS.
Replace MoS-A with MoS-LQ and MoS-CQ.
Reference update
Other Editorial Changes.

## Slide 4: Metric block overview
Multimedia QoE metrics
    Metric Block Name: Multimedia Quality Metrics Block
    Metric Name: MoS Value
    Measurement method:
    If MoS type is MoS-LQ and MoS-CQ, use measurement method defined in ITU-T Recommendation [G.107][P.564] or ETSI TS ETSI TS 101 329-5.
    If MoS type is MoS-V or MoS-AV, use measurement method defined in [P.NAMS],[P.BNAMS].
26/7/31
AVTCore IETF 82 Taipei

## Slide 5: Open issue
Issue 1: Do we need to distinguish different MOS algorithms to calculate MOS value for each MOS Type?
  Option 1: Yes
    it is more desirable to use signaling to distinguish them? No need to reflect it in the XR format.
  Option 2:Yes
    assign additional field in XR Block payload to distinguish them?
  Recommendation:
    Option 1:
Issue 2: Do we need to distinguish collecting data from different channel?
  Option 1:Yes,
    assign additional field in XR Block payload to distinguish them?
  Option 2: No,
    audio data in all channel is typically carried in one RTP flow,
    Layered video sent in each RTP flow.
  Recommendation:
    Leave this for specific implementation.
26/7/31
AVTCore IETF 82 Taipei

## Slide 6: Follow Up
26/7/31
AVTCore IETF 82 Taipei
Adoption as work item?
Question?