## Slide 1: RTCP XR Block for TS Decodability Statistics Metric
Draft-huang-xrblock-rtcp-xr-decodability-01
Rachel Huang ( rachel.huang@huawei.com )
Hitoshi Asaeda (asaeda@wide.ad.jp)
Qin Wu ( bill.wu@huawei.com )

## Slide 2: Status
Separated from draft-wu-avt-rtcp-xr-quality-monitoring based on Colin’s comments and suggestions.
Presented in the chair’s presentation in the IETF 79th, Beijing.
In compliance with monitoring architecture [draft-ietf-avtcore-monarch-05].

## Slide 3: Overview
Evaluate the content quality at the application layer is a problem for operators.
Define a new metric report block for MPEG transport streams.
The new metric follows ETSI TR 101 290.
The new metric can be applied to any codecs using Transport Stream.

## Slide 4: The Proposed Packet Format
Block Header
First Priority
Parameters
Second Priority Parameters

## Slide 5: Decodability Metric Block
8 most universal metrics from [ETSI TR 101 290] are adopted to decodability metric block.
  First Priority
    TS Synchronization Losses , Sync byte errors, Continuity count errors
  Second Priority
    Transport errors, PCR errors, PCR repetition errors, PCR discontinuity indicator errors, PTS errors.

## Slide 6: Next Step
Request for adoption as a new work item.