## Slide 1: DHCPv6/SLAAC Interaction Gaps (draft-liu-6renum-dhcpv6-slaac-switching-01) [Note: the title is different with the original one in the draft]
Bing Liu(speaker), Wendong Wang, Xiangyang Gong
@6man-IETF 84-Vancouver
Aug 2012

## Slide 2: Background 1/2
DHCPv6 and SLAAC are interacted by M/O flags in RA
“Managed Flag”: indicating the hosts there’s DHCPv6 available in the network
“OtherConfig Flag”: indicating other parameter (DNS, Routing .etc) available by DHCPv6

## Slide 3: Background 2/2
Behavior of interpreting M/O is ambiguous
In the old SLAAC standard (rfc2462), it had some clear specification of how to interpret the M/O flags when the hosts receive RAs
But it was removed in current SLAAC (rfc4862), the reason was “considering the maturity of implementations and operational experiences. [RFC4862]”

## Slide 4: But now the situation is…
Requirement of clear M/O behavior emerges in ISP
As I learned, there’s an ISP deploying IPv6 networks, they had strong requirement of clear M/O definition. But since the SLAAC standard is ambiguous, they had to directly specify to the CPE vendors. (This may be a common requirement for ISPs)
Behaviors of major desktop OSes had been varied
Desktop OSes are far more difficult to be customized than CPE, so this issue could be a problem for the network configuration/management.
We did a test on the OSes’ behaviors

## Slide 5: Test of major desktop OSes’ behaviors
We only tested M flag, since the draft’s scope is address configuration
Important test results (Windows 7; Linux-Ubuntu12.04-kernel-3.2.12; OS X Lion-10.7.3):
Windows 7 would start DHCPv6 discovery if there’s no RA for some time; Linux&OS-X only start DHCPv6 until receive RA with M=1 (unless you manually change the OS settings to “DHCPv6-only”)
SLAAC-configured hosts receiving RA with M=1: Win7 would start DHCPv6 and keep SLAAC; Linux/OS-X no action
DHCPv6-configured hosts receiving RA with M=0: Win7 would release DHCPv6 address and do SLAAC; Linux/OS-X no action
Some treat M as Prescriptive while some just Advisory
M flag semantic is ambiguous in standard

## Slide 6: Potential semantics of DHCPv6/SLAAC interaction
#1 Network provides both, let the hosts select by themselves (exactly current RFC4862 does)
#2 Network wants hosts to do DHCPv6 when online (Sending RAs M=1 and don't include PIO (Prefix Information Option), the host would "have to" initial DHCPv6, but it depends on the OS implementation, not decided by the network, a standard gap)
#3 Network wants the already SLAAC-configured hosts to do DHCPv6 (This may be a requirement in renumbering. With M=1, Win7 is OK, Linux/OS-X won’t work, this is a standard gap)
#4 Network wants the hosts to switch from DHCPv6 to SLAAC (Also may be a requirement in renumbering. With M=0, Win7 is OK, Linux/OS-X won’t work, a standard gap. )

## Slide 7: Proposed Solution-candidate 1
Clearly re-defining the M/O flags as Prescriptive. This can cover:
#2 Network wants hosts to do DHCPv6 when online
#3 Network wants the already SLAAC-configured hosts to do DHCPv6
#4 Network wants the hosts to switch from DHCPv6 to SLAAC
But would lose:
#1 Network provides both, let the hosts select by themselves

## Slide 8: Proposed Solution-candidate 2
Leave the current M/O flags as it is, covering #1
Using another reserved bit as “DHCPv6-Required” flag to cover #2 #3
Using one more bit as “ReleaseDHCPv6” flag to cover #4

## Slide 9: Questions
Do you agree the potential semantics?
Does 6man think we need to fix the M/O issue in standard?

## Slide 10: Comments? Thank you leo.liubing@huawei.com wdwang@bupt.edu.cn xygong@bupt.edu.cn Aug 1, @Vancouver