## Slide 1: IPv6 Site Renumbering Gap Analysis draft-ietf-6renum-gap-analysis-02
Bing Liu (speaker), Sheng Jiang, Brian.E.Carpenter, Stig Venass
IETF 84@Vancouver
July 2012
Notes: <number>

## Slide 2: Main revisions 1/3
Added a brief description of IPAM (IP address management) tools
in 3.2 : Existing Components for IPv6 Renumbering - Management Tools
IPAM tools usually integrate DHCP and DNS
Normally they don’t have a dedicated renumbering function.
However, their integration can benefit the renumbering process.
Notes: <number>

## Slide 3: Main revisions 2/3
Added two topics in “renumbering notification”
“router awareness” and “border filtering”, which are moved from enterprise scenarios draft
Deleted MSDP peers renumbering consideration
Since it is not IPv6 relevant
Notes: <number>

## Slide 4: Main revisions 3/3
Updated SLAAC/DHCPv6 co-existence issue analysis
A few notes were added in 5.1
(We have issued a new draft draft-liu-6renum-dhcpv6-slaac-switching, which is dedicated for the co-existence issue, but as a potential solution this is not in scope of 6renum at this time)
Notes: <number>

## Slide 5: Comments? Thank you leo.liubing@huawei.com jiangsheng@huawei.com brian.e.carpenter@gmail.com svenaas@cisco.com July 31, @Vancouver
Notes: <number>

## Slide 6: DHCPv6/SLAAC Address Configuration Switching for Host Renumbering draft-liu-6renum-dhcpv6-slaac-switching
Bing Liu (speaker), Wendong Wang, Xiangyang Gong
6renum@IETF 84
July 2012
Notes: <number>

## Slide 7: Background
The ambiguous M/O flags in RA messages
The old SLAAC standard (RFC 2462) had some clear specification of how to interpret the M/O flags when the hosts receive RAs
But it was removed in the current SLAAC standard (RFC 4862), the reason was “considering the maturity of implementations and operational experiences. [RFC4862]”
Notes: <number>

## Slide 8: But now the situation is…
Some requirements emerge from ISP
E.g. when an ISP is deploying IPv6 networks, they have a strong requirement of clear M/O definition. But since the SLAAC standard is ambiguous, they had to directly specify what they wanted to the CPE vendors.
Behaviors of major desktop OSes has varied
Windows 7 interprets M flag differently with Linux/OS X
Desktop OSes are far more difficult to be customized than CPEs, so this issue could be a problem for network management.
Notes: <number>

## Slide 9: Especially in renumbering
SLAACed hosts may need to switch to DHCPv6, or vice versa
Because the network may split, merge, relocate or be re-organized. Then the address configuration mode may need to switch.
How does the network make the hosts switch from SLAAC to DHCPv6? (Currently, M changed from 0 to 1 is just nonsense for Linux/OS X.)
How about from DHCPv6 to SLAAC? (If M changed to 0, Win7 will do it, but it is still nonsense for Linux/OS X.)
These are standard gaps. We may need a clearer specification of host behavior.
Notes: <number>