## Slide 1: RTP Media Stream Pause / Resume
draft-westerlund-avtext-rtp-stream-pause-02
Bo Burman
Notes: 2011-10-19
<number>

## Slide 2: IPR Disclosure
For referred draft-westerlund-avtext-rtp-stream-pause
  http://datatracker.ietf.org/ipr/1641/
Unchanged since -00

## Slide 3: Presentation Goal
WG consensus that it is a desired feature
WG consensus on suitability of proposed solution
Adoption as WG draft

## Slide 4: Problem and Motivation
Whenever there are more RTP media senders than presentation resources, some media may not be presented by any receiver, wasting uplink and possibly downlink bandwidth
Applicable also in other multi-party or multi-stream situations
Need for a stream can be based on central forwarding decisions or end-user UI interactions, and can thus be highly dynamic
Pausing has fairly relaxed timing, but resuming can be time critical
Different appropriate media receiver actions when sender intentionally pauses and when stream is not received for some other reason

## Slide 5: Wanted Functionality
Request to pause sending an RTP media stream (SSRC)
  Media receiver  media sender: temporarily stop sending
Indicate that an RTP media stream is temporarily paused
  Media sender  media receiver(s): certain media stream is active, but does currently not send any data
  Regardless of reason; on request or local media sender decision
  Indicate at what point stream was paused (eases loss handling)
Request to resume sending an RTP media stream
  Media receiver  media sender: quickly resume paused media
Explicit indication that the functionality is supported
  Separate support for request (pause) and indication (paused)
  Separate support for sending and receiving messages

## Slide 6: Main Topologies
Centralized (Star) Conference
Point-to-point
Conf
A
B
C
D
A
B
Multimedia conferencing is main targeted application
Solution will work reasonably also for multipoint topologies

## Slide 7: Signaling Performance Evaluation
Comparing SIP / SDP and RTCP based signaling
Wireless (4G) and fixed access
Favorable and unfavorable cases, while still reasonable
SIP
  Single audio and single video, compliant with 3GPP
  UDP, but TCP if message exceeds IP MTU
  Wireless signaling bearer may have to be re-established
RTCP
  200 kbps media  10 kbps RTCP
  Minimal compound RTCP packet (SR, SDES CNAME)
  Expected value used for randomized time components
Additional pre-conditions and assumptions in draft text

## Slide 8: Assumed Signaling Topology
AS
SIP Proxy
SIP Proxy
Media Server
Alice
Bob
Border Gateway
Signaling Gateway
Border Gateway
Signaling Gateway
SIP
SIP
SIP
SIP
SIP
SIP
SIP / H.248
Alice’s Provider’s Network
Bob’s Provider’s Network
RTCP
RTCP
RTCP
RTCP
Signaling Gateway
Signaling Gateway
Alice
Bob

## Slide 9: Signaling Message Size
1650
SIP
RTCP
250
500
750
1000
1250
1500
bytes
525
125
50
Dynamic SIP/SDP SigComp [RFC 5049]
Reduced size packet [RFC 5506]

## Slide 10: Transport Delay Wireless 4G
305
SIP
RTCP
50
100
150
200
250
300
ms
110
260
30
Uplink channel re-establishes fast
85
SIP
RTCP
70
225
25
255
SIP
RTCP
75
230
20
Wireless UA to Wireless UA
Wireless UA to Media Server
Media Server to Wireless UA
200 kbps media
Due to RTCP scheduling, not size
Downlink channel re-established because entered low-power state

## Slide 11: Transport Delay Wireless 4G
305
SIP
RTCP
50
100
150
200
250
300
ms
110
115
30
Uplink channel re-establishes fast
85
SIP
RTCP
70
80
25
255
SIP
RTCP
75
80
20
1000 kbps media
Wireless UA to Wireless UA
Wireless UA to Media Server
Media Server to Wireless UA
Due to RTCP scheduling, not size
Downlink channel re-established because entered low-power state

## Slide 12: Transport Delay Fixed
SIP
RTCP
50
100
150
200
250
300
ms
65
205
25
SIP
RTCP
50
200
15
SIP
RTCP
50
200
15
Fixed UA to Fixed UA
200 kbps media
Media Server to Fixed UA
Fixed UA to Media Server
Due to RTCP scheduling, not size
No unfavorable case; no bearer re-establishment and message size is a minor concern

## Slide 13: Transport Delay Fixed
SIP
RTCP
50
100
150
200
250
300
ms
65
60
25
SIP
RTCP
50
55
15
SIP
RTCP
50
55
15
Fixed UA to Fixed UA
1000 kbps media
Media Server to Fixed UA
Fixed UA to Media Server

## Slide 14: Chosen Signaling Technology
Media plane signaling chosen; extend CCM (RFC 5104)
  Responsive
  Bandwidth efficient
  Signaling has direct impact on media streams
  Localized to media stream; small session impact
Capability for solution is explicitly signaled in SDP

## Slide 15: Solution Relation to SDP
SDP handles semi-static properties of media descriptions
  Opening
  Closing
  Directionality
  Activating
  Inactivating
This draft targets
  One or more media streams (SSRC) within such media description
  Request to pause temporarily
  Explicit indication of pausing
  Request to resume from temporary pause

## Slide 16: Solution Relation to CCM
CCM TMMBR 0 kbps as PAUSE
  Any media receiver “pausing” will immediately pause stream
  This draft desires “consensus”; don’t pause if anyone wants stream
CCM TMMBR >0 kbps as RESUME
  TMMBR semantics requires guard period before increasing bitrate
  Contradictory to RESUME likely being time critical
CCM TMMBN 0 kbps as PAUSED
  Will likely work, but cannot provide any stream state information
CCM TMMBN as REFUSE for PAUSE and RESUME
  TMMBN semantics does not allow for refusing a TMMBR 0
  TMMBN semantics does not always allow for refusing TMMBR>0

## Slide 17: Solution Overview
Type=0
PAUSE request
PauseID
Parameter Len=0
RTP Extended Highest Sequence Number
All messages have a common SSRC of sender from RFC 5104, and each message also has a separate Target SSRC
RESUME request
REFUSE notification
Allows repeated requests; RTCP is lossy
Type=1
PauseID
Parameter Len=0
PAUSED indication
Type=2
PauseID
Parameter Len=1
Same as in effective PAUSE and/or PAUSED messages, and allows repeat
Type=3
PauseID
Parameter Len=0
Same as in refused PAUSE or RESUME message
The one valid when the stream was paused
Same as in PAUSE, or incremented from last PAUSED
Multiple messages can be sent in the same RTCP CCM message
Media sender decides!

## Slide 18: Way Forward
Should the problem be solved?
Is the proposed solution favored by the WG?
Should the draft be adopted as a WG draft?