## Slide 1: Bidirectional Forwarding Detection (BFD) on Link Aggregation Group (LAG) Interfaces Interfaces
Authors:
Manav Bhatia
Mach Chen
Sami Boutros
Marc Binderberger
Jeff Haas
<number>
Draft-mmm-bfd-on-lag-05
Presenter:
Sami Boutros
IETF84, July 2012
Notes: <number>

## Slide 2: Changes from 03  05 (Dedicated MAC)
Dedicated MAC address MUST be used for the immediate next hop when micro BFD session is in the Down/AdminDown and Init state.
In the Up state, the MAC address from the received BFD packets for the session MUST be used.
Micro BFD packets MUST always be sent untagged.
When operating in the context of IEEE 802.1q or IEEE 802.qinq, the micro BFD packets should either be untagged or sent with a vlan tag of Zero (802.1p priority tagged).
Implementations compliant to this standard MUST be able to receive both untagged and 802.1p priority tagged micro BFD packets.
<number>

## Slide 3: Changes from 03  05 (LACP interaction)
Addressed IEEE Liaison, no LACP interaction !!!
The LMM uses the status of the BFD session to determine whether the member link should be included in the LAG L2 load balance table.
Prior to LACP coming up, the micro BFD session is Passive and does not send BFD control packets.
Even when LACP is used and considers the member link to be ready to forward traffic, the member link is only used by the traffic load balancer when the micro BFD session is Up.
<number>

## Slide 4: Next steps
Any more comments are appreciated.
Ready for WG adoption.
Thank you
<number>