## Slide 1: WSON General WG Drafts
Routing and Wavelength Assignment Information Model for WSON (v14)
General Network Element Constraint Encoding for GMPLS Controlled (v08)
OSPF-TE Extensions for General Network Element Constraints (v04)

## Slide 2: Authors/Contributors
Greg Bernstein (Grotto Networking)
Diego Caviglia (Ericsson)
Ander Gavler (Acreo AB)
Jianrui (Rebecca) Han (Huawei)
Young Lee (Huawei)
Dan Li (Huawei)
Wataru Imajuku (NTT)
Jonas Martensson (Acreo AB)
Itaru Nishioka (NEC Corp.)
Pierre Peloso (ALU)
Rao Rajan (Infinera)
Plus a whole lot of folks on the CCAMP list and at the last five years of meetings.

## Slide 3: draft-ietf-ccamp-rwa-info-14.txt
Routing and Wavelength Assignment Information Model for Wavelength Switched Optical Networks
  No Changes
  Last changes from 13 to 14 version only clarification text
  Informational Document
  Ready for Last Call

## Slide 4: draft-ietf-ccamp-general-constraint-encode-08.txt
General Network Element Constraint Encoding for GMPLS Controlled Networks
  Changes from 07 version:
  In port label constraint changed reserved field to Switching Capability and Encoding to allow for self description of labels used and interface capability.
  Only applies for RestrictionType == Simple Label
  Switching Cap (RFC4203), Encoding (RFC 3471)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MatrixID | RestrictionType| Switching Cap | Encoding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Additional Restriction Parameters per RestrictionType |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 5: draft-ietf-ccamp-general constraint-encode-08.txt
Resolution flex-grid and ISCD concerns
  List e-mail 6/18/2012 explaining how available labels and shared backup labels can be used for link resource availability for a wide range of technologies if desired.
  Explained that these fields can be used in ISCD. The use of these fields in ISCD did not change this document (changes made in general constraint OSPF-TE) but did prompt the previous enhancement of the port label constraint.
Document is ready for WG Last Call

## Slide 6: draft-ietf-ccamp-gmpls-general-constraints-ospf-te-04.txt
OSPF-TE Extensions for General Network Element Constraints
  Changes from 03
  Removed Available Labels and Shared Backup Labels TLVs and modified text appropriately
    It was requested that these be put in the ISCD field. Extension of ISCD field is technology specific. WSON use is now described in WSON specific OSPF extensions.

## Slide 7: draft-ietf-ccamp-gmpls-general-constraints-ospf-te-04.txt
All comments resolved. Last discussed on list 6/18/2012
Document is ready for WG Last Call