## Slide 1: LMP Test Messages Extensions for Evolutive OTN
draft-ceccarelli-ccamp-gmpls-g709-lmp-test-04
CCAMP WG, IETF 84th Vancouver

## Slide 2: Authors/Contributors
Daniele Ceccarelli
  daniele.ceccarelli@ericsson.com
Diego Caviglia
  diego.caviglia@ericsson.com
Francesco Fondelli
  francesco.fondelli@ericsson.com
Fatai Zhang
  zhangfatai@huawei.com
Dan Li
  danli@huawei.com
Dieter Beller
  dieter.beller@alcatel-lucent.com

## Slide 3: Agenda
Recap up to -03
  Link Connectivity Verification [RFC4204]
    BEGIN_VERIFY class
  Trace Monitoring
    New TRACE object for G709v3
    Discovery response message for Layer Adjacency discovery
Changes from -03 to -04
Next steps

## Slide 4: Link Connectivity Verification
In band transmission of test messages over data link to verify physical connectivity, discover DP resources, exchanged IF_Id
Begin Verify Class: [RFC4204]

## Slide 5: Trace Monitoring
Trace Object Class: [RFC 4207]
  New C-Type (2)
  Trace Type: Used to identify the type of trace message
    ODU TTI, OTU TTI and 6 levels of TCM
  Trace Message:
    Includes the value of the expected message to be received in-band.
    The valid length and value combinations are determined by the ITU.T G.709 recommendation

## Slide 6: Discovery Response Message for Layer Adjacency Discovery
[G.7714.1] – Automatic layer adjacency discovery procedure applicable to G.709 OTN
  Discovery message sent via TTI
  Appendix III of G.7714.1 describes how to send a discovery response message to the originator (“discovery agent”) via LMP.
  TraceMonitor message [RFC4207] is used to convey the discovery response message.
  Discovery response message attributes mapping into TraceMonitor message objects or other fields of the LMP message

## Slide 7: From -03 to -04
Removed non normative signal types
  ODU3e1, ODU3e2 – G.sup43
LMP behavior negotiation updated
    OTN test bit in the BehaviorConfig (c-type=3)
    O bit – Indicates support for the OTN specific test messages defined in this ID

## Slide 8: Next steps
Keep on monitoring G.7714.1
G.709v3 OTN data plane stable
G.709v3 OTN control plane stable
   Adopt as working group document

## Slide 9: QUESTIONS ?
THANK YOU