## Slide 1: draft-ali-ccamp-rc-objective-function-metric-bound-02.txt draft-ali-ccamp-rsvp-te-include-route-02.txt draft-ali-ccamp-xro-lsp-subobject-02.txt
CCAMP
IETF 84 – Vancouver
July – August 2012

## Slide 2: draft-ali-ccamp-rc-objective-function-metric-bound-02.txt b draft-ali-ccamp-rsvp-te-include-route-02.txt g draft-ali-ccamp-xro-lsp-subobject-02.txt d
Authors list – as per the superscript:
  Zafar Ali bgd Cisco Systems
  Luyuan Fang b Cisco Systems
  Clarence Filsfils bgd Cisco Systems
  Gabriele Maria Galimberti g Cisco Systems
  Ori Gerstel gd Cisco Systems
  Matt Hartley d Cisco Systems
  Kenji Kumaki bgd KDDI Corporation
  Rüdiger Kunze bgd Deutsche Telekom AG
  Julien Meuric d France Telecom Orange
  George Swallowbgd Cisco Systems

## Slide 3: Overall Problem Space
The GMPLS UNI-C or NNI is blind to valuable information that a network may be willing to supply
The aim is to allow increased information flow across such boundaries, while respecting that not everything can or will be shared
Though of a theme, each draft stands on its own
Two drafts are focused on better understanding and use of metrics
Two are focused on diversity and better use of SLRG information
All are work in progress

## Slide 4: Overall Problem Space (2)
UNI-C
UNI-N
NNI
UNI-C
UNI-N
NNI
UNI-C
UNI-N
The “NNI” could as well be an inter-area or interdomain TE link
A TE headend has loss of visibility across these links

## Slide 5: Overall Problem Space (2)
UNI-C
UNI-N
NNI
NNI
UNI-C
UNI-N
The “NNI” could as well be an inter-area or interdomain TE link
A TE headend has loss of visibility across these links

## Slide 6: Objective Function
draft-ali-ccamp-rc-objective-function-metric-bound
Network performance criteria (e.g. latency) are becoming critical to path selection (e.g., in financial networks).
Providers are interested in paths that meet multiple constraints
For example,
  a financial customer wants a path that meets a certain delay
  The service provider is interested in the minimum cost path that meets that requirement
Extensions to the PCE have already been made to express objective functions

## Slide 7: Objective Function at a UNI
At a UNI
  The UNI-C may not have access to a PCE
  Or the UNI-N is fully capable of performing the calculations and thus no PCE has been deployed
When ERO contains loose hops, e.g., in inter-domain and GMPLS overlay cases, there is a need to carry objective function and/ or metric bounds.
15454
R5
R1
R10
R7
R3
R8
R2
R4
R9
R6
UNI
UNI
Path with Objective Func/
Metric bounds

## Slide 8: Expressing the Objective Function
Objective Function is tied to a loose hop
Two new ERO subobject types, Objective Function (OF) and Metric, are defined.
  OF subobject conveys a set of one or more specific optimization criteria that MUST be followed in expanding route of a TE-LSP.
  Metric subobject indicates the bound on the path metric that MUST NOT be exceeded for the loose segment
Note: Draft needs to be updated for the case where a loose hop expansion results in the insertion of a new loose hop

## Slide 9: Homogeneity and Fate-sharing
draft-ali-ccamp-rsvp-te-include-route
Requirement is to have two LPSs to follow same route:
  Fate Sharing.
  Homogeneous Attributes: E.g., when FA/RA-LSPs are bundled together, it is often required that the LSPs to have same delay and DV characteristics.
The ingress node requires certain SLRGs to be explicitly “included” when the loose hop is expanded.
  This derives, for instance, from an overall link diversity plan

## Slide 10: Homogeneity and Fate-sharing(2)
Ingress node may lack sufficient topological knowledge
It there must form an ERO with loose hop(s)
It cannot divide those loose hop(s) into a proper sequence of strict or a sequence of finer-grained loose hops (e.g., in inter-domain and GMPLS overlay networks).
UNI-C
UNI-N
NNI
NNI
UNI-C
UNI-N

## Slide 11: Homogeneity and Fate-sharing: Solution
Explicit Inclusion Route Subobject (EIRS)
  A new ERO subobject type
  Indicates an inclusion between a pair of explicit or abstract nodes
Encoding and processing rules are similar to Explicit Exclusion Route Subobject (EXRS) subobject of ERO defined in [RFC4874],
  (the exception being include vs. exclude semantics)
Subobjects supported by XRO/ EXRS are supported
  i.e., inclusion of links, nodes, SRLGs, tunnel/ LSP, unnumbered interfaces, etc.

## Slide 12: Route Diversity using Exclude Routes
draft-ali-ccamp-xro-lsp-subobject
Not all use-cases are covered with the existing XRO subobjects
  Exclusion of the route of an LSP
    Where the ingress node is denied RRO by policy
    Which does not involve the node signaling the diverse LSP
  LSP diversity is a responsibility of the server layer
    Permits client layer to broadly express diversity requirements

## Slide 13: Processing node exception
Optical UNI interface
Optical node has extremely high dataplane availability
Processing node is an acceptable exception
15454
R5
R1
R10
R7
R3
R8
R2
R4
R9
R6
UNI
UNI

## Slide 14: LSP Subobject
New LSP subobject of Exclude Route (XRO) Object and Explicit Exclusion Route Subobject (EXRS) defined in [RFC4874].
Carries FEC of the LSP or Tunnel from which diversity is desired
Defines flags:
  Exclusion-Flags: SRLG, Node, & Link exclusion.
  Attribute Flags:
    LSP ID ignored (Tunnel Exclusion)
    Destination node exception
    Processing node exception
    Penultimate node exception
  Last 3 are oriented toward UNI interface

## Slide 15: draft-ali-ccamp-xro-lsp-subobject: Solution
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|L| Type | Length |Attribute Flags|Exclusion Flags|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IPv4 tunnel end point address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Must Be Zero | Tunnel ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extended Tunnel ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IPv4 tunnel sender address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Must Be Zero | LSP ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Exclusion-Flags: SRLG exclusion, Node exclusion, Link exclusion.
Attribute Flags: LSP ID to be ignored, Destination node exception, Processing node exception, Penultimate node exception.

## Slide 16: Next Steps
Call for workgroup adoption
Solicit further input from the WG