## Slide 1: draft-dharinigert-ccamp-g-698-2-lmp-00
Dharini Hiremagalur; Ruediger Kunze; Gert Grammel; Gabriele Galimberti; Manuel Paul; John Drake

## Slide 2: Extended LMP Model

## Slide 3: G.698.2 (Black Link)-LMP
Goal: LMP correlates the link properties east and west of G.698.2 reference points
Non-Goal: LMP is neither a routing or signaling protocol
How it works for standard application codes:
  When connected, Router and Optical Line System perform discovery procedures and exchange Application codes
How it works for proprietary application codes:
  When connected, Router and Optical Line System perform discovery procedures and exchange capabilities such as e.g.:
    Tuning range (e.g. 96 OCh) vs. line system design (e.g. 40 Ch)
    Tuning precision (e.g. 50GHz) vs. Grid (e.g. 100GHz)
  Each side performs a property correlation e.g.
    Smallest common denominator: 40 Ch, 100GHz
  If one side of the link changes its property, the peering side is notified and updated accordingly
    Optical Management system configures available Wavelength set to one specific set of channels (e.g. by tuning filters)
    Router side is informed
    Both sides perform property correlation with updated data

## Slide 4: Link Property exchange
SNMP
NMS
OLS
OXC
NMS
SNMP
Link property exchange
Transponder capabilities
λ
Tx
dB
dB
Rx
Network Tolerance
λ
Tx
dB
dB
Rx
Operation range
Operation range
λ
Tx
dB
dB
Rx
λ
Tx
dB
dB
Rx
Link property correlation

## Slide 5: Next Steps
Stay aligned with draft-galimbe-kunze-g-698-2-snmp-mib-xx.txt
Include threshold information?
Include laser behavior (automatic shutdown, manual, …) in the information exchange?
Generalization for WSON?