## Slide 1: RSVP-TE Based MPLS LI & LB
J. Dong, M. Chen (Huawei), Z. Li (China Mobile)
IETF84 CCAMP July 2012 Vancouver
draft-dong-ccamp-rsvp-te-mpls-tp-li-lb-03

## Slide 2
In-band/NMS based LI & LB is defined in RFC 6435
LI and LB affect the data plane of the LSP
  As enabler of some other OAM functions
When dynamic control plane exists, could perform LI & LB through control plane signaling
  Ensure control plane & data plane consistency
  Does not rely on TTL expiration
Mechanism also applicable to other technologies using GMPLS
Background

## Slide 3
The Lock part is changed
  Re-use existing bits when possible (Thanks Lou, Fei and Francesco for the discussions)
  A (Administratively down) bit in ADMIN_STATUS is re-used for lock/unlock signaling
The Loopback part is unchanged in this version
  Wait for the discussion & progress of Cyril’s draft-lsp-attribute-ero
  Would like to revise this part accordingly when there is consensus
Change & Unchange in v-03

## Slide 4: RSVP-TE Based LI & LB
One re-used & one new flag in ADMIN_STATUS Object
  A: Administratively Down, re-used for Lock Instruct
  B: LoopBack
Lock Instruct is signaled using Path/Resv message
  MEP to MEP
Loopback is signaled using Notify message
  MEP to MIP or MEP to MEP
  May be revised in next version

## Slide 5
Revise the loopback part based on the progress of draft-lsp-attribute-ero
Further comments are welcome
Is this work useful to the WG?
Next Steps

## Slide 6: Operations – Lock Instruct
Lock
  Sending MEP: Path message with A and R bit set
  Receiving MEP:
    Success: Resv message with A bit set
    Failure: PathErr message with new OAM Error Value “Lock Failure”
Unlock
  Sending MEP: Path message with A bit cleared and R bit set
  Receiving MEP:
    Success: Resv message with A bit cleared
    Failure: PathErr message with new OAM Error Value “Unlock Failure”
LER1
LSR1
LER2
LSR2
perform Lock operation
Path with A and R set
Resv (success) or
PathErr (failure)

## Slide 7: Operations – Loopback
Enter Loopback
  Sending MEP: Notify message with A, B and R bit set
  Receiving MIP/MEP:
    Success: Notify message with A and B bit set and Error Code “0”
    Failure: Notify message with new OAM Error Value “Loopback Failure”
Exit Loopback
  Sending MEP: Notify message with A, R bit set and B bit cleared
  Receiving MIP/MEP:
    Success: Notify message with A bit set and B bit cleared and Error Code “0”
    Failure: Notify message with new OAM Error Value “Exit Loopback Failure”
LER1
LSR1
LER2
LSR2
Perform Loopback Operation
Notify with A, B and R set
Target node is LSR2
Notify the result