## Slide 1: Framework for GMPLS based control of Flexi-grid DWDM networks draft-ogrcetal-ccamp-flexi-grid-fwk-00 CCAMP WG, IETF 84
Oscar González de Dios, Telefónica
Ramon Casellas, CTTC
Fatai Zhang, Huawei
Xihua Fu, ZTE
Daniele Ceccarelli, Ericsson
Iftekhar Hussain, Infinera
Contributors:
Qilei Wang, Malcolm Betts, Sergio Belotti, Cyril Margaria, Xian Zhang, Yao Li, Fei Zhang, Lei Wang, Guoying Zhang, Takehiro Tsuritani, Lei Liu, Eve Varma, Young Lee, Jianrui Han, Sharfuddin Syed, Rajan Rao, Marco Sosa, Biao Lu, Abinder Dhillon, Felipe Jimenez Arribas, Andrew G. Malis, Adrian Farrel, Daniel King.
v6

## Slide 2: Intro draft-ogrcetal-ccamp-flexi-grid-fwk-00
Merge of previously submitted framework drafts:
  draft-zhang-ccamp-sson-framework-00
  draft-wang-ccamp-gmpls-flexigrid-framework-01
  draft-syed-ccamp-flexgrid-framework-ext-00
  draft-zhang-ccamp-flexible-grid-requirements-01.txt
Inputs from
  draft-li-ccamp-grid-property-01
  latest discussions / feedback from ITU-T (informal correspondence).
    [G.694.1] ITU-T Recommendation G.694.1, “Spectral grids for WDM applications: DWDM frequency grid”, draft v1.6 2011/12", 2011.
    [G.872] ITU-T Recommendation G.872, “Architecture of optical transport networks, draft v0.12 2012/03 and v0.13 2012/08 (for discussion)", 2012.
    [G.709] ITU-T Recommendation G.709, “Interfaces for the Optical Transport Network (OTN)", March 2009.

## Slide 3: What is the draft about?
Goals
  Establish a framework, for the purposes of GMPLS control, of ITU-T DWDM flexi-grid enabled networks, including
    Terminology,
    Data plane element models (i.e., “link and node characterization”),
    Layered / hierarchical network model (new – not yet agreed),
    Routing and Spectrum Assignment modes
  Lockstep with ITU-T data plane standardization
  Identify Control Plane Requirements (new)
    single document covering framework and requirements
Non Goals
  Define protocol extensions / encodings  Separate solutions draft

## Slide 4: Terminology: ITU-T flexi-grid “frequency slot”
Central Frequency = 193.1 THz + n * 0.00625 THz
Slot Width : the full width (in Hz) of a frequency slot, a multiple (m) of 12.5 GHz.
Frequency Slot: The frequency range allocated to a channel and unavailable to other channels within a flexible grid. A frequency slot is defined by its nominal central frequency and its slot width.
Flexi-Grid: a new WDM frequency grid defined with the aim of allowing flexible optical spectrum management, in which the Slot Width of the frequency ranges allocated to different channels are flexible (variable sized).
DWDM link
0
1
2
3
4
5
6
7
8
9
-9
-8
-7
-6
-5
-4
-3
-2
-1
Frequency slot 1:
Central frequency = 193.1 + 0.00625*(-5)
= 193.06875 THz
Slot width = 0.0125*3 = 0.0375 THz
Frequency slot 2:
Central frequency = 193.1 + 0.00625*(4)
= 193.125 THz
Slot width = 0.0125*4 = 0.05 THz
193.1 THz
...
…

## Slide 5: Frequency Slots
As a physical layer / data plane entity, frequency slots are “flat”
  The media does not support a hierarchy of frequency slots
As frequency (sub)ranges, they can (conceptually) be considered hierarchical
  By management / control
  A FS that spans the fiber “contains” several FS and, within a FS, a SSFS “contains” a single optical signal
Fig source: Malcolm, Xihua (ZTE)

## Slide 6: Terminology
SSON: Spectrum-Switched Optical Network
[open issue, cfr. slide 11 – updated by G.872 0.13 2012/08].
  Data plane connection is switched based on an optical spectrum frequency slot of a variable slot width, rather than based on a fixed grid and fixed slot width.
  Wavelength Switched Optical Network (WSON) ~ particular case of SSON in which all slot widths are equal and depend on the used channel spacing.
Flexi-LSP:
[deprecated, will use either media-LSP or signal-LSP (layer)]
  A control plane construct that represents a data plane connection in which the switching involves a frequency slot of a variable (flexible) slot width
RSA: Routing and Spectrum Assignment
SCC: Spectrum Continuity Constraint

## Slide 7: Layered Network model [G.872 0.13 2012/08]
Design consideration: decoupling of the management of the optical spectrum resource and the client signals  Separation of concerns
A flexi-grid network is assumed to be a layered network,
  the OCh Layer (the signal layer) is the client layer
  the flexi-grid layer (the media layer) is the server layer
    switching is based on a frequency slot, which defines the size of a media channel.
    the media channel itself can contain one or more optical signals (OCh-P).
Fig source: Malcolm, Xihua (ZTE) - ITU-T WP3 Q12 interim meeting

## Slide 8: SSON media layer element model
ROADM
A1
A3
A2
D1
D3
D2
DWDM link
DWDM link
Available frequency ranges: the set or union of frequency ranges that are not allocated.
Central frequency granularity: the step granularity of nominal central frequency.
Slot width granularity: the step granularity of slot width.
Slot width range: the minimal and maximal slot width a link supported.
DWDM Links
TX1
TX2
TX3
RX1
RX2
RX3
Available central frequencies: The set of central frequencies which can be used by an optical transmitter/receiver.
Slot width: The slot width needed by a transmitter/receiver.
Transmitters/Receivers

## Slide 9: RSA Models (now refer to the media layer)
Both of the route and frequency slot are determined before the signaling procedure. With Separate RSA, Routing may suggest candidate frequency slot to SA which will allocate final slot assignment from the candidate pool. |  | Only the route is determined before the signaling procedure, frequency slot is allocated by the signaling procedure
In all cases, the computation element(s) could reside on PCE(s) or ingress nodes. |  | 
Combined RSA
Routing
SA
A Single Computation Element
Separated RSA
Routing
SA
Computation Element 1
Computation Element 2
Routing and Distributed SA
Routing
SA
Computation Element
Signaling Procedure

## Slide 10: Open Issues (I): definition of SSON
A SSON (network) refers to the application of GMPLS based control to an ITU-T flexi-grid-enabled DWDM optical network. For the purposes of the framework document, such network encompasses two layers,
  The signal (client) layer  entity is the Optical Channel (OCh)
  The media (server) layer  entity is the media channel
Notes:
  There is a relationship of containment between Optical Signal and Media channels
    a media channel bound to a single OCh-P is named a network media channel
  it is not directly related or implies a MRN/MLN in the scope of GMPLS control
  There is no switching at the signal (OCh) layer, only Frequency Slot switching (Slot matrix)

## Slide 11: Open Issues (Ia):
Q1: Is SSON a SLN / MLN / MRN (for the purposes of GMPLS control)?
  Option A: MRN/MLN
    SSON is still a hierarchical LSP architecture, because we need to setup a OCh connection and the underlying media layer connection.
  Option B: Single Layer Network -establishment of the media channel (flexi-LSP).
    Signal layer (OChs) for the purpose of management and control of individual optical signals. Signal compatibility issues can be addressed as "properties" of media channel (LSP).
    WSON and SSON are at the same layer, which is a single abstraction layer of a multi-layer network (roughly the server one)
    Signal compatibility issues need to be taken into account in routing and signaling, but as parameter of the server layer and not as a client layer  No impairments managed
Note: apparent rough consensus for Option B (consider SSON as a SLN, control media-LSPs)
Q2: Relationship with / interop / interwork with WSON?
  Conditioned by Q1 (!)
  WSON/SSON “stitching” / nesting?
  Different cases for OCh-P (SSFS) and FS a) N:1 b) 1:1
  If SSON is a MRN, will a WSON LSP trigger both layers LSPs setup in SSON, before performing a LSP stitching operation at the OCh layer?

## Slide 12: Open Issues (Ib):
Q3: Hierarchy at the media layer?
  G.872  we cannot have a media channel hierarchy, the media resource is spectrum and spectrum has no structure and hence cannot support a hierarchy.
  From the perspective of a control plane application that "constructs" channels by first building "high bandwidth" channels (connections) in the core and then uses these to support edge to edge channels may create a hierarchy of media LSPs that represent the channels that have been constructed.
    Does this imply some kind of MRN ? high layer media-LSPs that correspond to network-media-channels over a low-layer media-LSP that corresponds to a media-channel, with the former channels slot being (sub)slots of the latter, bigger frequency slot?

## Slide 13: Open Issues (II): Switching capability
Q4: switching capability / switching type?
  Retain LSC ? (as considered in some drafts)
    Potential issues if we keep LSC yet use a different label format?
  New LSC-flexi / LSC-SSON?
    Latest OSPF-TE for WSON draft defines new LSC-WSON
    Note: draft-berger-ccamp-swcaps-update-02.txt: “A different Switching Type value SHOULD be used for each data plane technology even when those technologies share the same type of multiplexing or switching”.
     May need LSC for each layer

## Slide 14: Next Steps for Framework and Requirements
Track ITU-T updates
  [G872] expected to integrate important changes
  Terms are not yet stable / final
  Some assumptions are still at early stages (drafts/contributions)
Improve the hierarchical / layered network model.
Identify / improve control plane requirements to be fulfilled by solutions & protocol-related documents.
Reflect agreements during IETF84.

## Slide 15: Related Work
This draft covers framework and requirements,
However  identified questions that need to be discussed and solved before moving forward:
  Work on flexi-grid started before having a standardized data plane,
  Multiplicity of drafts appeared covering all aspects: framework, routing, signaling…
  Agreements and divergences
Most (all?) of such questions have been mentioned in ccamp@ietf
  Label format / encoding
  Signaling and traffic parameters
  Routing
  PCE work

## Slide 16: GMPLS Label for flexi-grid DWDM networks
Q5: Agree on a label format (what’s in a nam^H^H label?)
    Not only “encoding” but conveyed information
    See ccamp@ietf thread for arguments
  Q5.1. DWDM Grid value?
  Q5.2. Traffic parameters?
    Need a well defined layered network model
    Media layer  should focus on frequency slot parameters?
  Q5.3. Is the "m" field part of the label, the traffic parameters, or both?
    Option I "m" is part of the label, switching resource, ERO using Explicit Label Control; a cross-connect is defined by the tuple (port-in, label-in, port-out, label-out), "best effort LSP“. Slot Matrix Switching  Frequency slot switching
    Option II: "m" is not part of the label but of the TSPEC, needs to be in the TSPEC to decouple client signal traffic specification and management of the optical spectrum, having in both places is redundant and extra error checking.
    Option III: both, It reflects both the concept of resource request allocation / reservation and the concept of being inherent part of the switching.

## Slide 17: Signaling work
Generic requirements can already be identified
  Provisioning
  Recovery
  (subject to constraints from ITU-T, e.g. hitless rerouting not considered)
New requirements need a better (common) understanding of
  Network (layered) model and Terminology
    Assume a MRN and use common MRN procedures?
  Agreement on “switched resource” and “traffic parameters”
    Focus on the media layer

## Slide 18: Routing work
Existing drafts (routing) requirements are converging; identifying requirements to disseminate:
  I) nominal central frequencies availability / status
    Efficient encodings in separate solutions document
  II) transponder / ROADM status and capabilities
    [G.694.1] Applications may be defined where only a subset of the possible slot widths and positions are required to be supported
    Central frequency granularity, Slot width granularity, Slot width range
Note: trend to reuse WSON models for e.g.
  ROADM internal connectivity / constraints,
  Port label restrictions,
Align with switching capability agreement
  Can adapt ISCD / SCSI with new ISCD ? / Deprecate e.g. LSP bandwidth?
    At data rates of GBps / TBps, encoding bandwidths with bytes per second unit and IEEE 32-bit floating may be problematic / non scalable.
    There is not a 1-to-1 mapping between bps and Hz, since it depends on the modulation format, FEC… (modulations and spectral efficiency).

## Slide 19: Path Computation Element work
As per PCE-WG chair mail [1], PCE specific requirements have been put on hold / postponed:
  No special assumptions on the path computation function.
  In any case (source-based, PCE-based,…) the function may:
    Depend on the RSA models
    Consider Frequency Constraints (slot width, available central frequencies)
    Consider signal compatibility constraints,…
  Basic terms remain (commonly accepted?)
    e.g. PCE-based RSA.
  [1] http://www.ietf.org/mail-archive/web/ccamp/current/msg13286.html