## Slide 1: Expressing LSP attribute in ERO
CCAMP WG, IETF 84,
draft-margaria-ccamp-lsp-attribute-ero-01
Cyril Margaria
Nokia Siemens Networks
Dirk Schroetter
iX GmbH
Giovanni Martinelli
Cisco
Steve Balls; Ben Wright
Metaswitch

## Slide 2: Why
Chair said so 
Need to express LSP attributes targeted at specific nodes :
  Routing parameters for loose hops (draft-ali-ccamp-rc-objective-function-metric-bound,etc)
  Node specific parameters (draft-ietf-ccamp-wson-signaling)
  Label Set (draft-margaria-ccamp-label-set-ero)
  Hierarchy parameters (draft-zhang-ccamp-gmpls-h-lsp-mln)
  OAM parameters

## Slide 3: Objective
Objective : Generic mechanism to target any attribute to a specific hop/node

## Slide 4: How
Any Attribute -> LSP_ATTRIBUTE
Specific Hop -> ERO/SERO

## Slide 5: Simple Solution
New ERO subobject containing LSP_ATTRIBUTE TLVs
Simple, easy, not working :
Attribute TLV length field : 16 bit
ERO subobject length field : 8 bit
Drawbacks :
If same attribute is relevant to multiple hops information is repeated
Path
ERO Header
Hop 1
Hop Attribute
Hop 2
Hop Attribute
Hop 3
Hop Attribute
ERO

## Slide 6: Less simple solution
Use “pointers/references” :
ERO contains an index
Indexed LSP Attribute in LSP_ATTRIBUTE
Pro :
size is aligned (minus the index)
Several ERO subobject can point to the same attribute
Cons :
Processing rules are a bit more complex
Path
ERO Header
Hop 1
Hop Attr Index (2)
Hop 2
Hop Attr Index (1)
Hop 3
Hop Attr Index (1)
LSP ATTR Header
Hop Info TLV 1
Hop Info TLV 2
ERO
LSP_ ATTRIBUTE
Notes: Picture shows 3 hops, but referencing only 2 different per hop attributes.

## Slide 7: Other solutions
Replicate the ERO by using targeted lsp attributes:
Not really simplifying the processing rules (merge two objects)
Size is ok.

## Slide 8: Next steps
Consensus on the need for a generic solution
Solution direction
WG adoption?

## Slide 9
Questions?