## Slide 1: WSON Specific WG Drafts
Routing and Wavelength Assignment Information Encoding for Wavelength Switched Optical Networks (v14)
GMPLS OSPF Enhancement for Signal and Network Element Compatibility for Wavelength Switched Optical Networks (v09)

## Slide 2: Authors/Contributors
Greg Bernstein (Grotto Networking)
Diego Caviglia (Ericsson)
Ander Gavler (Acreo AB)
Jianrui (Rebecca) Han (Huawei)
Young Lee (Huawei)
Dan Li (Huawei)
Wataru Imajuku (NTT)
Jonas Martensson (Acreo AB)
Itaru Nishioka (NEC Corp.)
Pierre Peloso (ALU)
Cyril Margaria (NSN)
Rao Rajan (Infinera)
Plus a whole lot of folks on the CCAMP list and at the last five years of meetings.

## Slide 3: draft-ietf-ccamp-rwa-wson-encode-14.txt
Changes from 12 draft
  Replaced all instances of "ingress" with "input" and all instances of "egress" with "output".
Changes from 13 draft
  C bit of Resource Block Set Field is redundant and was removed, i.e., has been returned to “Reserved” block and appendix examples were updated to reflect the change.
  Enhanced section 4.2 encoding to allow for optionality of input or output wavelength set fields.
  Clarified that wavelength set fields use the Label Set field encoding from [Gen-Encode].
  Enhanced section 5.1 encoding to simplify the Modulation and FEC input and output cases.
Last Changed 2012-04-24

## Slide 4: draft-ietf-ccamp-rwa-wson-encode-14.txt
One outstanding CCAMP list item
  Sub-field associated with “Optical Interface Concept”
  Decisions comes down to whether we add a new sub-sub-TLV and/or remove some existing sub-sub-TLVs
  Whatever the WG decides here we will implement
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Set Field |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|I|E| Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Modulation Type List Sub-Sub-TLV (opt) |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| FEC Type List Sub-Sub-TLV (opt) |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Input Client Signal Type Sub-Sub-TLV (opt) |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Input Bit Rate Range List Sub-Sub-TLV (opt) |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Processing Capabilities List Sub-Sub-TLV (opt) |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 5: draft-ietf-ccamp-wson-signal-compatibility-ospf-08.txt
Change from 07-08: Added ISCD extensions for available labels and shared backup labels.
  Change made per request & WG email discussion
  Modeled changes on ISCD extensions in draft-ietf-ccamp-gmpls-ospf-g709v3-02
  New switching capability value:
Value Type
----- ----
151 (TBA by IANA) WSON-LSC capable (WSON-LSC)
Switching Capability and Encoding values MUST be used as follows:
Switching Capability = WSON-LSC
Encoding Type = Lambda [as defined in RFC3471]

## Slide 6: draft-ietf-ccamp-wson-signal-compatibility-ospf-08.txt
Switch Capability Specific Information (SCSI)
  Available Labels
  Shared Backup Labels
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = 1 (Available) | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| Available Label Sub-TLV |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ... ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = 2 (Shared backup) | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| Shared Backup Label Sub-TLV |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 7: Next Steps
Except for the resolution on OIC, there is no pending issue for both WSON-Encode and OPSF-TE.
After resolution of OIC, Ready for WG LC?