## Slide 1: Applicability Statement for Layer 1 Virtual Private Network (L1VPN) Enhanced Mode
draft-belotti-app-statement-l1vpn-em-00
Sergio Bellotti Sergio.Belotti@alcatel-lucent.com
Don Fedyk Donald.Fedyk@alcatel-lucent.com
Dimitri Papadimitriou Dimitri.Papadimitriou@alcatel-lucent.com
IETF 84 – CCAMP WG

## Slide 2: Acknowledgements
Based on expired draft-ietf-l1vpn-applicability-enhanced-mode-00.txt
  Tomonori Takeda, Hamid Ould-Brahim, Adrian Farrel, Deborah Brungard, Dimitri Papadimitriou

## Slide 3: Agenda
Why Enhanced L1VPNs ?
Enhanced Mode Models
  Extended Overlay Model
  Virtual Node Model
  Virtual Link Service Model
  Peer VPN Service Model
Signaling extensions
Summary
Initial Focus

## Slide 4: Why Enhanced L1VPNs?
A standard UNI interface between customer and provider networks with minimal dependencies.
L1VPN Enhanced mode goes beyond basic mode for additional capabilities such as diversity and delay etc.
Extensions beyond Basic Mode

## Slide 5: L1VPN Overlay Network Models (Review from IETF 67)
Virtual
link
Meshed Provider Network
UNI
PE1
CE1
UNI
PE2
CE2
P
P
C
C
CE
CE
Virtual Node
C
C
CE
CE
CE
CE
C
C
PE
PE
CE
CE
C
C
PE
PE
P
P
Overlay Extension Service Model
Virtual Link Service Model
  Virtual Node Service Model
Peer VPN Service Model

## Slide 6: Extended Overlay Model
A CE receives from its UNI attached PEs a list of TE link addresses to which it can request a VPN connection (i.e., membership information).
The CE does not receive any of the following from the PE:
  Routing information about the core provider network.
  Information about P device addresses.
  Information about P-P, PE-P or PE-PE TE links.
  Routing information about other customer sites.

## Slide 7: Virtual Node Service Model
Private routing exchange between the CE routing protocol instance and the VPN routing protocol instance running on the PE.
The provider network is considered as one private node from the customer's perspective.
Signaling mechanisms such as RFC 5251 and Auto discovery such as RFC 5252/RFC5195.

## Slide 8: Virtual Link Service Model
Virtual links are established between PEs.
A virtual link is assigned to each VPN and disclosed to the corresponding CEs.
The routing information exchanged between the CE and the PE includes:
  CE-PE TE links,
  virtual links
  may include CE-CE (or C-C) Forwarding Adjacencies as well as Customer control plane topology from the customer network (i.e., CE sites).

## Slide 9: Per-VPN Peer Service Model
The provider partitions TE links within the provider network per VPN.
The routing information exchanged between the CE and the PE includes:
  CE-PE TE links,
  partitioned portions of the provider network,
  may include CE-CE (or C-C) Forwarding Adjacencies and control plane topology from customer network (i.e., CE sites).

## Slide 10: Extensions Drafts
Signaling drafts applicable to models.
    draft-fedyk-ccamp-l1vpn-extnd-overlay
    draft-ali-ccamp-rc-objective-function-metric-bound,
    draft-ali-ccamp-te-metric-recording
    draft-zhang-ccamp-srlg-fa-configuration.
These drafts can be also be applied L1VPN models consistent with reducing dependency.
  Initial Enhanced mode focus is on:
  Extended Overlay Model

## Slide 11: Next Steps
Progress the drafts for L1VPNs Extended modes.
Solicit feedback/support/comments from the group

## Slide 12
Thank You!