## Slide 1: Optical Interface Class draft-martinelli-wson-interface-class-03
Authors:
Giovanni Martinelli (Cisco)
Gabriele Galimberti (Cisco)
Lyndon Ong (Ciena)
Daniele Ceccarelli (Ericsson)
Cyril Margaria (Nokia Siemens Network)

## Slide 2: The problem: Signal Compatibility
Originally stated in RFC6163, mentioned draft-ietf-ccamp-rwa-info, draft-ietf-ccamp-rwa-wson-encode and draft-ietf-ccamp-wson-signal-compatibility-ospf.
Currently solved through three parameters (FEC, Modulation Format, Bit rate) each with a range of predefined values, plus vendor specific encoding.
Proposal: use a unique, fixed size field instead.

## Slide 3: OIC vs ITU application Code
Application Code is *one* instance of the optical interface class (but one that is standardized).
ITU application code has a straightforward mapping on OIC.
OIC may eventually carry classes defined by other std bodies (currently only ITU or vendor specific).

## Slide 4: Some Questions
Does Application Code suffice for Signal Compatibility (see G.959.1 sec 6)?
  If two interfaces support the same application code: YES.
  If two interfaces do NOT support the same application code: TBD
Worth clarify semantic and usage through usual ccamp-itu liaison?

## Slide 5: Draft Updates 02->03:
Some editing around examples and vendor specific part.
Added code point for G.959.1 application code.
  No application codes are *NOT* only for G.698.[12]
Added Appendix for mapping Application Code within Optical Interface Class
  Initial proposed coding, pls provide comments

## Slide 6: Comments?
Thank you!