## Slide 1: Multi layer implications in GMPLS controlled networks draft-bcg-ccamp-gmpls-ml-implications-01
D. Ceccarelli, Ed., F. Fondelli (Ericsson)
S. Belotti, D. Papadimitriou, Ed. (Alcatel-Lucent)

## Slide 2: Motivations
Functional motivations
On the fly multi-layer traffic grooming
Hybrid packet (switching and regeneration pool) optical switches
Devices exposing capabilities of hybrid interfaces connected to an "opaque" matrix
Performance motivations (tradeoffs)
Too few routing info => crankback or resource misuse
Too much routing info (and signaled info) => crankback too (blocking resulting from dynamics)
blocking prob.
#info unit

## Slide 3: Adjustment pool
Adjustment pool: pool of reservable and sharable resources
  Allocated on demand/dynamically (for "intra-node" capability interconnection/relationship)
  Either assigned to a single SC (single adjustment pool model) or multiple SC (multiple adjustment pool model) or possibly their combination
-> Two models
  Single pool model
  Multiple pool model

## Slide 4: Single Pool Model
As part of OTH TE Link_1...N advertisement
ISCD sub_TLV 1 for OTH
IACD sub_TLV 1 for OTH to HO-SDH
Fiber 1
Fiber N
OTH
HO-SDH
L2SC
Fiber 1
Fiber N
L2SC
...
OTH
As part of L2SC TE Link_1..N advertisement
ISCD sub_TLV 1 for L2SC
IACD sub_TLV 1 for L2SC to HO-SDH
TE Link_1..N
Lower SC value of IACD sub-TLV: set to SC value of ISCD sub-TLV associated to the interface getting access to adjustment pool
Upper SC value of IACD sub-TLV: set to SC capability of adjustment resource pool itself
LSP (upper) encoding set to 0xFF
=> Model typically used when node exposes only capability associated to its I/O (nodes in same TE domain can still take into account adjustment capacity usage on that node)
Capacity associated to IACD  interconnection capacity between interface X (L2SC or OTH) to Y = (HO-SDH/TDM)

## Slide 5: Multiple pool model
Lower SC value of IACD sub-TLV: set to SC value of ISCD sub-TLV of the interface(s) that gets access to the adjustment pool
Upper SC value of IACD sub-TLV: set to SC capability of adjustment pool itself where The "upper SC" value corresponds to at least one of the SC value associated to ISCD sub-TLVs
Fiber 1
Fiber N
OTH
HO-SDH
L2SC
Fiber 1
Fiber N
As part of TE Link_1 advertisement ( Fiber 1)
IACD sub_TLV 1 for L2SC to HO-SDH
ISCD sub_TLV 1 for L2SC
ISCD sub_TLV 2 for HO-SDH
ISCD sub_TLV 3 for OTH
...
As part of TE Link_N advertisement ( Fiber N)
ISCD sub_TLV 1 for L2SC
ISCD sub_TLV 2 for HO-SDH
ISCD sub_TLV 3 for OTH
IACD sub_TLV 1 for L2SC to HO-SDH
Capacity associated to IACD  interconnection capacity between pool HO-SDH/TDM and pool L2SC (accessed by)

## Slide 6: Multiple pool model
As part of TE Link_1 advertisement ( Fiber 1)
ISCD sub_TLV 1 for L2SC
ISCD sub_TLV 2 for HO-SDH
ISCD sub_TLV 3 for OTH
IACD sub_TLV 1 for L2SC to HO-SDH
IACD sub_TLV 2 for HO-SDH to OTH
...
As part of TE Link_N advertisement ( Fiber N)
ISCD sub_TLV 1 for L2SC
ISCD sub_TLV 2 for HO-SDH
ISCD sub_TLV 3 for OTH
IACD sub_TLV 1 for L2SC to HO-SDH
IACD sub_TLV 2 for HO-SDH to OTH
Fiber 1
Fiber N
OTH
HO-SDH
L2SC
Fiber 1
Fiber N
Capacity associated to IACD sub-TLV 1  interconnection capacity between pool HO-SDH/TDM and L2SC (accessed by)
Capacity associated to IACD sub-TLV 2  interconnection capacity between pool HO-SDH/TDM and OTH (accessed by)

## Slide 7: Additional Requirements: Example
ODU2/TDM
ODU1/TDM
ODU3/TDM
The relationship between IACD have to be maintained and advertized
Four different type of C/S scenarios :
  Signal type X to Signal type Y (1:1)
  Example: Ethernet over OCh
  Signal type X to Intra switching technology Hierarchy Y (1:N) –
  Example: Ethernet over ODU
  Intra-switching technology Hierarchy X to Signal Type Y (M:1)
  Example: ODU over OCh
  Intra-switching technology Hierarchy X to Intra switching technology Hierarchy Y (M:N)
  Example: SDH over ODU

## Slide 8: Additional Requirements: Example
Single pool: ODU/TDM
The inner structure of the pool remains hidden
Four different type of C/S scenarios :
  Signal type X to Signal type Y (1:1)
  Example: Ethernet over OCh
  Signal type X to Intra switching technology Hierarchy Y (1:N) –
  Example: Ethernet over ODU
  Intra-switching technology Hierarchy X to Signal Type Y (M:1)
  Example: ODU over OCh
  Intra-switching technology Hierarchy X to Intra switching technology Hierarchy Y (M:N)
  Example: SDH over ODU

## Slide 9: Check list
1. Capability to identify from which branch of X to which branch of Y the mapping is performed
2. Adaptation information (e.g., type) from X to Y to be used in case of i) X mapped over Y and Y being switched or ii) both X and Y being switched
3. Available bandwidth in the mapping between X and Y (as per actual IACD definition)
4. Capability to advertise intra-switching capability associated to internal interconnections
5. Capability to advertise inter-switching capability associated to internal interconnections

## Slide 10: Next steps
Verify WG interest in the work (progress this doc as analysis against req. document)
Extend the scope from just inter-switching capability MLNs to intra-switching capability MLNs
Start working on processing and format/encoding (separate doc.)