## Slide 1: Revised Definition of The GMPLS Switching Capability and Type Fields draft-berger-ccamp-swcaps-update-02
Lou Berger lberger@labn.net
Julien Meuric julien.meuric@orange.com

## Slide 2: Changes
-swcaps-update-00
  Presented at last IETF
-swcaps-update-01
  Included presented planned changes
    Rename: ILH  ITH
      Intra-Layer Hierarchy  Intra-Technology Hierarchy
-swcaps-update-02
  Removed ITH
    ITH specific not as mature as rest of draft

## Slide 3: Current Draft Scope
Simplifies definition of Switching Capability
  Only indicates switching technology
    Removes existing overload – no intra-technology significance
  Different SCSI formats MUST use different values
    Removes existing SCSI format ambiguity
Deprecate intra-layer / unused PSC values
  PSC 24
Keep values used in routing and signaling aligned
  No change: keep using IANA Switching Type registry
No substantive change for signaling
Matches discussion on list and last meeting
  Aligned with current OTN drafts

## Slide 4: Considered Alternatives
Goal: Address two issues for future definitions
  (i.e., no impact to existing RFC-based implementations, apart from PSC-N that appear to be unused)
  Current representation of (1) switching types, (2) technologies, and (3) multiplexing is inconsistent
  Current definition of Switching Capability (and types) is overloaded
Alternatives considered – two extremes:
  Assign Switching Type per potential SCSI format
    i.e., at least one Switching Type per switching technology
    different SC specific information field formats imply different Types
  Have Switching Type represent (1), (2) and (3)
    i.e., for a given technology, as many Types as multiplexing levels (ala PSC-N)
Selected Approach

## Slide 5: Next steps
Poll to be WG document