## Slide 1: CLUE RTP usage
Andy Pepperell
andy.pepperell@silverflare.com

## Slide 2: Problem statement
CLUE consumers need to receive multiple RTP streams for decoding
  Might be left + center + right camera and associated audio
  Might be 16 loudest speaker streams for composition into 4 x 4 grid
  More generally, could be any combination of streams being forwarded from other providers via a middle box (e.g. an MCU)

## Slide 3: Simple case
Single audio, single video
Provider
Consumer
AC1
VC1

## Slide 4: Complex case
MCU
Remote providers
Remote consumer
VC1
VC2
VC3

## Slide 5: Possible solutions
Extra information in SDP for multi-stream
  Pre-declaration of sender SSRC values
Extra information in CLUE and RTP
  draft-lennox-clue-rtp-usage-04
  Solution to be presented here

## Slide 6: RTP sessions
Number of capture encodings from provider to consumer may be large
  Sufficiently large to need multiple RTP streams per RTP session / “m line”
  General agreement that multiple RTP streams need to be sent within single “m line”
  Many existing (Telepresence) endpoints already send multiple streams within a single RTP session

## Slide 7: Proposal
Additional ID in RTP streams of capture encodings
  IDs chosen by consumer when it makes stream selection
  IDs transported in RTP header extensions
    SSRC and other header fields unaltered for forwarded streams
    Multiple IDs possible for solving complex cases

## Slide 8: RTP header extension usage
MCU
Remote providers’ media
Remote consumer
VC1
. . .
. . .
. . .
. . .
. . .
. . .
MCU middle box changes which stream to forward, but does not change new CLUE RTP header extension contents

## Slide 9: Advantages
Scales well to complex cases
No impact on SDP, only later CLUE phase
  No need to declare SSRC values in advance
RTP header fields can be forwarded from source
  RTCP behavior simplified
  Consumer acts in standard way on SSRC change within a capture encoding
Keeps CLUE concepts in CLUE

## Slide 10: Disadvantages of fixed SSRCs
Does not scale well to complex cases
  Impact on SDP (and thus compatibility)
RTCP implications
  Handling of BYEs, SDES
Other SSRC-centric issues
  SRTP rollover counters

## Slide 11: Draft updates
Forthcoming changes to draft-lennox-clue-rtp-usage-04:
  Use of new consumer-chosen ID in extension header
  More detail on encryption