## Slide 1
Roni Even
Jonathan Lennox
Mapping RTP streams to CLUE media captures
draft-even-clue-rtp-mapping-03
IETF-84

## Slide 2: Introduction
CLUE framework
  Defines Media Captures that provide information about the semantics of streams, like spatial relation
  Allows consumers to request specific Captures
RTP is used to transmit the requested streams
SDP is used to negotiate the characteristics of codecs and connections over which streams are sent
Need to map between media captures and actual streams sent over RTP
Try to avoid duplication of information between SDP and CLUE
<number>
Notes: <number>

## Slide 3: Assumptions
CLUE systems support different topologies
  Point to point
    Sender source is one to one mapped to RTP streams
  Media mixers
    Senders’ sources are visible as Contributing sources (CSRCs).
  Media switching mixers
    Sender’s source is visible as a Contributing source (CSRC).
  Source projection mixers
    Each media source is one to one mapped to a SSRC in Participant’s RTP session.
<number>

## Slide 4: RTP/RTCP behavior
Topologies show two major behaviors:
    Mixer either uses source SSRC or uses its own SSRC when forwarding RTP packets.
      One RTP session and source information is in SSRC or CSRC.
    Mixer terminates RTCP from source, creating separate RTP sessions with peers.
      The source information is not available in RTCP but may be available using out of band means, e.g. SIP conference event package (RFC4575).
<number>
Notes: <number>

## Slide 5: SSRC behavior
Topologies show two major SSRC behaviors:
    Static SSRCs
      SSRCs assigned by MCU/mixer.
      A static SSRC can be used for each CLUE media Capture.
      Source information may be conveyed in CSRC.
    Dynamic SSRCs
      SSRCs of the original source relayed by the Mixer/MCU to participants.
      Mapping between SSRCs and Media Captures changes with every source switch.
<number>

## Slide 6: Examples
  Video switching MCU
    Media Mixer behavior for audio.
    Media switching Mixer or a Source-Projection Mixer for video.
    The audio will be static source, whereas the video could be dynamic.
  Endpoint may send the same sources both for static and dynamic captures.
    Endpoint can provide both three cameras (VC0, VC1, and VC2) for left, center, and right views, as well as a switched view (VC3) of the loudest panel.
    Using Source-Projection Mixer topology for VC3
    VC0, VC1, VC2 have static mapping.
<number>

## Slide 7: Mapping options (1)
Advertisements are created by the next peer
  MCU / Mixer in multipoint
  TP endpoint in point to point call
Use a “capture ID” SDP source attribute.
  For each SSRC and media capture. This is a static mapping.
Use RTP Header extension as in draft-lennox-rtp-usage-04
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ID=1 | length=4 | Capture ID :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
<number>

## Slide 8: Mapping options (2)
RTP header extension sent with every packet (or with selected packets) of a dynamic mapped RTP stream.
  The RTP header extension is provided by the source for point to point calls and by the middle box in Multipoint case.
The same Capture-ID value can be used when using static mapping in SDP and for dynamic mapping in the RTP header extension.
<number>

## Slide 9: Proposal
Media mixers and Media Switching mixers are common in products
Source projection mixers are also used in products.
  Allow more flexibility for switched captures
Products may have mixed behavior for static and dynamic SSRC support
Mapping static SSRCs to CLUE Media Captures - adding the RTP header extension for each packet is not necessary.
Endpoints MUST support, as receivers, both the static declaration of capture encoding SSRCs, and the RTP header extension method of sharing capture IDs, with the extension in every media packet.
An RFC3264 offer can specify a static mapping to a CaptureID for a given SSRC and later an RTP header extension can use the same CaptureID for a different SSRC. This will be a media switch for the specified CLUE media Capture.
<number>