## Slide 1: draft-romanow-clue-call-flow-02
Allyn Romanow
Rob Hansen
Arun Krishna

## Slide 2: Call Flow overview
Alice
Bob
SIP: INVITE
SIP: ACK
SIP: 200 OK
(optional) Single-stream media
CLUE: Advertisement
CLUE: Configure
Multi-stream media
Negotiate CLUE channel
CLUE: Advertisment
CLUE: Configure

## Slide 3: Illustrative Transport: SCTP (over DTLS) over UDP
Reliable, in-order delivery
Can follow the same path as RTP
  Can use ICE
Can be encrypted/authenticated with DTLS
  May wish to make this mandatory (null cipher for unencrypted)
Negotiated in SDP

## Slide 4: SDP
Implementations may advertise one m-line per media type, or multiple if desired.
Audio and video remain on separate m-lines
SDP negotiates RTP session and codec limits
  CLUE does not replace SDP; all media MUST remain within these limits

## Slide 5: CLUE in SIP/SDP
INVITE sip:bob@example.com SIP/2.0
Supported: clue
...
v=0
o=alice 2890844526 2890844526 IN IP4 client.atlanta.example.com
s=-
c=IN IP4 192.0.2.101
a=fingerprint: SHA-1 4B:AC:B7...
a=extmap:1 urn:ietf:params:clue:mux
t=0 0
b=AS:6064
m=audio 49172 RTP/AVP 0
...
m=video 49174 RTP/AVP 96
...
m=application 49176 UDP/DTLS/SCTP/CLUE *
a=setup:actpass
a=connection:new

## Slide 6: Post-SIP behaviour
CLUE-specific SDP parameters will be ignored by non-CLUE devices
  Will result in a conventional single-stream call
Before CLUE is negotiated:
  MUST be ready to receive single-stream media
  MAY(SHOULD?) send single-stream media

## Slide 7: CLUE Messages
A call is made up of two independent, unidirectional CLUE negotiations
Additional advertisement/configure messages may be sent at any point
  Messages to include sequence numbers to identify the advertisement a configure message is referring to.
XML encoding for messages

## Slide 8: SCTP channel re-establishment and CLUE state
Mid-call re-establishment of SCTP channel triggered by SDP may mean far end has no knowledge of previous state
Hence on re-establishment CLUE MUST be renegotiated
  Endpoints on hold should not deactivate the CLUE channel to avoid renegotiation.

## Slide 9: SIP/CLUE mid-call interaction
CLUE advertisements may also trigger SIP reINVITEs to make SDP changes
Alice
Bob
SIP: INVITE (4M)
SIP: ACK
SIP: 200 OK

## Slide 10: SIP/CLUE mid-call interaction
CLUE advertisements may also trigger SIP reINVITEs (eg, to alter bandwidth)
Alice
Bob
SIP: INVITE (4M)
SIP: ACK
SIP: 200 OK
CLUE: Advertisement (3 1080p screens)

## Slide 11: SIP/CLUE mid-call interaction
CLUE advertisements may also trigger SIP reINVITEs (eg, to alter bandwidth)
Alice
Bob
SIP: INVITE (4M)
SIP: ACK
SIP: 200 OK
CLUE: Advertisement (3 1080p screens)
SIP: INVITE (12M)
SIP: ACK
SIP: 200 OK
CLUE: Configure (3 1080p screens)

## Slide 12: RTP multiplexing
Consensus not yet reached on method
  draft-lennox-clue-rtp-usage-04
  draft-even-clue-rtp-mapping-03
Demultiplex by SSRC or RTP extension header
  Format for RTP extension header:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ID=1 | L=3 | capture id |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| capture id |
+-+-+-+-+-+-+-+-+

## Slide 13: Questions