## Slide 1: Diameter Overload Control Justification and Use Cases
Martin Dolly
AT&T Labs

## Slide 2: Reason for Overload (Use Cases)
Inadequate capacity
Network element failures resulting in failover
Registration storms
Aggressive mobile devices (i.e., smart phones)
Correlated network failures and/or events
Uncorrelated network failures and/or events
Congestion causing message loss in other NEs
Denial of Service attacks

## Slide 3: Impacts of Overload (Justification)
Diameter interface is defined for signalling between many core network nodes and services. Overload on these interfaces can lead to server congestion or even collapse. The impact to services can be:
  Denial of services, persistent access restriction,
  loss of IMS and broadband services,
  Loss of location information for emergency services and lawful intercept,
  Loss of ability to use policy control to provide service personalization,
  Loss of ability to use policy control to optimize network resources,
  Billing errors and loss of revenue.
An analysis table for these interfaces and service impact is shown in in the following slides.
Source: 3GPP S2-122906

## Slide 4
Core Network nodes | Defined interface | Services | overload impact
PCRF –PCEF/TDF | Gx, Sd | Policy control and DPI | Denial of services, loss of policy control for service personalization and network optimization, billing errors and revenue loss
PCRF/PCEF/AS/MRFC—OCS/OFCS | Sy, Gy/Ro, Ro, Gz | Online/offline charging, service authorization, policy control, charging information reporting | Denial of some services, billing errors and loss of revenue
PCRF—AF, P-CSCF | Rx | application and IMS services | Denial of IMS services
PCRF—UDC/SPR/HSS | Sp/Ud |  | Improper policy management, connection and service impact, network management impact,
HPCRF--VPCRF | S9 | Roaming authentication/authorization | Loss of roaming service
CDF/CGF—MRFC/MGCF/AS/SCC-AS/I-/S-CSCF, etc | Rf | Offline charging, | 
HSS/UDC—MME/SGSN | S6a, SLg, S6d | Mobility management, registration, authentication and location services | Denial of Services, signalling storms leading to congestion collapse, and persistent inability to access the network,
HSS/UDC—GMLC/MME | SLg, SLh | UE location reporting | Unable to provide location information to core/IMS network, including emergency services, lawful interception and location services.
HSS/UDC—I-/S-CSCF | Cx/Dx | UE IMS registration, authentication, and domain management | Denial of IMS services, signalling storm leads to congestion collapse, reselection from LTE to 2/3G,
HSS/UDC—SCC-AS/AS | Sh/Dh | IMS services delivery | Denial of or unpredictable behavior of certain services (e.g., voice call routed to voicemail, delayed messaging…)
HSS/UDC—BSF | Zh | Bootstrapping Server Function | 
Note 1: Reference: TS 23.203, TS 32.240,
Note 2: If a DRA (Diameter Routing Agent) is deployed, it relays these interfaces between functional nodes to HSS/SPR/UDC and/or PCRF.
Source: 3GPP S2-122906

## Slide 5
3GPP Diameter Interfaces