## Slide 1: Diameter Group Signaling
Tuesday, July 31st , 2012
draft-ietf-diameter-group-signaling-00
Mark Jones, Marco Liebsch
IETF 84
Vancouver, Canada

## Slide 2: Motivations
Reduce signaling in those use cases that require many Diameter sessions to be modified or terminated at the same time
Add group signaling to existing Diameter applications with minimal impact and ambiguity
Describe the problem space in an application neutral fashion (best practices?) to aid other SDOs in tackling this problem

## Slide 3: Two Problem Aspects
Managing group assignments
  How to add or remove sessions from groups
  Guidelines for modifying group assignments
Manipulating groups of sessions
  Defines new formatting of commands for group operations
  Defines rules how group operations can be applied to session state machines

## Slide 4: Document history & work item status
draft-jones-dime-group-signaling adopted as WG draft after IETF83
draft-ietf-dime-group-signaling-00 published in June 2012
Discussion and evaluation of formatting options
Next: Progress draft towards stable state

## Slide 5: Managing Group Assignments
In the current version of the draft:
  Either Diameter peer may assign a session to a group
  Mid-session modification of group assignments are allowed
  A Diameter peer may remove the group(s) assigned to the active session by its peer

## Slide 6: Manipulating Groups of Sessions
Current version of the draft defines new group command equivalents for the group actions
Alternative approaches have been discussed:
  Single Bulk-Operation command, used as container for existing commands
  Re-use of existing commands and their format
Proposals have been evaluated and assessed
Progress and update draft-ietf-dime-group-signaling to reflect selected format

## Slide 7: DEDICATED GROUP COMMANDS

## Slide 8: Dedicated Group Commands: Overview
Working Assumptions:
  Group commands will not contain the same AVPs as their non-group equivalents, e.g. no Session-ID or User-Name
  ABNF is a valuable specification tool for describing commands
  Application and Command Identifiers are NOT scarce resources
New commands are defined each group operation
  e.g. Group-RAR/RAA, Group-STR/STA, Group-ASR/ASA
When grafting group functions onto existing Diameter applications, these new commands will trigger the need for a new Application-Id

## Slide 9: Dedicated Group Commands: Command Header Example
For example, a new NASREQ-based application that requires group functions for RAR and ASR operations
G-RAR Command Header:
  Command flags: Same as RAR command
  Command Code: NEW G-RAR code
  Application-Id: NEW Grouped-NASREQ
G-ASR Command Header:
  Command flags: Same as ASR command
  Command Code: NEW G-ASR code
  Application-Id: NEW Grouped-NASREQ

## Slide 10: Dedicated Group Commands: G-RAR Command ABNF
<GRAR> ::= < Diameter Header: TBD, REQ, PXY >
* { Session-Group-Id }
{ Origin-Host }
{ Origin-Realm }
{ Destination-Realm }
{ Destination-Host }
{ Re-Auth-Request-Type }
[ Origin-State-Id ]
* [ Proxy-Info ]
* [ Route-Record ]
[ Session-Group-Action ]
* [ AVP ]
One or more Group IDs
RAR AVPs which are NOT session-specific
Required re-auth action (see draft)

## Slide 11: Dedicated Group Commands: G-ASR Command ABNF
<GASR> ::= < Diameter Header: TBD, REQ, PXY >
* { Session-Group-Id }
{ Origin-Host }
{ Origin-Realm }
{ Destination-Realm }
{ Destination-Host }
[ Origin-State-Id ]
* [ Proxy-Info ]
* [ Route-Record ]
[ Session-Group-Action ]
* [ AVP ]
One or more Group IDs
ASR AVPs which are NOT session-specific
Required STR action (see draft)

## Slide 12: BULK OPERATION COMMAND

## Slide 13: Bulk operation command principle
Single Diameter command for bulk operations
Objective: apply to existing Diameter commands which handle single sessions
Key command is <BULK-OPERATION>
  Command code of the command, which is to be applied to a group of sessions (e.g. RAR, ASR), is encoded inside the Bulk Operation message header
  Mandatory AVPs of the embedded command and required AVPs, which are common to all sessions in the group, are carried in the body of the Bulk Operation message
Application has space for more commands, e.g. for dynamic treatment of groups
  Add/remove sessions from group independent of AAR/AAA, RAR/RAA exchange

## Slide 14: Bulk operation command ABNF
< Bulk-Operation > ::= < Diameter Header: ###, REQ, PXY,
Bulk-Application-ID >
< Command-Id >
{ Group-Id }
{ Command-Application-Id }
* { Carried-Command-Required-AVP }
* [ Carried-Command-Optional-AVP ]
* [ AVP ]
Command-Id: command code of the bulk-executed Diameter message, e.g. RAR, ASR
Command flags: R: According to operation (e.g. RAR, RAA)
P: According to capability of the proxy to handle bulk operations
Group-Id: Group identifier, must be present
Bulk command main header
Group identification
Carried command message body
Attributes which apply to the group

## Slide 15: Example: NAS, group re-authentication
< Bulk-Operation > ::= < Diameter Header: ###, REQ, PXY >
< 258 >
{ 1020 }
{ Session-Id }
{ Origin-Host }
{ Origin-Realm }
{ Destination-Realm }
{ Destination-Host }
{ Auth-Application-Id }
{ Re-Auth-Request-Type }
* [ AVP ]
RAR command code
Group ID
Required attributes from RAR message body
Bulk operation message for RAR:
Attributes which apply to each member of the group
Notes: <number>

## Slide 16: Example: NAS, group re-authentication
< Bulk-Operation > ::= < Diameter Header: ###, PXY >
< 258 >
{ 1020 }
{ Session-Id }
{ Origin-Host }
{ Origin-Realm }
{ Destination-Realm }
{ Destination-Host }
{ Auth-Application-Id }
{ Re-Auth-Request-Type }
* [ AVP ]
Bulk operation message for RAA:
RAR command code
Group ID
Required attributes from RAR message body
Attributes which apply to each member of the group

## Slide 17: ASSESSMENT OF FORMAT OPTIONS

## Slide 18: Snapshot of formatting discussion
New group command codes and application
  + Straight forward approach
  + low level of ambiguity
  – new command codes and formats* needed for all bulk-enabled commands
  – Proxy needs to be aware of the new application
Single new bulk operation command, indicate command to be executed in a separate command ID field of the message
  + ‘one-for-all’ approach, no new formats and command codes needed for bulk operations
  – Session-ID AVP needs to be ignored or used to carry group ID
  – Proxy needs to be aware of the new application
  – Potential issue with mandatory attributes in the body when they apply to a single session
* may be advantageous..

## Slide 19: Next Steps
Solicit further input to formatting discussion and design requirements
Converge on solution now
Update draft in Aug 2012 to reflect the selected formatting