## Slide 1: DMM Requirements draft-ietf-dmm-requirements
H. Anthony Chan, h.a.chan@ieee.org
Dapeng Liu, liudapeng@chinamobile.com
Pierrick Seite, pierrick.seite@orange-ftgroup.com
Hidetoshi Yokota, yokota@kddilabs.jp
Charles E. Perkins, charliep@computer.org
Jouni Korhonen, jouni.korhonen@nsn.com
Melia Telemaco, telemaco.melia@alcatel-lucent.com
Elena Demaria, elena.demaria@telecomitalia.it
Jong-Hyouk Lee, jh.lee@telecom-bretagne.eu
Tricci So, tso@zteusa.com
Carlos J. Bernardos, cjbc@it.uc3m.es
Peter McCann, PeterMcCann@huawei.com
Seok Joo Koh, sjkoh@knu.ac.kr
Wen Luo, luo.wen@zte.com.cn
Marco Liebsch, liebsch@neclab.eu
Carl Williams, carlw@mcsr-labs.org

## Slide 2: REQ1: Distributed deployment
IP mobility, network access and routing solutions provided by DMM MUST enable a distributed deployment of mobility management of IP sessions so that the traffic can be routed in an optimal manner without traversing centrally deployed mobility anchors.
Motivation: The motivations of this requirement are to match mobility deployment with current trend in network evolution: more cost and resource effective to cache and distribute contents when combining distributed anchors with caching systems (e.g., CDN); improve scalability; avoid single point of failure; mitigate threats being focused on a centrally deployed anchor, e.g., home agent and local mobility anchor.

## Slide 3: REQ1 addresses following problems
PS1: Non-optimal routes – Routing via a centralized anchor often results in a longer route, and the problem is especially manifested when accessing a local or cache server of a Content Delivery Network (CDN).
PS2: Non-optimality in Evolved Network Architecture – The centralized mobility management can become non-optimal as a network architecture evolves and becomes more flattened.
PS3: Low scalability of centralized route and mobility context maintenance – Setting up such special routes and maintaining the mobility context for each MN is more difficult to scale in a centralized design with a large number of MNs. Distributing the route maintenance function and the mobility context maintenance function among different networks can be more scalable.
PS4: Single point of failure and attack – Centralized anchoring may be more vulnerable to single point of failure and attack than a distributed system.

## Slide 4: REQ2: Transparency to Upper Layers when needed
The DMM solutions MUST provide transparency above the IP layer when needed. Such transparency is needed, when the mobile hosts or entire mobile networks [RFC3963] change their point of attachment to the Internet, for the application flows that cannot cope with a change of IP address. Otherwise the support to maintain a stable home IP address or prefix during handover may be declined.
Motivation: The motivation of this requirement is to enable more efficient use of network resources and more efficient routing by not maintaining a stable home IP address when there is no such need.

## Slide 5: REQ2 addresses following problems
PS5: Wasting resources to provide mobility support to nodes not needing such support – IP mobility support is not always required. For example, some applications do not need a stable IP address during handover, i.e., IP session continuity. Sometimes, the entire application session runs while the terminal does not change the point of attachment. In these situations that do not require IP mobility support, network resources are wasted when mobility context is set up.
O-PS1: Mobility signaling overhead with peer-to-peer communication – Wasting resources when mobility signaling (e.g., maintenance of the tunnel, keep alive, etc.) is not turned off for peer- to-peer communication.

## Slide 6: REQ3: IPv6 deployment
The DMM solutions SHOULD target IPv6 as primary deployment and SHOULD NOT be tailored specifically to support IPv4, in particular in situations where private IPv4 addresses and/or NATs are used.
Motivation: The motivation for this requirement is to be inline with the general orientation of IETF. Moreover, DMM deployment is foreseen in mid-term/long-term, hopefully in an IPv6 world. It is also unnecessarily complex to solve this problem for IPv4, as we will not be able to use some of the IPv6-specific features/tools.

## Slide 7: REQ4: Compatibility
The DMM solution SHOULD be able to work between trusted administrative domains when allowed by the security measures deployed between these domains. Furthermore, the DMM solution MUST be able to co-exist with existing network deployment and end hosts so that the existing deployment can continue to be supported. For example, depending on the environment in which DMM is deployed, the DMM solutions may need to be compatible with other existing mobility protocols that are deployed in that environment or may need to be interoperable with the network or the mobile hosts/routers that do not support the DMM enabling protocol.
Motivation: The motivation of this requirement is to allow inter-domain operation if desired and to preserve backwards compatibility so that the existing networks and hosts are not affected and do not break.

## Slide 8: REQ4 addresses following problems
O-PS2: Complicated deployment with too many variants and extensions of MIP Deployment is complicated with many variants and extensions of MIP. When introducing new functions which may add to the complexity, existing solutions are more vulnerable to break.

## Slide 9: REQ5: Existing mobility protocols
A DMM solution SHOULD first consider reusing and extending the existing mobility protocols before specifying new protocols.
Motivation: The purpose is to reuse the existing protocols first before considering new protocols.

## Slide 10: REQ6: Security considerations
The protocol solutions for DMM MUST consider security, for example authentication and authorization mechanisms that allow a legitimate mobile host/router to access to the DMM service, protection of signaling messages of the protocol solutions in terms of authentication, data integrity, and data confidentiality, opt-in or opt-out data confidentiality to signaling messages depending on network environments or user requirements.
Motivation and problem statement: Mutual authentication and authorization between a mobile host/router and an access router providing the DMM service to the mobile host/router are required to prevent potential attacks in the access network of the DMM service. Otherwise, various attacks such as impersonation, denial of service, man-in-the-middle attacks, etc. are present to obtain illegitimate access or to collapse the DMM service.
Signaling messages are subject to various attacks since these messages carry context of a mobile host/router. For instance, a malicious node can forge and send a number of signaling messages to redirect traffic to a specific node. Consequently, the specific node is under a denial of service attack, whereas other nodes are not receiving their traffic. As signaling messages travel over the Internet, the end-to-end security is required.