## Slide 1: Unified framework and DMM gap analysis draft-chan-dmm-framework-gapanalysis
H. Anthony Chan, h.a.chan@ieee.org

## Slide 2: Abstract the functions of MIP family
Mobility routing (MR) function: to intercept packets to/from the HoA of a mobile node and to forward the packets, based on the internetwork location information, either to the destination (or to some other network element that knows how to forward to the destination).
Home address allocation: allocate the home network prefix or HoA to a MN.
Location management (LM) function: to manage and to keep track of the internetwork location of a MN, which includes a mapping of the HoA to the routing address of the MN (or of another network element that knows how to forward packets towards the MN).
one (or more) proxy may exist between LM and MN so that the LM function is maintained in the hierarchy LM-proxy-MN.

## Slide 3: Unified framework
REQ5: Considering existing protocols first
  Abstracting existing protocol functions is a way to see how to maximize the use of existing protocols
REQ4 (part 2): Compatibility
  Different deployments using the same abstract functions can be compatible with each other
REQ3: IPv6 deployment
  Functions are abstracted from MIPv6 and PMIPv6
Logical Functions (abstracted MIP/PMIP):
1. MR: Mobility routing (data plane)
2. HoA allocation
3. LM: Location management (control plane)
4. Proxy (HMIP)

## Slide 4: Network-based versus Host-based
a. MIP |  |  |  |  |  |  |  | 
IP(HoA) |  | IP(HoA) | IP(HoA) |  | IP(HoA) |  |  | 
 |  |  | IP(CoA) |  | IP(CoA) |  |  | 
CN |  | HA |  |  | MN |  |  | 
b. PMIP |  |  |  |  |  |  |  | 
IP(HoA) |  | IP(HoA) | IP(HoA) |  | IP(HoA) | IP(HoA) |  | IP(HoA)
 |  |  | IP(CoA) |  | IP(CoA) |  |  | 
CN |  | MA |  |  | MAG |  |  | MN
IP layer of the protocol stack are comparable
Packet from CN: no difference other than treating the MAG-MN combination in PMIP as MN in MIP

## Slide 5: Unified framework MIP
REQ6: Security:
Trust between MN and MR
LM, MR, and HoA allocation in home network only
Logical Functions (abstracted MIP/PMIP):
1. MR: Mobility routing (data plane)
2. HoA allocation
3. LM: Location management (control plane)
4. Proxy (HMIP)
MN11
MR1
LM1
HoA11
IP32,HoA11
HoA1 alc
network1
network3
network2
CN21
host-based
IP3 alc
IP2 alc

## Slide 6: Unified framework PMIP
REQ6: Security:
Trust between AR and MR, in addition
LM, MR, and HoA allocation in home network only
Logical Functions (abstracted MIP/PMIP):
1. MR: Mobility routing (data plane)
2. HoA allocation
3. LM: Location management (control plane)
4. Proxy (HMIP)
MN21
MN11
MR1
LM1
HoA11
IP32
IP31
HoA1 alc
network1
network3
network2
AR31
CN21
Client-based or network-based
HoA11
network-based
IP3 alc
IP2 alc

## Slide 7: Unified framework HMIP
REQ6: Security
Trust between MR’s, in addition
LM, MR, and HoA allocation in home network
LM proxy, MR in visited network
Logical Functions (abstracted MIP/PMIP):
1. MR: Mobility routing (data plane)
2. HoA allocation
3. LM: Location management (control plane)
4. Proxy (HMIP)
MN11
MN31
MR1
MR3
LM1
HoA11
IP32,HoA11
IP31
HoA1 alc
network1
network3
network2
AR31
CN21
network-based or host-based
IP3 alc
IP2 alc
MR
MR
MN
MN
LM

## Slide 8: Unified framework Multiple home networks
REQ1 (part 1): Distributed deployment (part 2) avoiding non-optimal routes
  (part 1) May deploy functions in each network
  (part 2 later)
LM, MR, and HoA allocation in each network
Logical Functions (abstracted MIP/PMIP):
1. MR: Mobility routing (data plane)
2. HoA allocation
3. LM: Location management (control plane)
4. Proxy (HMIP)
MN11
LM2
MN31
MR1
MR3
MR2
LM3
LM1
HoA11
IP32,HoA11
IP31
HoA1 alc
HoA3 alc
HoA2 alc
network1
network3
network2
AR31
CN21
network-based or host-based

## Slide 9: Unified framework HAHA
HAHA as a possible DMM solution
  Requires signaling between different LM’s
LM=LM1+LM3+LM2
Logical Functions (abstracted MIP/PMIP):
1. MR: Mobility routing (data plane)
2. HoA allocation
3. LM: Location management (control plane)
4. Proxy (HMIP)
MN11
LM
MN31
MR1
MR3
MR2
LM
LM
HoA11
IP32,HoA11
IP31
HoA1 alc
HoA3 alc
HoA2 alc
network1
network3
network2
AR31
CN21
network-based or host-based

## Slide 10: Unified framework
REQ2: Providing mobility support dynamically
  Home network and HoA was associated with MN. Need to associate instead with an application of the MN (which may have multiple applications)
LM, MR, and HoA allocation in each network
Details in draft-liu-dmm-dynamic-anchor-discussion;
see also draft-bernardos-dmm-pmip; draft-sarikaya-dmm-dmipv6
Logical Functions (abstracted MIP/PMIP):
1. MR: Mobility routing (data plane)
2. HoA allocation
3. LM: Location management (control plane)
4. Proxy (HMIP)
MN11
LM2
MN31
MR1
MR3
MR2
LM3
LM1
HoA11
IP32,HoA11
IP31
HoA1 alc
HoA3 alc
HoA2 alc
network1
network3
network2
AR31
CN21
network-based or host-based

## Slide 11: Unified framework
REQ1 (part 1): Distributed deployment (part 2) avoiding non-optimal routes
  (part 1) Deploy functions in each network
  (part 2) May generalize the LM’s into a distributed database. MR may cache the LM information
  (part 2) Need MR in CN’s network to optimize the route
REQ6: Security
  Trust between MR and LM, in addition
Location management: control plane is supported by hierarchical and distributed database
MN11
LM2
MN31
MR1
MR3
MR2
LM3
LM1
HoA11
IP32,HoA11
IP31
HoA1 alc
HoA3 alc
HoA2 alc
Logical Functions (abstracted MIP/PMIP):
1. MR: Mobility routing (data plane)
2. HoA allocation
3. LM: Location management (control plane)
4. Proxy (HMIP)
network1
network3
network2
AR31
CN21
network-based or host-based