## Slide 1: Out of Jurisdiction Emergency Routing draft-winterbottom-ecrit-priv-loc-01.txt
James Winterbottom, Hannes Tschofenig, Laura Liess

## Slide 2: Device-Centric Emergency Services Model
+---Location Request---+
| (1) |
+---+----+ +---V---+
| |<--Location--| LIS |
| Caller | (2) +-------+ +--------+
| | | ESRP/ |
| |----Find Service-------+ | PSAP |
+------^-+ (3) | +--------+
| | +--------V----+ ^
| +-----Service----| LoST Server | |
| (4) +-------------+ +---+---+
+-------------Call Initiation------------>| VSP |
(5) +-------+
Challenges with the approach have been described in http://tools.ietf.org/html/rfc6444

## Slide 3: Softswitch-Centric Calling Model
+---Location Request---+
| (2) |
+---V---+ |
| LIS | |
+----+--+ +----+----+
| | |
+----Location--->| Soft |
+--------+ (3) | Switch |
| Caller |------Call Initiation------------> | |
+--------+ (1) +-+-^---+-+
+-------------+ | | |
| LoST Server |<-Find Service--+ | |
+------+------+ (4) | |
| | |
+----------Service--------+ |
(5) |
+-----------+ |
| ESRP/PSAP |<------Call----+
+-----------+ (6)
Approach had been explored in various countries, such as UK, Canada, etc. Various challenges exist, such as lack of LoST infrastructure.

## Slide 4: Problem Description
Security: One concern is about the possibility of the software of the end device being able to tamper with location.
Privacy: There is the desire to allow location information to be provided to emergency organizations rather than any other party, including the end device or a VSP.

## Slide 5: Observations
Rough location information is required to route emergency calls.
The VSP needs the ability to determine the correct LIS to retrieve location information.
The VSP needs the ability to contact a LoST server to acquire routing information from.
The end host does not acquire or convey location to the emergency network.
Access network provider aim to provide location only to emergency service authorities.
Precise location information is required to dispatch first responders.

## Slide 6: Our Approach
The VSP queries the LIS using HELD and the IP address of the calling device as an identity extension.
The LIS determines the location and uses it request routing information for the local LoST server.
The LIS return a location URI and the local Emergency Service Routing Proxy (ESRP) URI to the VSP.