## Slide 1
Local Power Distribution
(“Nanogrids”)
draft-nordman-nanogrids-00
Bruce Nordman
Lawrence Berkeley National Laboratory
August 1, 2012
BNordman@LBL.gov — nordman.lbl.gov
IETF 84

## Slide 2: What is OSI Model equivalent for energy ?
7 - Application
6 - Presentation
5 - Session
4 - Network (IP)
3 - Transport
2 - Data Link
1 - Physical
Notes: This talk to emphasize breadth, not depth.

## Slide 3: What is OSI Model equivalent for energy ?
Functionality
Power distribution
7 - Application
6 - Presentation
5 - Session
4 - Network (IP)
3 - Transport
2 - Data Link
1 - Physical
Notes: This talk to emphasize breadth, not depth.

## Slide 4: What is OSI Model equivalent for energy ?
7 - Application
6 - Presentation
5 - Session
4 - Network (IP)
3 - Transport
2 - Data Link
1 - Physical
Functionality
Power distribution
User interface
Discovery/events
Common data model
Exchange between grids
Exchange within grid
Moving electrons on wire
Price
Quantity
Notes: This talk to emphasize breadth, not depth.

## Slide 5: Power distribution
“Technology / infrastructure that moves electrons from devices where they are available to devices where they are wanted”
Important similarities between moving bits and moving electrons
Important differences between moving bits and moving electrons
All bits/packets different; all electrons same
Notes: This talk to emphasize breadth, not depth.

## Slide 6: Ideal power system characteristics*
Scalable
Resilient
Flexible / Ad hoc
Interoperable
Renewable-friendly
Cost-effective
Customizable
Enable new features
Enable new applications
*Roege, Paul, Scalable Energy Networks, Joint Forces Quarterly, #62, Q3, 2011
Notes: This talk to emphasize breadth, not depth.

## Slide 7: Needed system capabilities
Scalable
Resilient
Flexible / Ad hoc
Interoperable
Renewable-friendly
Cost-effective
Customizable
Enable new features
Enable new applications
*Roege, Paul, Scalable Energy Networks, Joint Forces Quarterly, #62, Q3, 2011
Optimally match supply and demand (price)
Match reliability and quality to device needs
Enable arbitrary and dynamic connections
  devices, generation, storage, and “grids”
  “plug and play”; networked
Efficiently integrate local renewables and storage
Work with or without “the grid”
  (or any other grid)
Use standard technology
What grid model enables this?
Notes: This talk to emphasize breadth, not depth.

## Slide 8: Traditional power distribution
Grid is a single undifferentiated “pool” of power
Enormous complexity suggests difficult to manage
  Only works because it is NOT managed
  Fails to meet specified needs
Notes: This talk to emphasize breadth, not depth.

## Slide 9: “Distributed” power distribution
Network of “grids” of various sizes
Grids are managed locally
Generation and storage can be placed anywhere
Interfaces between grids
  enable isolation
  enable exchanging power any time mutually beneficial
Notes: This talk to emphasize breadth, not depth.

## Slide 10: “Distributed” power distribution
Distributed power looks a lot like the Internet
  A network of grids (“intergrid”)
Peering exchanges can be multiple, dynamic
With reliability at edge, core can be less reliable
Smallest piece is “nanogrid”
Notes: This talk to emphasize breadth, not depth.

## Slide 11: Scaling structure: communications and power
Internet
Building/Campus Network
Local Area Network
“The Grid”
Microgrid
Nanogrid
Wide area
Management
Device
Notes: This talk to emphasize breadth, not depth.

## Slide 12: What is a Nanogrid?
“A (very) small electricity domain”
Like a microgrid, only (much) smaller
Has a single physical layer (voltage; usually DC)
Is a single administrative, reliability, and price domain
Can interoperate with other (nano, micro) grids and generation through gateways
Wide range in technology, capability, capacity
Notes: This talk to emphasize breadth, not depth.

## Slide 13: Existing nanogrid technologies
No communications
Vehicles – 12 V, 42 V, 400 V, …
eMerge – 24 V, 380 V
Downstream of UPS – 115 VAC
With communications
Universal Serial Bus, USB – 5 V
Power over Ethernet, PoE – 48 V
HDBaseT – 48 V
Proprietary systems
Power adapter systems (emerging)
Wireless power technologies
Universal Power Adapter for Mobile Devices, UPAMD – IEEE
Notes: This talk to emphasize breadth, not depth.

## Slide 14: IEEE – Universal Power Adapter for Mobile Devices
Source:
IEEE
Notes: This talk to emphasize breadth, not depth.

## Slide 15: Nanogrids do NOT (but Microgrids do)
incorporate generation (?)
optimize multiple-output energy systems
  e.g. combined heat and power, CHP
provide a variety of voltages (both AC and DC)
provide a variety of quality and reliability options.
connect to the grid
require professional design / installation
Notes: This talk to emphasize breadth, not depth.

## Slide 16: Village example
Start with single house – car battery recharged every few days
  Light, phone charger, TV, …
  Add local generation – PV, wind, …
B
PV
Notes: This talk to emphasize breadth, not depth.

## Slide 17: Village example
Start with single house – car battery recharged every few days
  Light, phone charger, TV, …
  Add local generation – PV, wind, …
Neighbors do same
  Interconnect several houses
B
PV
PV
PV
Notes: This talk to emphasize breadth, not depth.

## Slide 18: Village example
Start with single house – car battery recharged every few days
  Light, phone charger, TV, …
  Add local generation – PV, wind, …
Neighbors do same
  Interconnect several houses
School gets PV
  More variable demand
Eventually all houses, businesses connected in a mesh
  Can consider when topology should be changed
Existence of generation, storage, households, and connections all dynamic
B
PV
PV
PV
PV
B
B
Notes: This talk to emphasize breadth, not depth.

## Slide 19: Village example
Start with single house – car battery recharged every few days
  Light, phone charger, TV, …
  Add local generation – PV, wind, …
Neighbors do same
  Interconnect several houses
School gets PV
  More variable demand
Eventually all houses, businesses connected in a mesh
  Can consider when topology should be changed
Existence of generation, storage, households, and connections all dynamic
Can later add grid connection(s)
From no electricity to distributed power – skip traditional grid; Similar to no phone to mobile phone – skip landline system
B
PV
PV
PV
PV
B
B
Notes: This talk to emphasize breadth, not depth.

## Slide 20: Forward Operating Base Example
Reliable nanogrid
Bulk nanogrid
Sleeping
Showers
Eating
Commun ication
Vehicle Maint.
Water Treatment
Fossil generation
Renewable gen.
External storage
Each reliable nG also has local storage; Reliable nGs serve electronics and lighting; Bulk nGs serve HVAC, pumps.
Supervisor server collects data and makes policy recommendations to nGs (does NOT control directly);
Notes: This talk to emphasize breadth, not depth.

## Slide 21: Nanogrid operation - internal
Loads (devices) may always get ‘trickle power’ to communicate
Loads request authority to use power (controller grants)
Controller sets local price (forecast) and distributes
Controller manages storage
Normal operation – all allocation done by loads themselves based on price
Emergency – controller can revoke/cut power
Details technology-specific
Notes: This talk to emphasize breadth, not depth.

## Slide 22: Nanogrid operation – external (gateways)
Controllers discover other grids (and generation)
Exchange interest in sharing power (price, quantity)
When mutually beneficial, power is exchanged
External prices will often affect internal ones
Controllers may track cumulative energy, $$$$
Only data exchanged are price, quantity
Visibility only to immediately adjacent grids
Notes: This talk to emphasize breadth, not depth.

## Slide 23: Why Nanogrids?
Bring individual devices into grid context
Pave way for Microgrids
  Increase microgrid utility; enable local microgrid prices
  Reduce microgrid cost and complexity
  Can scale/deploy much faster than microgrids
Enable “Direct DC” (~10% savings)
Better integrate with mobile devices, mobile buildings
Help bring good electricity services to developing countries
More secure
  Coordinate only with immediately adjacent (directly attached) grids / devices
  No multi-hop “routing” of power
Notes: This talk to emphasize breadth, not depth.

## Slide 24: The way forward
Better document existing nanogrids
  Technologies, capabilities, applications, deployment, …
Define a “meta-architecture” for controllers, gateways, prices, …
Define specific gateways (voltage, communication)
Define nanogrid implementation for existing technologies
Create working nanogrids – loads, controllers, gateways
Create a nanogrid simulator
Notes: This talk to emphasize breadth, not depth.

## Slide 25: Conclusions
Nanogrids can optimally match supply and demand
  Price: internally and externally
Nanogrids can be key to success of microgrids
  Can be deployed faster, cheaper
Need to be standards-based, universal
Key missing technologies: pricing and gateways
Nanogrids are a “generally useful technology”
Notes: This talk to emphasize breadth, not depth.

## Slide 26: Thank you
Notes: Thank you, and I look forward to comments, questions, and discussion.

## Slide 27: Inspiration
  Existing technology
  Modeling network architecture on Internet
    Randy Katz et al., UCB; “LoCal” – local.cs.berkeley.edu
  Developing country needs; off-grid households
    Eric Brewer, UCB; TIER – tier.cs.berkeley.edu Technology and Infrastructure for Emerging Regions
  Network of networks  Internet — Network of grids  Intergrid
photos: Colombia University
Notes: This talk to emphasize breadth, not depth.

## Slide 28
Photo: Matthew Kam, TIER
School near Lucknow, India