## Slide 1: Session-ID Requirements for IETF84
draft-ietf-insipid-session-id-reqts-00
1 August 2012
Paul Jones, Gonzalo Salgueiro, James Polk,
Laura Liess, Hadriel Kaplan

## Slide 2: Illustrating the Problem: Alice and Bob via B2BUA or SBC
Carol
Bob
B2BUA
dialog ID “X”
dialog-ID “Y”
What is the end-to-end dialog identifier?
Alice thinks it is X and Bob thinks it is Y.
BOTH think they are communicating directly with the other
Alice

## Slide 3: Agenda
Review existing proposals from use-cases in WG-00.txt with new text from list messages.
Review remaining 2 open requirements
  Determine which are good as is
Discuss open issues

## Slide 4: Session-ID old Use-cases (1/2)
End-to-end identification of a communication session
End-to-end identification of a communication session that includes a plurality of signaling protocol (e.g., SIP, H.323, and XMPP) wherein a session might originate using one protocol and terminate using a different protocol
Distinguish between devices taking part in the same multipoint conference

## Slide 5: Session-ID old Use-cases (2/2)
Tracking sessions transferred from one endpoint to another
Facilitate the recording of SIP sessions and correlating those sessions
  (the WG will not define parts within other protocols, but will take due consideration of future interoperability with protocols (e.g., H.323, RTCP, RSVP).)
Logging for the purposes of accounting, billing, debugging, communication tracking (such as for security purposes in case of theft of service), etc.

## Slide 6: Session-ID retained Use-cases (1/2)
3.1. Session Recording: A SIP Session is established between UA A and UA B with a SIP B2BUA acting as a middlebox. Both UA A and UA B establish a recording session with a session recording server (SRS) using the SIPREC protocol. The SRS needs to be able to determine from the metadata provided by UA A and UA B that the media streams are associated with the same communication session (CS).
Derived Requirements: REQ1, REQ3, REQ4

## Slide 7: Session-ID retained Use-cases (1/2)
3.2. Protocol Interworking: A communication session might originate in an H.323 endpoint and pass through a Session Border Controller before ultimately reaching a terminating SIP user agent. Likewise, a call might originate on a SIP user agent and terminate on an H.323 endpoint. It MUST be possible to identify such sessions end-to-end across the plurality of devices, networks, or administrative domains.
It is expected that the ITU-T will define protocol elements for H.323 to make the end-to-end signaling possible.
Derived Requirements: REQ7, REQ9a.
Notes: Need a consistency of style across all use-cases, similar (probably) to 3.1.
This level of verboseness is what is expected for each use-case.

## Slide 8: Session-ID new Use-cases (1/8)
3.X End-to-end identification of a communication session
“SIP messaging that either does not involve SIP servers or only involves SIP proxies, the Call-ID: header value sufficiently identifies each SIP message within a transaction or dialog. This is not the case when either B2BUAs or SBCs are in the signaling path between UAs. Therefore, we need the ability to identify each communication session per transaction through a single SIP header-value regardless of which type of SIP servers are in the signaling path between UAs. For transactions that create a dialog, have each message within the same dialog MUST use the same identifier.
Derived Requirements: REQ#1”

## Slide 9: Session-ID new Use-cases (2/8)
3.X Identification of devices taking part in the same multipoint Conference
“SIP messaging can easily be multipoint in nature, specifically with several UAs communicating with a multipoint control unit (MCU) as part of a conference. The ability to distinguish all participants in single focus based multipoint conference to be identified as in the same communications session with all the other participants (i.e., in a single star configuration), verses in another conference session.
Derived Requirements: “

## Slide 10: Session-ID new Use-cases (3/8)
3.X Tracking sessions transferred from one endpoint to another
“It is difficult to track which SIP messages where involved in the same call across transactions, especially when invoking supplementary services such as call transfer or call join. The ability to track communications sessions as they are transferred, one side at a time, through until completion of the session (i.e., until a BYE is sent).
Derived Requirements: “

## Slide 11: Session-ID new Use-cases (4/8)
3.X Session Signal Logging
“An after the fact search of SIP messages to determine which were part of the same transaction or call is difficult when B2BUAs and SBCs are involved in the signaling between UAs. Mapping more than one Call-ID together can be challenging because all of the values in SIP headers on one side of the B2BUA or SBC will likely be different than those on the other side. If multiple B2BUAs and/or SBCs are in the signaling path, more than two sets of header values will exist, creating more of a challenge. Creating a common header value through all SIP entities will greatly reduce any challenge for the purposes of accounting, billing, debugging, communication tracking (such as for security purposes in case of theft of service), etc.
Derived Requirements: “

## Slide 12: Session-ID new Use-cases (5/8)
3.X Identifier Porting to Other Protocols - RSVP
“There may be a desire to associate SIP session signaling with corresponding media flows. To facilitate this association, it should be possible to insert the Session-ID into a media-related message, such as an RSVP PATH message. This association would allow, as an example, for network monitoring equipment to associate troubled network flows with the end-to-end SIP session signaling.
Derived Requirements: REQ9b”

## Slide 13: Session-ID new Use-cases (6/8)
3.X Identifier Porting to Other Protocols - RTCP
“There may be a desire to associate SIP session signaling with corresponding media flows. To facilitate this association, it should be possible to insert the Session-ID into a media-related message, such as an RTCP sender report message. This association would allow, as an example, for network monitoring equipment to associate troubled network flows with the end-to-end SIP session signaling.
Derived Requirements: REQ9c”

## Slide 14: Session-ID new Use-cases (7/8)
3.X Traffic Monitoring
“UA A and UA B communicate using SIP messaging with a SIP B2BUA acting as a middlebox which belongs to a SIP service provider. For privacy reasons, the B2BUA changes the SIP headers that reveal information related to the SIP users, device or domain identity. The service provider uses an external device to monitor and log all SIP traffic coming to and from the B2BUA. In the case of failures reported by the customer or when security issue arise (e.g. theft of service), the service provider has to analyze the logs from the past several days or weeks and correlates those messages which were messages for a single end-to-end SIP session.
For this scenario, we must consider three particular use cases:
a) The UAs A and B support the end-to-end Session Identifier.
Derived Requirements: REQ1, REQ4, REQ5, REQ8.
b) Only the UA A supports the end-to-end Session Identifier, the UA B does not.
Derived Requirements: REQ1, REQ4, REQ5, REQ7, REQ8.
c) UA A and UA B do not support the end-to-end Session Identifier.
Derived Requirements: REQ1, REQ4, REQ5, REQ7, REQ8”

## Slide 15: Session-ID new Use-cases (8/8)
3.X 3PCC Use Case.
Third party call control refers to the ability of an entity to create a call in which communication is actually between two or more parties. For example, a B2BUA acting as a third party controller could establish a call between two SIP UA's using 3PCC procedures as described in section 4.1 of RFC 3725 the flow for which is reproduced below.
A Controller B
|(1) INVITE no SDP | |
|<------------------| |
|(2) 200 offer1 | |
|------------------>| |
| |(3) INVITE offer1 |
| |------------------>|
| |(4) 200 OK answer1 |
| |<------------------|
| |(5) ACK |
| |------------------>|
|(6) ACK answer1 | |
|<------------------| |
|(7) RTP | |
|.......................................|
Figure 1. Session-ID 3PCC Scenario
Such a flow must result in a single session identifier being used for the communication session between UA A and UA B.
Derived Requirements: REQ10

## Slide 16: Session-ID Requirements (1/2)
REQ1: It must be possible for an administrator or an external device which monitors the SIP-traffic to use the identifier to identify those dialogs which were at some point in time components of a single end-to-end SIP session (e.g., parts of the same call).
REQ1a: { with above, not felt necessary any longer }
REQ6: { merged into REQ5 }

## Slide 17: Session-ID Requirements (2/2)
REQ10: It must be possible to correlate two end-to-end sessions when the sessions are created by a third party controller using 3PCC procedures as described shown in Figure 1, as described in RFC 3725.

## Slide 18: Open Issues
Minimal feedback about use-case text for draft…
Iron out final wording on Use-cases and Requirements