## Slide 1: End-to-End SIP Session-ID at IETF84
draft-jones-insipid-session-id-00
1 August 2012
James Polk, Paul Jones
Gonzalo Salgueiro, Chris Pearce

## Slide 2: Why an E2E Session-ID?
Identify issues in the network (debugging)
Track sessions as they move (e.g., transfer)
Associate media flows with a session by inserting the Session ID into RTCP, RSVP, or other protocols
Enable monitoring or recording of sessions (with proper end-to-end identification)
Associate sessions that are related (e.g., participants in a multipoint conference or part of a targeted single or multi-party session to be recorded)

## Slide 3: Existing Call Identifiers
Both SIP and H.323 define identifiers that can identify a “call” or “session”
None of the existing identifiers allow for an intermediary like a B2BUA or SBC to “join” call legs in the network and maintain and end-to-end identifier
Often, B2BUAs or SBC modify call identification information

## Slide 4: Illustrating the Problem: Alice and Bob via B2BUA or SBC
Alice
Carol
Bob
B2BUA
Call ID “X”
Call-ID “Y”
What is the end-to-end call identifier?
Alice thinks it is X and Bob thinks it is Y.
BOTH think they are communicating directly with the other

## Slide 5: Let Each Endpoint Contribute
Rather than having the calling device or called device assign a Session-ID, let each assign part of the end-to-end Session-ID
We then concatenate the values (in a predictable manner)

## Slide 6: The New Session ID
Alice
Carol
Bob
Session-ID is
A || B
B2BUA
Session-ID part “A”
Session-ID part “B”
UUID A=0xaeffa652b22911dfa81f12313a006823
UUID B=0xbe11afc8b22911df86c412313a006823

## Slide 7: Call Transfer
Alice
Carol
Bob
Session-ID part “C”
Session-ID part “B”
Session-ID is
B || C
B2BUA
Session-ID part “A”
Session-ID part “B”
Session-ID is
A || B
Alice transfers Bob to Carol

## Slide 8: The ‘JOIN’ Case
Alice
Bob
Dave
B2BUA1
Alice calls Bob, transfers Bob to Carol
Carol
B2BUA2
Alice calls Bob, transfers Alice to Dave
Session-ID is A || B, becomes B || C
Session-ID is B || A, becomes D || A
Becomes: Carol talking to Dave
Session-ID is C || D

## Slide 9: Associating Participants in a Conference (1/2)
Alice
George
Bob
Carol
Frank
Ed
Dave
MCU
MCU assigns the same Session-ID component “M” to each endpoint in the same conference
Each endpoint assigns a unique Session-ID component, making each e2e Session-ID unique, but enabling the association of all entities in the same conference via “M”
Session-ID is
A || M
B || M
C || M
D || M
E || M
F || M
G || M

## Slide 10: Associating Participants in a Conference (2/2)
Alice
George
Bob
Carol
Frank
Ed
Dave
MCU
MCU assigns the same Session-ID component “M” to each endpoint in the same conference
Each endpoint assigns a unique Session-ID component, making each e2e Session-ID unique, but enabling the association of all entities in the same conference via “M”
Session-ID is
A || M
B || M
C || M
D || M
E || M’
F || M’
G || M’

## Slide 11: New 3PCC and Session-ID
Alice
Bob
B2BUA
Session-ID part “X”
3PCC from B2BUA to Alice and Bob
INVITE
200 OK
Session-ID part “A||X”
INVITE
Session-ID part “A”
200 OK
Session-ID part “B||A”
ACK
ACK
Session-ID part “B||A”
Session-ID part “B||A”
RTP

## Slide 12: Session-ID Construction
Session-ID is two RFC 4122 defined 32-byte UUIDs (or “half-keys”) concatenated together.
Several choices to make
  Hex or base64
    Seems to be a byte savings issue exclusively
  Half key ordering (fixed size keys, with separator)
    Have a prefix (From:X, To:Y)
    Lowest value first, highest second
    Sender first, receiver second (reordered when UAS sends)
    Send in any order, at any time

## Slide 13: Notes
Each component of the Session-ID contributed by each endpoint is a UUID/GUID, so it is unique
Each half Session-ID visible upon initial transmission of SIP message from that UA.
UAS combines each Session-ID half to form full Session-ID in SIP response
The Session-ID can be in session signaling, debugging logs, RTCP, RSVP, or other protocols to associate signaling and media, perform diagnostics, create CDRs, etc.
ITU-T SG16 initiated parallel work to allow session identification even when interworking between H.323 and SIP networks

## Slide 14: Next Steps
Is this ready to be adopted?