## Slide 1: IETF 84 – Vancouver August 2012
LSP Ping Support for E-VPN and PBB-EVPN
(draft-jain-l2vpn-evpn-lsp-ping-00.txt)
Parag Jain (Cisco Systems Inc.),
Sami Boutros (Cisco Systems Inc.),
Samer Salam (Cisco Systems Inc.)

## Slide 2: LSP Ping Support for E-VPN and PBB-EVPN
Define LSP Ping procedures for E-VPN and PBB-EVPN
Support ingress replication and P2MP P-trees for Broadcast, multicast and unknown unicast.
Define 3 new sub-TLVs for Target FEC Stack for identifying various FEC under test

## Slide 3: Proposed E-VPN MAC sub-TLV Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Route Distinguisher |
| (8 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ethernet Segment Identifier |
| (10 octets) |
+ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| | must be zero |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ethernet Tag ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MAC Address |
+ (6 Octets) +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| | MAC Addr Len | IP Addr Len |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IP Address (4 or 16 Octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| EVI |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 4: Proposed E-VPN Inclusive Multicast sub-TLV Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Route Distinguisher |
| (8 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ethernet Segment Identifier |
| (10 octets) |
+ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| | must be zero |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ethernet Tag ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| EVI |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 5: Proposed E-VPN Auto-Discovery sub-TLV Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Route Distinguisher |
| (8 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ethernet Segment Identifier |
| (10 octets) |
+ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| | must be zero |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ethernet Tag ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| EVI |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 6: Remote MAC Connectivity test
Echo Request with target FEC stack TLV containing E-VPN MAC sub-TLV.
Echo Request packet will be encaped with E-VPN MAC label as the bottom label:
  {Transport Label(s), E-VPN MAC Label}

## Slide 7: Multicast Connectivity test for Ingress Replication
Echo Request with target FEC stack TLV containing E-VPN Inclusive Multicast sub-TLV.
Echo Request packet will be encaped with E-VPN Inclusive Multicast label as the bottom label:
  {Transport Label(s), E-VPN Inclusive multicast Label}
For PBB-EVPN, if remote PE is not DF for the tag (ISID) ID in the inclusive Multicast sub-TLV on some Ethernet Segments, the remote will reply with a special return code –
  “FEC exists on the router and the behavior is to drop the packet because of not DF”
For E-VPN case, Echo Request packet may carry an Ethernet AD sub-TLV and associated MPLS Split Horizon Label at the bottom of the MPLS label stack for the other remote MH PE who will respond with a special return code.
  “FEC exists on the router and the behavior is to drop the packet because of Split Horizon Filtering”

## Slide 8: Multicast Connectivity test for P2MP P-tree
Echo request to the remote PE with the target FEC stack TLV containing E-VPN Inclusive Multicast sub-TLV.
When Using Inclusive P2MP P-trees, send Echo Request packet with the following label stack:
  {P2MP P-tree label}
When Using Aggregate Inclusive P2MP P-trees, send Echo Request packet with the following label stack:
  {P2MP P-tree label, Upstream assigned E-VPN Multicast Label }
For PBB-EVPN, if remote PE is not DF for the tag (ISID) ID in the inclusive Multicast sub-TLV on some Ethernet Segments, the remote will reply with a special return code –
  “FEC exists on the router and the behavior is to drop the packet because of not DF”
For E-VPN case, Echo Request packet may carry an Ethernet AD sub-TLV and associated MPLS Split Horizon Label at the bottom of the MPLS label stack for the other remote MH PE who will respond with a special return code.
  “FEC exists on the router and the behavior is to drop the packet because of Split Horizon Filtering”

## Slide 9: Aliasing State Connectivity test
Echo request to the remote PE with the target FEC stack TLV containing E-VPN Ethernet AD sub-TLV.
Echo Request packet encaped with E-VPN Ethernet AD label as the bottom label:
  {Transport Label(s), E-VPN Ethernet AD Label}

## Slide 10: Next Steps
Seeking Feedback
Looking for WG adoption