## Slide 1: draft-boutros-l2vpn-evpn-vpws-00.txt Sami Boutros Ali Sajassi Samer Salam IETF 84, July 2012 Vancouver, Canada

## Slide 2: E-VPN For VPWS
E-VPN enables the following characteristics for VPWS:
  Active/standby redundancy.
  Active/active multi-homing with flow-based load-balancing.
  Eliminates the need for single-segment and multi-segment PW signaling
  Provides faster convergence using data-plane prefix independent convergence upon node or link failure in comparison to control-plane convergence with PW redundancy.

## Slide 3: How it works?
[E-VPN] has the ability to forward customer traffic to/from a given customer Attachment Circuit (aka Ethernet AD route) without any MAC lookup. This capability is ideal in providing P2P services (aka VPWS services).
[MEF] defines EVPL service as P2P service between a pair of ACs (designated by VLANs). EVPL can be considered as a VPWS with only two ACs. In delivering an EVPL service, traffic forwarding capability of E-VPN between a pair of Ethernet AD routes is used; whereas, for more general VPWS, traffic forwarding capability of E- VPN among a group of Ethernet AD routes (one Ether AD route per AC/site) is used.
MPLS label associated with the destination Ether AD route can be used in forwarding user traffic to the destination AC.

## Slide 4: BGP Extensions
No new BGP messages.
Repurposes Ethernet AD route to signal P2P services.
  Ethernet Segment Identifier field is set to the ESI of the attachment circuit of the VPWS service instance.
  Ethernet Tag field is set to 0 in the case of an Ethernet Private Wire service, and to the VLAN identifier associated with the service for Ethernet Virtual Private Wire service.
  Route- Target (RT) extended community attribute identifies the service instance (together with the Ethernet Tag field when non-zero)

## Slide 5
Operation..
Ethernet Ethernet
Native |<---------E-VPN Instance----------------------->| Native
Service | | Service
(AC) | |<-PSN1->| |<-PSN2->| | (AC)
| V V V V V V |
| +------+ +---------+ +---------+ +------+ |
+-----+ | | PE1 |======|ASBR1|==|ASBR2|===| PE3 | | +------+
| |------+-------+ +---------+ +---------+ +------+-------| |
| CE1| | | |CE2 |
| |-------+-------+ +---------+ +---------+ +------+-------| |
+-----+ | | PE2 |======|ASBR3|==|ASBR4|===| PE4 | | +------+
^ +------+ +---------+ +----------+ +-------+ ^
| Provider Edge 1 ^ Provider Edge 2 |
| | |
| | |
| E-VPN Inter-provider point |
| |
|<---------------- Emulated Service --------------------------------->|
iBGP sessions between PE1, PE2, ASBR1, ASBR3, and PE3, PE4, ASBR2, ASBR4.
eBGP sessions between ASBR1, ASBR2, ASBR3, and ASBR4.
Exchange E-VPN Ethernet A-D routes - one route per AC. ASBRs re-advertise routes with Next Hop self.
CE link between is an C-TAG or S-TAG interface as described in [802.1Q].
A VPWS with multiple sites or multiple EVPL services on the same CE port can be included in one EVI between 2 or more PEs.
An Ethernet Tag corresponding to each P2P connection and known to both PEs is used to identify the services multiplexed in the same EVI.
In CE multi-homing, Ethernet AD Route encodes the ESI associated with the CE. This allows flow-based load-balancing of traffic between PEs.
Ethernet Segment route may be used too, for discovery of multi-homed CEs.

## Slide 6: P2P PW and EVPN Comparison
P2P PW redundancy is limited to Active/Standby mode, while with E-VPN both Active/Active and Active/Standby.
P2P PW, backup PWs are not used to carry traffic, while E-VPN traffic can be load-balanced among primary and secondary PEs.
On link or node failure, E- VPN can trigger failover with the withdrawal of a single BGP route per service, whereas with VPWS PW redundancy, the failover sequence requires exchange of two control plane messages: one message to deactivate the group of primary PWs and a second message to activate the group of backup PWs associated with the access link.
E- VPN may employ data plane local repair and PIC mechanisms not available with P2P PW.

## Slide 7: Next steps
Comments are appreciated.
Thank you