## Slide 1: VLAN-Aware Bundling for EVPN/VPLS draft-cai-l2vpn-evpn-vlan-aware-bundling-00
Dennis Cai (dcai)
Sami Boutros (sboutros)
Samer Salam (ssalam)
Reshad Rahman (rrahman)
Cisco Systems
IETF 84, July 2012 Vancouver, Canada

## Slide 2: A simple scenario: DC LAN Extension
EVI/VFI
UNI
PE1
PE2
PE3
Solution 1: EVI/VFI per each VLAN
 Provisioning/configuration/scale overhead
Solution 2: QinQ, VLANs are bundled into same EVI/VFI
 No VLAN separation, for example, duplicated MAC across VLANs could cause issue
 Unnecessary packet flooding to PE3 for VLAN 51-100 (in this example)
 Unnecessary MAC withdrawal ( in the multi-homing scenario)
UNI
UNI
BD
BD
BD
C-VLAN: 1-100
C-VLAN: 1-100
C-VLAN: 1-50
EVI/VFI
EVI/VFI

## Slide 3: What’s the “VLAN-aware bundling”?
It’s “enhanced” QinQ with customer VLAN separation
“VLAN-aware” means “VLAN separation”, which means:
  Customer VLANs are in different broadcast domain
  MAC learning/flushing is per customer VLAN
“VLAN-aware” includes both UNI and WAN side
  UNI: “vlan-aware” bundling (or “vlan-aware” qinq)
  WAN side: “vlan-aware” evpn/vpls
EVI/VFI
UNI
UNI
C-VLANs
C-VLANs
C-VLANs are aggregated over single EVC: EVI/VFI
EVI/VFI
“VLAN-aware” bundling
“VLAN-aware” EVPN/VPLS
Separated C-VLAN bridge-domains
BDs
BDs

## Slide 4: What do we gain?
Use a simple example
  5 DC sites, each site has two PEs
  1000 VLANs
Scale per PE | Classic VPLS | VLAN-aware VPLS
VFIs | 1000 | 1
PWs | 10,000 | 9
ACs | 1000 | 1
Bridge-domains | 1000 | 1000
Lines of configuration | ~ nx1000 lines, depend on the platform | ~10 lines

## Slide 5: Standard requirement
UNI and C-VLAN separation(bridge-domain)
  Vendor specific implementation
NNI (WAN): EVPN/VPLS
  Need inter-operation between vendors
  The focus of this presentation
EVI/VFI
UNI
UNI
C-VLANs
C-VLANs
C-VLANs aggregated over single EVI/VFI
EVI/VFI
Vendor specific implementation
Standard requirement
BDs
BDs

## Slide 6: “VLAN-aware bunlding” for EVPN
This draft recommend to use Ethernet Tag field in the Ethernet Auto-Discovery Route, Mac Advertisement route, and inclusive multicast Ethernet tag route to to multiplex VLANs over the same EVI
Please refer to the EVPN draft for details: draft-ietf-l2vpn-evpn-01

## Slide 7: “VLAN-aware bundling” for VPLS
The PW VLAN Vector TLV is described as below
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1|1| VLAN Vector(TBD)| Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|first VLAN Value |NumberOfValues | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| VLANFlushBits[NumberOfValues] |
| " |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
A new PW VLAN vector TLV is defined, the new PW VLAN Vector TLV will
be included in LDP PW label mapping messages, as well it can be
included in the MAC flush message

## Slide 8: “VLAN-aware” VPLS/EVPN Operation (1)
Flooding packet pruning
  PE only flood the packet based on the VLAN list which it receive from peer PEs
  IGMP/PIM snooping still works as before
Mac withdrawal
  MAC learning, pruning is per each customer VLAN or bridge-domain basis, not per VFI/EVI
  VPLS Mac withdrawal message or EVPN Ethernet AD route should include the list of VLANs. Those VLAN need to have mac flushing on the remote PEs
  VLAN 0 is for the wildcat

## Slide 9: “VLAN-aware” VPLS/EVPN Operation (2)
VLAN translation
  VLAN translation is per local PE
  After VLAN translation, the VLAN ID must be global significant among all PEs within the same VFI/EVI
OAM
  Customer domain OAM will work transparently over VLAN-aware VPLS/EVPN
  Current MPLS OAM mechanisms need to be extended to verify connectivity in the E-VPN or VPLS instance shared by the customer bridge-domains. However, MPLS OAM extensions is out of scope of the document

## Slide 10: Next steps
Comments are appreciated
Thank you