## Slide 1: 802.1aq and 802.1Qbp Support over EVPN draft-allan-l2vpn-spb-evpn-00
Dave Allan, Jeff Tantsura, Don Fedyk, Ali Sajassi

## Slide 2: What is 802.1aq SPB?
802.1aq is a routed Ethernet solution that has been specified by the IEEE
  IS-IS aspects documented in RFC 6329
Two modes defined
  SPBV (VLAN mode) – Based on the 802.1ad (QinQ) dataplane
    Expected to scale to ~100 bridges
  SPBM (MAC mode) – Based on the 802.1ah (MACinMAC) dataplane
    Expected to scale to ~1000 bridges
For SPBM, all control functionality has been collapsed into a single protocol (IS-IS)
  So no M/RSTP, no MVRP/MMRP etc.
This draft focuses on SPBM

## Slide 3: What is important to understand about SPBM?
It is compute based
  Analogous to M-OSPF
It is still trees
  They are shortest path instead of rooted spanning trees
  Unicast and multicast frames follow the same path between any two points in a given B-VID
  Uses deterministic tie breaking
It uses loop prevention AND loop mitigation
It uses edge based load spreading
  Customer VLANs are mapped to Backbone VLANs

## Slide 4: Draft-allan Design Goals
Decouple as much as possible the different EVPN served Ethernet “Islands”
  Minimize the amount of state in any given “island” vis-à-vis the  of set of “islands”
  Decouple network design, engineering & operation, full CP independence
Keep local topology changes out of BGP to maximize stability
Minimize the amount of configuration
Be able to tie together SPBM-islands, 802.1Qbp islands, 802.1ah PBB-MESs/PBBNs etc. into a common L2 domain
  Scale to the sum of all parts
  To be clear we are not discussing one BIG broadcast domain, we are discussing LOTs of small and medium sized broadcast domains

## Slide 5: SPBM and EVPN
802.1ad
PBN
802.1ah
PBBN
802.1Qbp
EVPN
802.1aq
SPBM
MES
MES
MES
MES
MES
MES
PBB
MES
BGP
ISIS
ISIS
PBB
MES
PBB
MES
CE
LACP
STP
CE
CE
CE
CE
STP

## Slide 6: What the draft documents
Elements of procedure
  Control plane interworking between ISIS-SPB and EVPN
  B-VID DF election
  Mapping of ISIS-SPB LSAs to BGP NLRI and vice versa
  Dataplane procedures
    B-Tag stripping & insertion procedures
    Multicast splicing (future version)
  802.1ah/802.1aq/802.1Qbp interworking
    Maps onto the existing PBB-EVPN draft

## Slide 7: Next Steps
Comments from the list
WG adoption (?)