## Slide 1: MVPN MIB draft-ietf-l3vpn-mvpn-mib-00
Saud Asif, AT&T
Andy Green, BT
Sameer Gulrajani, Cisco
Pradeep Jain, ALU
Jeffrey Zhang, Juniper
84th IETF, Vancouver

## Slide 2: Goals
Provide a single MVPN MIB for MVPNs with either PIM- or BGP-signaled C-multicast states
  Referred to as PIM-MVPN and BGP-MVPN respectively
Standard based: RFC 6513/6514
Comparable to existing Cisco PIM-MVPN MIB
  Some text taken verbatim from draft-svaidya-mcast-vpn-mib-02.txt

## Slide 3: MVPN MIB Structure
MvpnPmsiConfig
MvpnSpmsiConfig
MvpnBgpGeneral
MvpnGeneral
MvpnPmsi
TunnelAttribute
MvpnSpmsi
MvpnIpmsi
MvpnInterAs
Ipmsi
MvpnMroute

## Slide 4: MvpnPmsiConfig
Tunnel Configuration on Ingress PE
  Referred to by:
    MvpnGeneral (for Inter/Intra-AS inclusive tunnels)
    MvpnSpmsiConfig (for selective tunnels)
  Avoid repeating the attributes in several entries
    MvpnGeneral (twice: inter &intra-as)
    MvpnSpmsiConfig
MvpnPmsiConfigEntry ::= SEQUENCE {
mvpnPmsiConfigTunnelType INTEGER,
mvpnPmsiConfigTunnelAuxInfo Unsigned32,
mvpnPmsiConfigTunnelPimGroupAddressType InetAddressType,
mvpnPmsiConfigTunnelPimGroupAddress InetAddress,
mvpnPmsiConfigTunnelOrTemplateName SnmpAdminString,
mvpnPmsiConfigEncapsType INTEGER,
mvpnPmsiConfigRowStatus RowStatus
}

## Slide 5: MvpnPmsiTunnelAttribute
Signaled (sent/received) PMSI attributes
  Referred to by:
    mvpnIpmsiEntry: for BGP-signaled I-PMSI
    mvpnSpmsiEntry
MvpnPmsiTunnelAttributeEntry ::= SEQUENCE {
mvpnPmsiTunnelAttributeType Unsigned32,
mvpnPmsiTunnelAttributeLabel MplsLabel,
mvpnPmsiTunnelAttributeFlags OCTET STRING,
mvpnPmsiTunnelAttributeId OCTET STRING,
mvpnPmsiTunnelPointer RowPointer,
mvpnPmsiTunnelIf RowPointer
}

## Slide 6: MvpnSpmsiConfig
S-PMSI configuration on Ingress PE
MvpnSpmsiConfigEntry ::= SEQUENCE {
mvpnSpmsiConfigCmcastAddressType InetAddressType,
mvpnSpmsiConfigCmcastGroupAddress InetAddress,
mvpnSpmsiConfigCmcastGroupPrefixLen Unsigned32,
mvpnSpmsiConfigCmcastSourceAddress InetAddress,
mvpnSpmsiConfigCmcastSourcePrefixLen Unsigned32,
mvpnSpmsiConfigThreshold Unsigned32,
mvpnSpmsiConfigPmsiPointer RowPointer,
mvpnSpmsiConfigRowStatus RowStatus
}

## Slide 7: MvpnSpmsi
Signaled (sent/received) S-PMSIs
MvpnSpmsiEntry ::= SEQUENCE {
mvpnSpmsiCmcastAddrType InetAddressType,
mvpnSpmsiCmcastGroup InetAddress,
mvpnSpmsiCmcastGroupPrefixLen InetAddress,
mvpnSpmsiCmcastSource InetAddress,
mvpnSpmsiCmcastSourcePrefixLen InetAddress,
mvpnSpmsiOrigAddrType InetAddressType,
mvpnSpmsiOrigAddress InetAddress,
mvpnSpmsiTunnelAttribute RowPointer,
mvpnSpmsiUpTime TimeInterval,
mvpnSpmsiExpTime TimeInterval,
mvpnSpmsiRefCnt Unsigned32
}

## Slide 8: MvpnMrouteEntry
Augments ipMRouteEntry
MvpnMrouteEntry ::= SEQUENCE {
mvpnMroutePmsiPointer RowPointer,
mvpnMrouteNumberOfLocalReplication Unsiged32,
mvpnMrouteNumberOfRemoteReplication Unsiged32
}
Need to add traffic rate information
  to MvpnMrouteEntry or ipMrouteEntry?

## Slide 9: Pending Work
Accommodate comments
Add conformance groups
Remove MvpnPmsiConfigTable
  Purpose was to avoid listing attributes in both MvpnGeneral and MvpnSpmsiConfig
  But is it worth maintaining a tree for that?