## Slide 1: Bidirectional P-tunnels in MVPN
Bidirectional P-tunnel:
  MP2MP LSP per RFC 6388
  PIM MDT per RFC 5015, GRE Encapsulation
Accommodated by existing RFCs:
  RFC 6514 allows such tunnels to be specified in PMSI Tunnel Attribute of x-PMSI A-D routes
  RFCs 6513 and 6517 discuss use of these tunnels:
    For saving state in intermediate nodes, and/or
    Preferred method of supporting customers who use BIDIR-PIM (C-BIDIR support)

## Slide 2: Filling the Gaps
Existing RFCs do not provide full specification for use of bidir P-tunnels; mostly say:
  “full specification is out of scope of this document”
draft-ietf-l3vpn-mvpn-bidir fillx these gaps by providing the complete specification for using bidir P-tunnels in MVPN
Two ways of using bidir P-tunnels defined:
  Unpartitioned method: useful, e.g, for I-PMSI or (C-*,C-*) S-PMSI, all PEs in VPN can transmit and receive on it
  Partitioned method: useful for C-bidir support as discussed in RFC 6513 section 11.2
New Wild Card (C-*,C-BIDIR) also defined, to enable binding of all C-bidir flows to a given (bidir) P-tunnel

## Slide 3: Unpartitioned Method
Used to instantiate I-PMSI or WildCard S-PMSI
  Can be used to support PIM/MI-PMSI, but also can be used with BGP C-multicast
All PEs in VPN must identify same P-tunnel in the corresponding A-D routes
  mLDP FEC provisioned,
  root node need not be PE

## Slide 4: Unpartitioned Method Issues
Doesn’t provide RFC 6513 section 11.2 C-bidir support
Duplication prevention:
  Single forwarder selection
  PIM Asserts
  “Discard from wrong PE” technique only available if upstream-assigned labels are used to identify transmitting PE
    this requires that the root node be a PE, and
    that the root node use the PE Distinguisher Labels attribute to bind upstream-assigned labels to PE addresses
    a PE transmitting onto the tunnel would identify itself in the data plane with the corresponding upstream-assigned label

## Slide 5: Partitioned Method
Provides C-bidir support as envisaged in RFC 6513 section 11.2, & recommended in RFC 6517
  The bidir P-tunnels are advertised in S-PMSI A-D routes to which C-bidir flows are bound:
    (C-*,C-*),
    (C-*,C-G) where C-G is a bidir group
    New (C-*,C-BIDIR) wildcard
  The draft also provide rules for using these tunnels to carry unidirectional C-flows
Two variations: with/without LSP hierarchy
  Will discuss “without” variation first

## Slide 6: What’s the Big Deal about C-bidir?
Every BIDIR-PIM Group Address is associated with a Rendezvous Point Address (RPA)
A BIDIR-PIM distribution tree is rooted at the node closest to the RPA
Traffic can enter the tree at any point
Traffic goes both upstream and downstream from the entry point
At every vertex, traffic goes both upstream and downstream
This creates a duplicate detection issue

## Slide 7: What’s the Big Deal about C-bidir?
N1
N2
N3
N5
N7
N4
N6
(*,G) Tree rooted at N1
Possible path of (N7,G) flow
Assume N3 is the Designated Forwarder for the LAN
Note that N2 does not get N7’s traffic from the LAN
N2 gets N7’s traffic from N1 not from N5
N2 does not send traffic from N1 onto LAN
These restrictions necessary to prevent duplicates
No RPF check on data is possible
Restrictions effected by Designated Forwarder Election on LAN;
Only DF (N3 in this case) can take data from downstream off LAN and send upstream
Only DF can put data from upstream on LAN

## Slide 8: Implications for MVPN
Instead of a LAN, we have tunnels across the SP backbone
We do not want to have the PEs of a given MVPN run the BIDIR-PIM DF Election procedures across the backbone
  Not recommended outside a LAN environment
  Don’t want to require PE-PE PIM interactions as precondition of supporting C-BIDIR
Alternative 1: Put the RPA in the backbone (no DF election on the RPA)
Alternative 2: Partitioned Method

## Slide 9: Partitioned Method
  In a given MVPN, when a PE gets Join(*,G) from a CE, where C-G is a BIDIR-PIM group, PE independently selects a “root PE” for C-G
  The selected root PE will be the “upstream PE” (as defined in RFC 6513) for G’s C-RPA
  Any PE that might be the root PE for some bidir group advertises an S-PMSI A-D route (C-*,C-G) or (C-*,C-*) or (C-*,C-BIDIR) whose PMSI Tunnel attribute specifies an MP2MP LSP
  Any PE with (C-*,C-G) traffic to send to other PEs sends on the MP2MP LSP advertised by the root PE for C-G
  When a PE receives (C-*,C-G) traffic from another PE, it discards it unless it has arrived on the MP2MP LSP advertised by the root PE for C-G

## Slide 10: Example
Path of (CE5,G):
  CE5PE5PE2{PE4CE4,
  CE2C-RPCE1PE1PE3CE3}
Path of (CE3,G):
  CE3PE3PE1CE1C-RPCE2PE2{PE5CE5,
  PE4CE4}
No duplication, no DF election, C-RPA at customer site
C-RP
for G
CE1
CE2
CE3
PE2
PE4
CE4
PE1
PE3
PE5
CE5
Two MP2MP LSPs:
PE1-rooted
PE2-rooted
All 5 PEs join both
C1 is root of C-BIDIR tree, group G
Blue nodes choose PE2 as UMH to C-RP, red nodes choose PE1

## Slide 11: Multiple MP2MP LSPs? Really?
  Seems a bit odd
  Very useful though:
    A sender always sends on tree rooted at (independently chosen) DF
    A receiver never accepts traffic on tree not rooted at DF
    Traffic flows not necessarily optimal, but that’s the nature of BIDIR
  Will also work with BIDIR-PIM tunnels in the SP backbone, instead of MP2MP LSPs
  Bidirectional P-tunnels can also be used to carry unidirectional C-flows when the root of the P-tunnel is the UMH of the C-flow
  If upstream-assigned labels (and PE Distinguisher Labels attribute) are available, the whole set of MP2MP LSPs in a given VPN can be aggregated onto a single “outer” MP2MP LSP, thus saving state in the P routers