## Slide 1: MVPN Extranet
First, a little background:
  MVPN Effort that began in 2004 culminated in the set of RFCs 6511-6517 in 2012! (Well, really finished in 2010, mostly)
  Left a few loose ends, including “wild cards” and “extranet”
  Wild cards spec’ed in RFC 6625 (2011-2012)
Extranet is last of the big missing pieces
  Two individual extranet drafts have existed for awhile
    Draft-rosen-l3vpn-mvpn-extranet, covering only PIM C-multicast, 2010, based on text that appeared in 2008
    Draft-raggarwa-l3vpn-bgp-mvpn-extranet, covering only BGP C-multicast, 2009
  Editors have been working (on and off) over past year to merge these two drafts
  Almost done, didn’t quite make the pre-Vancouver deadline

## Slide 2: What Took So Long?
Sorry about the delay
Merge turned out to be fairly intricate:
  not due to any technical disagreement,
  due to complexity of the subject matter, and hard-to-please editors
MVPN Extranet is actually a fairly complex feature
  Base L3VPN mechanisms isolate VPNs from each other, but:
    enable holes to be punched through the isolation mechanisms to allow some inter-VPN traffic, assuming that
    Inter-VPN traffic must use unambiguous addressing in the face per-VPN overlapping address spaces
  MVPN adds further complexity:
    multicast considerations
    wildcard mechanisms
    need to accommodate multiple functional models

## Slide 3: Purpose of This Presentation
Briefly outline some of the fundamental issues
Briefly outline the solutions
Whet the WG’s curiousity so that folks will read the draft when it comes out!

## Slide 4: Some Basic Concepts
Extranet C-source: transmitter allowed to send multicast data to (multiple) other VPNs
Extranet C-group: ASM group address whose transmitter(s) is(are) not necessarily in same VPN as receivers; receivers can be in different VPNs too
Extranet C-flow: (C-S,C-G) multicast data stream with receivers not necessarily in same VPN as transmitter(s)
Extranet C-RP: rendezvous point for extranet C-group, not necessarily in same VPN as transmitters and/or receivers

## Slide 5: Some Basic Assumptions
Certain sources/RPs are designated by the VPN customer as extranet C-sources; customer communicates this information to SP
Extranet C-sources do not also transmit non-extranet C-flows
  If a receiver can get any C-flow from a given source, it can get all the C-flows from that sources
  If a receiver can get any traffic to a given ASM multicast group, it can get all the traffic to that group, regardless of sources

## Slide 6: UMH-Eligible Extranet C-S/C-RP Routes
RFC 6513 defines notion of route that is eligible for use in determining Upstream Multicast Hop of a given C-S/C-RP
Either unicast VPN-IP routes or SAFI-129 routes
  Use of SAFI-129 prevents unicast extranet traffic from being sent to an extranet multicast source
  Route to extranet C-RP must be VPN-IP route, since PIM Registers are unicast packets
Extranet requires extra RT provisioning:
  If C-S in VPN A is to transmit to C-R in VPN B, then A must export route to C-S with an RT that is an import RT of B
  Usually don’t want all routes from A to be exported to B, so some careful RT choices must be made

## Slide 7: RTs on MCAST-VPN Routes
If an extranet C-source from VPN A is exported to VPN B, RTs must be assigned to MCAST-VPN routes to ensure:
  B imports I-PMSI A-D route from A
  If S-PMSI A-D route advertises tunnel that may carry extranet C-flow (C-S,C-G), for some C-G, route must be imported by B
VPN with receivers for an extranet C-group must import:
  x-PMSI A-D routes advertising tunnels carrying flows in that group,
  Source Active A-D routes advertising C-sources of that group
  In some cases, VPNs with receivers must originate I-PMSI A-D routes to be imported by VPNs with transmitters
RT assignment rules of RFC6514 still apply, but additional rules are added

## Slide 8: Additional RT Assignment Constraints on MCAST-VPN Routes
More restrictive rules are added
  Will not cover details in presentation, see draft
  But the restrictions are the following sort of thing: except in certain defined circumstances, if a P-tunnel is not to be used to carry traffic from a given extranet C-sources, it must not be advertised in a PMSI A-D route that carries an RT in common with the route to that C-source
  The more restrictive rules are used to implement a strategy of “discard packets from the wrong tunnel”, which is needed under specified circumstances
  Note that this is not the same as “discard packets from wrong upstream PE”, as specified in RFC 6513, because in extranet, the wrong tunnel can come from the right PE
  Needed because of some address ambiguity issues

## Slide 9: Extranet and Address Ambiguity
This is really the key technical problem
We impose certain address uniqueness requirements that are assumed to be met:
  If C-S in VPN A sends a flow to C-R1 in VPN B and C-R2 in VPN C, then C-S must have an address that is unique in VPNs A,B,C
  If C-G is the group address of that flow, and C-G is an ASM address, C-G must be a unique address in VPNs A, B, C, and its C-RP must have a similarly unique address
But this does not prevent all address ambiguity problems!

## Slide 10: Example of Extranet Address Ambiguity
S2
A
VRF A
A
VRF B
S1
S2
A
VRF C
A
VRF D
R1: Joins (S1,G)
Joins (S2,G)
R2: Joins (S2,G)
PE2
PE1
S2 and S2 are different systems (i.e., ambiguous address between VPNs A and B)
The address uniqueness rules are not violated as long as S2 is not imported by D and S2 is not imported by C
But suppose a tunnel from A carries both (S1,G) and (S2,G)
Then C must import A-D route from A announcing that tunnel
C must also import A-D route from B announcing the other tunnel

## Slide 11: Example of Extranet Address Ambiguity
  VRF C gets both (S2,G) and (S2,G)
  VRF C MUST discard (S2,G), or R1 will get the both streams, and R1 will have no way distinguish them.
S2
A
VRF A
A
VRF B
S1
S2
A
VRF C
A
VRF D
R1: Joins (S1,G)
Joins (S2,G)
R2: Joins (S2,G)
PE2
PE1

## Slide 12: Solutions?
  Provision a policy that prevents this from happening
    E.g., no more than one source (or one ASM group) per tunnel
  or
  Make sure that:
    the UMH-eligible route matching S2 has no RT in common with the A-D route that advertises the tunnel from B
    the UMH-eligible route matching S2 has no RT in common with the A-D route that advertises the tunnel from A
  Now C control plane can infer that traffic from S2 shouldn’t come from B’s tunnel
  Data plane at C is then set up to discard (S2,G) traffic from B’s tunnel
S2
A
VRF A
A
VRF B
S1
S2
A
VRF C
A
VRF D
R1: Joins (S1,G)
Joins (S2,G)
R2: Joins (S2,G)
PE2
PE1

## Slide 13: Functional Models
Extranet Separation or not?
  Option for ensuring that no tunnel contains both extranet C-flows and non-extranet C-flows (e.g., different I-PMSIs for each)
  Differing opinions on whether this is worthwhile
  Spec’d only for BGP PE-PE C-multicast
Is it ever desirable for ingress PE to transmit a single flow on multiple PMSIs?
  Differing opinions on whether this is worthwhile
  Multiple transmission spec’ed only for PIM PE-PE
We have not tried to provide every possible combination, in absence of demonstrated interest

## Slide 14: Wild Card Issues
RFC 6625 contains elaborate set of rules for determining whether to expect (C-S,C-G) and/or (C-*,C-G) traffic on a particular P-tunnel, depending upon whether the P-tunnel is advertised in an I-PMSI, (C-S,C-*) S-PMSI, (C-*,C-G) S-PMSI, (C-*,C-*) S-PMSI, or (C-S,C-G) S-PMSI A-D route
These rules are augmented, in certain specific cases, to require that a C-flow is expected from a given P-tunnel only if that P-tunnel is advertised in an x-PMSI A-D route that has an RT in common with the installed UMH-eligible route to the C-S or C-RP.
This is important for determining the right tunnel when wild cards are used

## Slide 15: Stuff Specific to PE-PE PIM
PE-PE PIM requires tunnels to be grouped into emulated LANs, and Joins are send over those “e-lans”.
A VRF that is part of an extranet is on multiple “e-lans”
  In one model, must be able to receive from multiple e-lans
  In another model, must be able to send on multiple e-lans
  Or both …
Rules are given for performing the grouping of tunnels into e-lans
  Basically, x-PMSI A-D routes advertising P-tunnels that are part of the same e-lan must carry an RT in common, and this RT must not be carried by any other x-PMSI A-D routes
  In some cases, multiple I-PMSI A-D routes must be originated by a given VRF, this is spec’ed out in detail

## Slide 16: PIM-specific vs. BGP-specific Rules
For PIM, once tunnels are properly grouped into e-lans, rules for specifying which tunnel to send a join on, which tunnel to expect a flow from, etc., can be inferred from “ordinary” PIM procedures
For BGP, we don’t have this “level of indirection”, all procedures must be explicitly spelled out in terms of the BGP routes and their attributes
Thus the draft has PIM-specific and BGP-specific sections
As already mentioned, some functional models have not been spec’ed for both

## Slide 17: Next Steps
Finish and post the draft (hopefully this August)
Ask for acceptance as WG draft
Critical examination and review by WG members