## Slide 1: mLDP “In-Band Signaling” in a VRF Context
MPLS WG has adopted draft-ietf-mpls-mldp-in-band-signaling as a WG document
  Provides specification for creating a multicast distribution tree that consists of two PIM trees spliced onto an mLDP MP LSP
  Useful when two islands of PIM are connected by a backbone that is mLDP-capable but PIM-free
As specified in that draft, the procedures can be used only in global table context, not in VRF context
As always, everything that works in global table context needs to work also in VRF context!
E.g., useful technique for certain sorts of content distribution, and some SPs do content distribution in VRF context
So what’s the simplest extension to make mLDP in-band signaling work in VRF context?

## Slide 2: How the “In-band” Signaling Works
Very simple signaling paradigm:
  Egress signals PIM Join(S,G)
  Backbone egress edge signals mLDP, encoding (S,G) into mLDP FEC element
  Backbone ingress edge decodes (S,G) from mLDP signal and signals PIM Join(S,G) into ingress area
  One (S,G) per mLDP MP LSP
  C-Bidir MDT always mapped to MP2MP LSP, SSM MDTs mapped to P2MP LSPs

## Slide 3: What Does “In-Band” Mean Anyway?
Does not mean “in the data plane”, all signaling is in control plane
Means that PIM “(S,G)” is encoded in the mLDP FEC element, and carried through the backbone in mLDP messages
  (S,G) encoded in opaque value field of FEC Element
  Intermediate nodes do not parse the opaque value field and do not base any procedures of (S,G) encoding; but its presence can be useful for troublshooting
No need for an additional, separate layer of signaling between ingress and egress edge nodes

## Slide 4: Why Doesn’t it Work As Is in VRF Context?
When VRFs are used, (S,G) might not be globally unique
  But mLDP FEC element that encodes (S,G) does have to be globally unique in backbone, since each LSP in backbone has to have a unique FEC element
  What can we add to the FEC element in addition to (S,G) to make it globally unique?
When an mLDP “in-band signal” arrives at the backbone ingress edge, how does the edge node know which VRF is the proper context for the signal?
  What can we add to the FEC element in addition to (S,G) so that it identifies a VRF?

## Slide 5: The Usual Solution when VRFs are Used
Add an RD to the signaling
The draft just proposes a simple extension tp draft-ietf-mpls-mldp-in-band-signaling, by defining new FEC types that include an RD

## Slide 6: What does this have to do with VPNs?
Nothing, really
VRFs, RDs sometimes used for solving other problems with different requirements
Proposal is useful, we’d like to see it adopted by whatever WG the powers that be think it should be assigned to