## Slide 1: MVPN/BGP Support for Customers That Use mLDP
RFCs 6513/6514:
  support Multicast VPN Service for customers that use PIM
  provide extensive support for use of MPLS multicast in the SP backbone
But the RFCs do not provide adequate support for customers that use mLDP
  some support is provided, but there unfortunate restrictions, which we will discuss
Purpose of draft-rosen-l3vpn-mvpn-mldp-nlri is to provide more complete MVPN support for customer use of mLDP

## Slide 2: Identification of C-flows in MCAST-VPN Routes
RFC 6514 defines MCAST-VPN routes that identify specific customer flows (C-flows) or sets thereof
  PIM identifies customer flows (C-flows) with a pair of addresses: <source address, group address> (S,G)
  RFC 6514 defines BGP MCAST-VPN routes that identify C-flows by encoding (S,G) into the NLRI
  Also sets of C-flows can be identified in a single NLRI by encoding a “wildcard” in place of S or G or both
When customer uses mLDP, C-flows are identified differently

## Slide 3: Identification of C-flows in mLDP
mLDP (RFC 6388) identifies a C-flow by a MP FEC Element:
  FEC Type (P2MP or MP2MP)
  Root Node (IP address)
  Opaque Value, encoded as a TLV
    Note that there are multiple types of opaque value
    Note that opaque value is variable length
To provide MVPN support for mLDP C-flows, MCAST-VPN routes need to have mLDP FEC element encoded into NLRI
  Only S-PMSI A-D routes, Leaf A-D routes, and C-multicast Source Tree Joins need to identify mLDP C-flows

## Slide 4: mLDP C-flow Support as Already Specified in RFC 6514
RFC 6514 already specifies some mLDP C-flow support:
  Root node of mLDP FEC coded into multicast source address field
  Opaque value of mLDP FEC coded into multicast group address field
Why isn’t this satisfactory?
  No encoding of FEC type (P2MP vs. MP2MP)
  Assumption that opaque value can fit into the same number of octets that are used to encode an IP address; this is true for one opaque value type, but is not true in general
  No way to tell whether NLRI encodes a PIM (S,G) or an mLDP FEC element:
    So won’t work if a customer uses both mLDP and PIM

## Slide 5: Possible Solutions
Straightforward: Define new NLRI encoding that:
  Has a flag to say that the NLRI identifies an mLDP FEC Element, not a PIM (S,G)
  Contains a full mLDP FEC Element, including type, and including TLV encoding for opaque value
Alternative: Overload various length fields so that particular combinations of length values can be used to infer that the NLRI identifies an mLDP FEC Element
  This style may be familiar from RFC 6515!
  Advantage: no new formats
  Disadvantage: silly
So we propose to define new NLRI encodings

## Slide 6: The Proposal
RFC 6514 defines first octet of MCAST-VPN SAFI to be a “route type”; values 1-7 are defined
We propose to take two high order bits to identify the customer multicast protocol:
  00 for PIM, 01 for mLDP
  Backwards compatible
  Plenty of room for additional route types and/or customer multicast protocols
  Ensures that an NLRI identifying a PIM C-flow is different than an NLRI identifying an mLDP C-flow
Also, create an IANA registry for the MCAST-VPN “route type” field, to accommodate any future expansion

## Slide 7: Proposal, Continued
The MCAST-VPN NLRI still begins with type and length
Remaining octets of NLRI contain mLDP FEC Element exactly as defined in RFC 6388, including:
  FEC type (P2MP/MP2MP),
  Root node field with AFI
  Opaque value encoded as TLV
Note: if the route type field indicates mLDP, the NLRI is not interpreted as an (S,G)
This proposal seems very straightforward
Issue: should the handling of mLDP as specified in RFC6514 be deprecated?

## Slide 8: But What About WildCards?
Does the elaborate treatment of wildcards in RFC 6625 still apply when the C-flows are mLDP rather than PIM? If so, how are the wildcards encoded?
Proposal: allow the NLRI to contain the encoding of an mLDP Typed Wild Card FEC element (RFCs 5918,6388)
But shouldn’t the draft contain more than an encoding for wildcards, maybe some use cases and procedures?
  Yes, the existing wildcard section is really just a placeholder for now.

## Slide 9: Accept as WG Document?
Seems simple, straightforward, and useful.
Is anything controversial about it?
We would like to see it accepted as a WG document.
Comments?