## Slide 1: l3vpn end-system draft
Pedro Marques <roque@contrailsystems.com>

## Slide 2: Overview
Defines a mechanism to associate an end-system virtual interface to an L3VPN.
  Co-located forwarder: interface instantiation.
  External forwarder: XMPP as PE-CE protocol.
Decouples PE control and forwarding functionality:
  PE forwarding functionality may be delegated to an hypervisor switch (or an external device).
  XMPP between PE control plane and forwarder.

## Slide 3: Overview
PE forwarding functionality implemented by server OS, hypervisor, or external forwarder.
Data-plane
Server OS
app
app
Server OS
appliance
hypervisor
VM
VM
PE Control Plane
PE Control Plane
BGP
xmpp
xmpp
xmpp
MPLS-over-X

## Slide 4: Applicability
Appliance in Service Provider POP:
  Decouple routing and forwarding from service.
  Example: content cache appliance working in VPN context.
Service providers want to deploy service appliances on COTS hardware.
  Unrelated to data-center.
l3vpn is a reality in data-center today:
  Interconnection of data-centers (run by multiple admin-domains).
  Interconnection of “IP subnets” inside the data-center.
l3vpn control plane is encapsulation agnostic.

## Slide 5: Technology
Existing L3VPN functionality:
  CE interface may be connected to 1 or more Virtual Networks;
  Policy based definition of VPN;
  Per RT route distribution trees (RFC4684);
  Traffic filtering between VPNs (BGP flow-spec RFC 5575);
End-system draft:
  Standards based protocol (XMPP) for delegating a PEs forwarding functionality.

## Slide 6: End-system PE
PE performs VRF import/export functionality.
PE is management point.
Operational scale: PE should be able to control +1000x of CE (end-system) interfaces.
PE
Server OS (Forwarder)
End-system

## Slide 7: End-system extensions
Not the same as having hypervisor be an L3VPN PE.
  Operational: provisioning and diagnostics;
  Software complexity: on the PE.
  Protocol to the Forwarder: XML documents.
Decoupling PE Control Plane and Forwarding is useful regardless of application.

## Slide 8: XMPP
Simple mapping between BGP l3vpn data and an XML document.
XML: extendable, flexible.
XMPP provides publish subscribe functionality:
  A network participant “subscribes” to events on that network.
  Network reachability is propagated as an “event”.

## Slide 9: Beyond connectivity
RFC 5575
  draft-marques-sdnp-flow-spec-00
Multicast
  draft-marques-l3vpn-mcast-edge-00
Provisioning
  draft-marques-l3vpn-schema-00

## Slide 10: Summary
Authors would like to gauge the interest for WG adoption.
The document defines:
  PE-CE interaction.
  Decoupling of PE control and data-plane.
There are multiple target applications.
The mechanism is useful independently of application.