## Slide 1: LISP MIB draft-lisp-mib-05
Vancouver IETF - LISP WG
Gregg Schudel, Amit Jain, Victor Moreno
July 2012

## Slide 2: draft-ietf-lisp-mib-05
Several changes from -03 and -04 versions
  The -05 update includes corrections to “add back” several tables that were erroneously omitted starting with the -03 submittal. (clerical/multi-author errors). (Apologies). These are:
    lispIidToVrf :: provides information mapping a LISP instance-id to a VRF
    lispGlobalStats :: provides global statistics for a given LISP instance-id per address-family
    lispConfiguredLocator :: represents the set of configured routing locators
  Several "objects" were added to other tables as well, also for LISP instance-id support
  The IANA-ADDRESS-FAMILY-NUMBERS-MIB DEFINITIONS reference was moved from the Informative to the Normative section
  The draft was compared against RFC 4191 (again.) Formatting changes were made to achieve compliance
  The MIB was run through a "MIB compile tool" -- it compiles successfully
LISP MIB
Vancouver IETF July 2012
Slide 2

## Slide 3: draft-ietf-lisp-mib-05
We believe the MIB is in good shape now and stable
MIB’s are useful even for experimental protocols
The Authors believe draft-lisp-mib-05 is ready for WG last-call
Comments?
LISP MIB
Vancouver IETF July 2012
Slide 3

## Slide 4: Backups

## Slide 5: Problem Statement
Define the LISP MIB
  One MIB covering all LISP Devices
    ITR, ETR, MS, MR, PITR, PETR
Requirements
  Track LISP device “configuration”
    LISP features enables and attributes configured on the device
  Track current LISP device “values” such as:
    Map-Cache and Mapping-Database entries
    LISP site registration entries
  Track current device “operational statistics” such as:
    Packet encapsulation and decapsulation (number of packets and bytes
    map-registers, map-requests, map-replies, etc.
LISP MIB
Slide 5
Vancouver IETF July 2012

## Slide 6: LISP MIB Tables
lispFeatures | The various lisp features that can be enabled on LISP devices
lispIidToVrf | Information representing the mapping of LISP instance ID to a VRF
lispGlobalStats | Global statistics for a given Instance ID per address-family on a LISP device
lispMappingDatabase | The EID-to-RLOC database that contains the EID-prefix to RLOC mappings configured on an ETR
lispMappingDatabaseLocator | The set of routing locators in the EID-to-RLOC database configured on an ETR
lispMapCache | The short-lived, on-demand table on an ITR that stores, tracks, and times-out and otherwise validates EID-to-RLOC mappings
lispMapCacheLocator | The set of locators per EID prefix contained in the map-cache table of an ITR
lispConfiguredLocator | The set of routing locators configured on a LISP device
lispEidRegistration | On a Map-Server, the properties of each EID prefix registered to this device
lispEidRegistrationEtr | On a Map-Server, the properties of the different ETRs that send registers for a given EID prefix to this device
lispEidRegistrationLocator | On a Map-Server, the properties of the different locator per EID prefix registered to this device
lispUseMapServer | The properties of all Map-Servers this device is configured to use
lispUseMapResolver | The properties of all Map-Resolvers this device is configured to use
lispUseProxyEtr | The properties of all Proxy ETRs this device is configured to use
LISP MIB
Slide 6
Vancouver IETF July 2012

## Slide 7: LispAddressType
LispAddressType ::= TEXTUAL-CONVENTION
STATUS current
DESCRIPTION
"LISP architecture can be applied to a wide variety of
address-families. This textual-convention is a
generalization for representing addresses that belong
to those address-families. For convenience, this
document refers to any such address as a lisp address.
LispAddressType textual-convention consists of
the following four-tuple:
1. IANA Address Family Number: A field of length
2-octets, whose value is of the form following the
assigned AddressFamilyNumbers textual-convention
described in [IANA]. The enumerations are listed
in [IANA]. Note that this list of address family
numbers is maintained by IANA.
2. Length of LISP address: A field of length 1-octet,
whose value indicates the octet-length of the next
(third) field of this LispAddressType four-tuple.
3. Lisp address: A field of variable length as
indicated in the previous (second) field, whose
value is an address of the IANA Address Family
indicated in the first field of this LispAddressType
four-tuple. Note that any of the IANA Address
Families can be represented. Particularly when the
address family is LISP Canonical Address Format
(LCAF) [LCAF] with IANA assigned Address Family
Number 16387, then the first octet of this field
indicates the LCAF type, and the rest of this field
is same as the encoding format of the LISP Canonical
Address after the length field, as defined in [LCAF].
4. Mask-length of address: A variable-length field
comprised of the remaining octets of this
LispAddressType four-tuple, whose value is the
mask-length to be applied to the lisp address
specified in the previous (third) field.
ipv4 = 1
ipv6 = 2
lcaf = 16387
ipv4 = 4
ipv6 = 16
lcaf = variable
Variable in each case
ipv4 = 192.168.1.1
ipv6 = 2001:db8:2::1
lcaf = per draft
e.g
LISP MIB
Slide 7
Vancouver IETF July 2012

## Slide 8
Example 1: Suppose that the IPv4 EID prefix stored is
10.10.10.0/24. In this case, the values within
lispMapCacheEntry would be:
lispMapCacheEidLength = 8
lispMapCacheEid = 1, 4, 10.10.10.0, 24
... [skip] ...
where 8 is the total length in octets of the next
object (lispMapCacheEID of type LispAddressType). Then,
the value 1 indicates the IPv4 AF (per [IANA]), the
value 4 indicates that the AF is 4-octets in length,
10.10.10.0 is the IPv4 address, and the value 24 is the
mask-length in bits. Note that the lispMapCacheEidLength
value of 8 is used to compute the length of the fourth
(last) field in lispMapCacheEid to be 1 octet - as
computed by 8 - (2 + 1 + 4) = 1.
LISP MIB
Slide 8
Vancouver IETF July 2012
Example 3: As an example where LCAF is used, suppose
that the IPv4 EID prefix stored is 10.10.10.0/24 and it
is part of LISP instance id 101. In this case, the values
within lispMapCacheEntry would be:
lispMapCacheEidLength = 11
lispMapCacheEid = 16387, 7, 2, 101, 1, 10.10.10.0, 24
... [skip] ...
where 11 is the total length in octets of the next object
(lispMapCacheEID of type LispAddressType). Then, the value
16387 indicates the LCAF AF (see [IANA]), the value 7
indicates that the LCAF AF is 7-octets in length in this
case, 2 indicates that LCAF Type 2 encoding is used (see
[LCAF]), 101 gives the instance id, 1 gives the AFI (per
[IANA]) for an IPv4 address, 10.10.10.0 is the IPv4
address, and 24 is the mask-length in bits. Note that the
lispMapCacheEidLength value of 11 octets is used to compute
the length of the last field in lispMapCacheEid to be 1 octet,
as computed by 11 - (2 + 1 + 1 + 1 + 1 + 1 + 4) = 1.”