## Slide 1: AT&T AMT Multicast Update
IETF 84
Vancouver, BC

## Slide 2: AT&T AMT Landscape
Production ready Relays deployed in 12 national sites
  Based on v9
  Moving to v14 4Q12 (assuming it is finalized and approved)
Total of 150 to 200 Gbps capacity by EOY 2012
Soliciting large Content Providers with popular multicastable content
Engaged with Octoshape to utilize AMT capabilities to distribute their customers’ content
  Octoshape’s proprietary technology ensures reliable delivery with high quality (quality metrics from Octoshape GW client)
  Primary used for high-scale broadcast-quality video distribution
    24x7 broadcast: Examples: CNN live video (cnn.com), TVEverywhere
    Events: Examples: Eurovision Song Contest, French Open

## Slide 3: Eurovision Song Contest
Partnered with Octoshape
Up to 10’s of thousands of simultaneous clients viewing
Supported 10’s of Gbps at peak period
Approx Domestic = 70%, International = 30%
Single Anycast address
No failures and sampling showed excellent quality
Interesting issue discovered w/respect Anycast routing
  As busy peering locations quiesced the AMT tunnels burrowed deeper into BB to non-peering located Relays
  Possible solution = separate Anycast address for Peering and Non-peering located Relays

## Slide 4: Anycast Issue
PeerRelay
AT&T
Peering Router
Internal Relay
Peer Router
Peer Router
1
2
3
4
5
6
External Network
AT&T Network
External network peering router initially sends requests to nearest AT&T Relay at peering location
And receives content back from nearest AT&T Relay at peering location
AT&T Relay exceeds capacity limits for tunnels and quiesces
Requests routed (by AT&T Peering Routers) to Internal Relay
Internal Relay sends content via nearest peering router
Wasted BW as it would be better to serve out of the Peer Relay at the egress location
  Short term solution is Internal and External Anycast address for Relays
  Longer term: Router Based Relays with “infinite” BW
AT&T
Peering Router
PeerRelay
4

## Slide 5: Next Steps
Continue to deploy capacity as demand warrants
Working to make this a Product Offering (managed service)
Will allow CPs to use with their own external MC source
Integration with caching services
Integrate with other ISPs to support interdomain CDN Multicast
  Setup Interconnection
  Includes AMT and Native
  Completed ATIS specification
  Working IETF draft BCP