## Slide 1: Possible approaches to signal IPv4 embedded IPv6 Multicast Address

## Slide 2: Agenda
IPv4-IPv6 Mcast: Problem Statement
Possible Solutions.
Solution Comparison
Q&A

## Slide 3: IPv4-IPv6 Mcast: Problem Statement
Scenarios identified by draft-ietf-mboned-v4v6-mcast-ps as part of IPv4 to IPv6 Multicast translation,
IPv4 source and Receivers connected over IPv6-Only network (4-6-4)
IPv6 Receiver Connected to IPv4 source via IPv4 Access and IPv6 network (6-4-6-4)
IPv6 Receivers and Source connected via IPv4-Only network (6-4-6)
IPv6 Receivers and IPv4 Source (6-4)
IPv4 Receivers and IPv6 Source (4-6)
Scenarios involving IPv4 as source are of top priority.

## Slide 4: IPv4-IPv6 Mcast: Problem Statement Contd..
Raises below requirement,
Embed IPv4 group address in IPv6 group address.
Procedure to signal any AFBR that IPv4 group is embedded in IPv6 group address.

## Slide 5: Possible Solutions
Designated bit/flag in IPv6 Multicast Address
  A designated field of 4 bits are reserved as 64IX for IPv4-IPv6 interconnection.
  First bit “M” is reserved to signal that IPv4 group is embedded.
  This is documented in draft-ietf-mboned-64-multicast-address-format-02.
Well known IPv6 Multicast prefix
An IPv6 Multicast prefix dedicated for IPv4-IPv6 translation usage.
Using PIM Join Attribute & MLD Auxiliary Data
New PIM Join Attribute or MLD Auxiliary Data with T flag to signal that IPv4 is embedded.
This is documented in draft-kumar-mboned-64mcast-embedded-address.
Manual Configuration on each border device
Assigning a specific prefix for IPv4-IPv6 translation usage and statically configure the prefix in each border device.
Dynamic signaling of translation prefix using another protocol (e.g. BGP)
Prefixes used for IPv4-IPv6 translation can be advertised across domains.

## Slide 6
IPv6 Cloud
IPv6 Cloud
IPv4 Cloud
IPv4 Source
IPv4 Receiver
IPv6 Receiver
IPv4 Cloud
MLD
FF3x:0:64IX:G:239.1.1.1
Transit Router doesn’t require to understand 64XI bits
PIMv6
FF3x:0:64IX:G:239.1.1.1
AFBR requires to understand 64XI bits.
PIMv4
239.1.1.1
IGMP
239.1.1.1
AFBR requires to embed IPv4 group with 64XI bits.
PIMv6
FF3x:0:64IX:G:239.1.1.1
PIMv4
239.1.1.1
Designated bit/flag in IPv6 Multicast Address
No changes required on End Host
AFBR should understand 64XI bits
Backward compatible issue.

## Slide 7
IPv6 Cloud
IPv6 Cloud
IPv4 Cloud
IPv4 Source
IPv4 Receiver
IPv6 Receiver
IPv4 Cloud
MLD
Prefix::239.1.1.1
Transit Router doesn’t require to understand Well-known prefix
PIMv6
Prefix::239.1.1.1
AFBR requires to understand Well-known prefix.
PIMv4
239.1.1.1
IGMP
239.1.1.1
AFBR requires to embed IPv4 group with well-known prefix.
PIMv6
Prefix:239.1.1.1
PIMv4
239.1.1.1
Well Known IPv6 Multicast Prefix
No changes required on End Host
AFBR should understand WKP
Permanent reservation for intermittent solution.

## Slide 8
IPv6 Cloud
IPv6 Cloud
IPv4 Cloud
IPv4 Source
IPv4 Receiver
IPv6 Receiver
IPv4 Cloud
MLD
Auxiliary-Daya=T-flag
Any-Prefix::239.1.1.1
DR requires to understand new Auxiliary Data
PIMv6
Join-Attribute=T-flag
Any-Prefix::239.1.1.1
AFBR requires to understand new Join Attribute.
PIMv4
239.1.1.1
IGMP
239.1.1.1
AFBR requires to embed IPv4 group with new Join Attribute.
PIMv6
Join-Attribute=T-flag
Any-Prefix:239.1.1.1
PIMv4
239.1.1.1
Using PIM Join Attribute & MLD Aux. Data
Changes required on End Host
AFBR should understand Join Attribute & Aux. Data
Backward Compatible with no permanent reservation.

## Slide 9
IPv6 Cloud
IPv6 Cloud
IPv4 Cloud
IPv4 Source
IPv4 Receiver
IPv6 Receiver
IPv4 Cloud
MLD
AS-local-Prefix::239.1.1.1
Transit Router doesn’t require to understand AS-Local-prefix
PIMv6
AS-local-Prefix::239.1.1.1
AFBR look into manual table to identify AS-local-prefix.
PIMv4
239.1.1.1
IGMP
239.1.1.1
AFBR look into manual table and embed IPv4 group with AS-local-prefix.
PIMv6
AS-local-Prefix:239.1.1.1
PIMv4
239.1.1.1
Manual Configuration on each Border Devices
No changes required on End Host
Manual configuration required on all AFBR. This is not scalable
Inter-AS – Not possible.

## Slide 10
IPv6 Cloud
IPv6 Cloud
IPv4 Cloud
IPv4 Source
IPv4 Receiver
IPv6 Receiver
IPv4 Cloud
MLD
AS-local-Prefix::239.1.1.1
Transit Router doesn’t require to understand AS-Local-prefix
PIMv6
AS-local-Prefix::239.1.1.1
AFBR look into BGP table to identify AS-local-prefix.
PIMv4
239.1.1.1
IGMP
239.1.1.1
AFBR look into BGP table and embed IPv4 group with AS-local-prefix.
PIMv6
AS-local-Prefix:239.1.1.1
PIMv4
239.1.1.1
BGP-UPDATE
Prefix=AS-local-prefix::
Dynamic Signaling of translation prefix
No changes required on End Host
Complex approach.

## Slide 11: Solution Comparison
Solution | Advantage | Disadvantage
Designated bit/flag in IPv6 Multicast Address | Can be signaled via existing devices | Changes to format. Backwards compatible issue if using existing flags
Well known IPv6 Multicast prefix | Backward compatible | Does not work with embedded-RP. Inter-domain hard.
Using PIM Join Attribute & MLD Auxiliary Data | No restrictions on group addresses | Requires some code changes
Manual Configuration on each border devices | Simple to use | Not Scalable Inter-domain communication is not possible
Dynamic signaling of translation prefix using another protocol | Flexibility | Complexity

## Slide 12: Q&A
Open for questions